| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| COVER PAGE (TO BE COMPLETED BY SYSTEMS ENGINEERING SUPPORT MANAGER) |
| Originator: D Williamson | Date: 9/17/04 |
| ECP No: ECP-015 | ECP Title: MCWF Contract-Negotiated Changes and General Revision to Winding Form Types A, B, and C. |
| Required Reviewers |
| Required Reviewers for this ECP: P. Heitzenroeder, L. Dudek |
| ECP Approval Level Expedited ECP? Yes No Change Level: Approving Official: |
| Actions Update Table 6-1 in NCSX specification NCSX-CSPEC-141-03 to reflect the updated drawings per ECN # 4903 Update the following drawings per ECN # 4903: SE-141-114 through SE-141-116 and SE-141-101 through SE-141-103 |
| APPROVALS (TO BE COMPLETED BY APPROVING OFFICIALS) |
| Change Level | Approving Official | Approval? | Signature |
| 3 | NCSX Project Manager | Yes No |  |
| 3a (Expedited ECP) | NCSX Engineering Manager | Yes No |  |
| 2 | NCSX Federal Project Director | Yes No |  |
| 1 | Associate Director OFES | Yes No |  |
| 0 | Under Secretary of Energy | Yes No |  |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: Dave Williamson | Date: 9/17/04 |
| Overview of Change Type of of ECP: EXPEDITED STANDARD Type of Change: TECHNICAL COST SCHEDULE EDITORIAL (Check all that Apply) Reason for Change: Contract-negotiated changes will reduce the cost of the production winding forms. Lead block dimensional changes are proposed to make Types A and B similar to Type C (see ECP-012). Impacted WBS Elements: WBS 141 Modular Coil Winding Form Impacts of Change (Briefly Describe): Cost impacts were already captured in ECP-014. Elimination of the spherical seats and other modifications will reduce the cost of the winding forms. No impact on the winding process is anticipated. Lead block changes will improve the conductor configuration and provide space for additional insulation and mechanical support. Assessment of Other Options: None. |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: Dave Williamson | Date: 9/17/04 |
| Detailed Description of the Change: (Use Continuation Sheets and/or Attach Information/Sketches, As Needed) List Attachments, Impacted Documents, etc. NCSX-CSPEC-141-03-04 (not signed) ECN #4903 Description of Change: Updated NCSX-CSPEC-141-03 to NCSX-CSPEC-141-04 to reflect revise Table 6-1. SE141-101, All views updated to reflect changes to SE141-114 SE141-114, Sheet 2, Quad G4 - Removed spherical seats, revised tee relief, added dimensions SE141-114, Sheet 2, Quad F7 - Added 45-deg x .03 chamfer at VPI groove edge SE141-114, Sheet 3, Quad C4 - Revised hole in vessel support boss SE141-114, Sheet 7, Quad C2 - Revised lead block protrusion dimensions SE141-114, Sheet 9, Quad C7 - Revised dimension of cooling inlet/outlet hole SE141-114, Sheet 10, Quad D3/D7 - Updated image SE141-114, Sheet 11, Quad E3 - Removed Tables III, IV SE141-102, All views updated to reflect changes to SE141-115 SE141-115, Sheet 2, Quad G4 - Removed spherical seats, revised tee relief, added dimensions SE141-115, Sheet 2, Quad F7 - Added 45-deg x .03 chamfer at VPI groove edge SE141-115, Sheet 3, Quad F4 - Added assembly fixture attachment boss SE141-115, Sheet 7, Quad B4 - Revised lead block protrusion dimensions SE141-115, Sheet 9, Quad F4 - Revised dimension of cooling inlet/outlet hole SE141-115, Sheet 11, Quad D3/D7 - Updated image SE141-115, Sheet 12, Quad E3 - Removed Tables III, IV SE141-103, All views updated to reflect changes to SE141-116 SE141-116, Sheet 2, Quad G4 - Removed spherical seats, revised tee relief, added dimensions SE141-116, Sheet 2, Quad F7 - Added 45-deg x .03 chamfer at VPI groove edge SE141-116, Sheet 11, Quad D3/D7 - Updated image SE141-116, Sheet 12, Quad E3 - Removed Tables III, IV |