PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 4933 Rev 1

COGNIZANT INDIVIDUAL:	Paul Goranson (ORNL)

ECN TITLE:	Modification  of Vacuum Vessel Subassembly (VVSA) Inner Support Bosses to Utilize Simplified Hangers

CC/WP/Job:	9450-1***-1203-405		AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP number:  1103

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE120-002 | 1 | Vacuum Vessel Subassembly (VVSA) |
| SE120-004 | 1 | Vacuum Vessel Period Inspection and Leak Check Assembly |
| SE122-018 | 1 | Vacuum Vessel Port 12 Flange Detail |
| SE122-019 | 1 | Vacuum Vessel Port 12 Seal Retainer |
| SE122-049 | 1 | Vacuum Vessel Port 4 Flange Detail |

DESCRIPTION OF CHANGE: (state drawing no.,zone.group, or list attachments)

SE120-002		Editorial change to BM

SE120-004, sht 1	Editorial change to BM

SE120-004, sht 13	Add find numbers for nut and washer. (ECN Revision 1)

SE120-004, sht 15	Editorial change to callouts

SE120-004, sht 18	Design change to inner weld bosses to accommodate new support interface, including change in location, thread size and orientation.

SE122-018		Relax in tolerance

SE122-019		Relax in tolerance

SE122-049		Relax in tolerance

SE122-057		Add missing dimension, relax tolerance

SE122-072		Add missing true position callout, relax tolerance

SE122-104		Add missing port dimension

SE122-105		Change recess to full radius per contractor request

SE122-172		Relax tolerances, add missing stock thickness

SE122-173		Relax tolerances

REASON FOR CHANGE:

To incorporate a design change to the supports which will streamline assembly and installation procedures for the VVSA, and incorporate editorial changes and requests by the contractor.

ENGINEERING CHANGE NOTICE APPROVALS: ECP-017		DATE: 11/04/2004

COGNIZANT INDIVIDUAL MAKING CHANGE:  Paul Goranson

RESPONSIBLE LINE MANAGER:	Larry Dudek

PPPL ENGINEERING CHANGE NOTICE (ECN)	ECN # _____

COGNIZANT INDIVIDUAL:	Paul Goranson (ORNL)

ECN TITLE:	Modification  of Vacuum Vessel Subassembly (VVSA) Inner Support Bosses to Utilize Simplified Hangers

CC/WP/Job:	          AREA OR PROJECT:  NCSX

| DRAWING(S) (CONTIN.) AFFECTED NUMBER: | NEW REV. | TITLE |
| --- | --- | --- |
| SE120-057 | 1 | Vacuum Vessel Port 4 Seal Retainer Detail |
| SE120-072 | 1 | Vacuum Vessel Port NB Flange Detail |
| SE120-104 | 1 | Vacuum Vessel Port 12 Cover Test Flangs Weldment |
| SE120-105 | 1 | Vacuum Vessel Leak Test Block |
| SE120-172 | 1 | Vacuum Vessel NB Port Cover Test Flange |
| SE120-173 | 1 | Vacuum Vessel Port NB Seal Retainer |