| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| COVER PAGE (TO BE COMPLETED BY SYSTEMS ENGINEERING SUPPORT MANAGER) |
| Originator: Paul Goranson | Date: 11/04/2004 (11/24/04 – Revision 1) |
| ECP No: ECP-017 | ECP Title: Modification of Vacuum Vessel Subassembly (VVSA) Inner Support Bosses to Utilize Simplified Hangers |
| Required Reviewers |
| Required Reviewers for this ECP: WBS Manager, WBS 1 Project Engineer, Engineering Manager, QA, Project Manager |
| ECP Approval Level Expedited ECP? Yes No Change Level: Approving Official: |
| Actions Update listed documents to reflect approved changes. . |
| APPROVALS (TO BE COMPLETED BY APPROVING OFFICIALS) |
| Change Level | Approving Official | Approval? | Signature |
| 3 | NCSX Project Manager | Yes No |  |
| 3a (Expedited ECP) | NCSX Engineering Manager | Yes No |  |
| 2 | NCSX Federal Project Director | Yes No |  |
| 1 | Associate Director OFES | Yes No |  |
| 0 | Under Secretary of Energy | Yes No |  |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: Paul Goranson | Date: 11/04/2004 (11/24/04 – Revision 1) |
| Overview of Change Type of of ECP: EXPEDITED STANDARD Type of Change: TECHNICAL COST SCHEDULE EDITORIAL (Check all that Apply) Reason for Change: To incorporate a new support design which will streamline assembly and installation procedures for VVSA, and incorporate editorial changes and vendor recommendations. Impacted WBS Elements: 1202 Impacts of Change (Briefly Describe): The change will reduce complexity and cost of VVSA handling and installation. Assessment of Other Options: None |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: Paul Goranson | Date: 11/04/2004 (11/24/04 – Revision 1) |
| Detailed Description of the Change: (Use Continuation Sheets and/or Attach Information/Sketches, As Needed) List Attachments, Impacted Documents, etc. (Revision 1) Ref : ECN-4933 Revision 1 VVSA Product SpecificationFor the Vacuum Vessel System Sub-Assembly (NCSX-CSPEC-121-02-03) Description of Change: ECN 4933 Revision 1 replaces previous model and drawing files with three zip files: ZIP File Model Description (from Pro/Intralink database, edited) Rev VV_Prod_pdf_Files_Rev1.zip ZIP file containing pdf drawing files including Rev 1 changes 1 VV_Prod_ProEModels_Rev1.zip ZIP file containing all ProE models including rev 1 changes 1 VV_Prod_step_Rev1.zip ZIP file containing all step files including Rev 1 changes. Also contains step files for the die geometry. 1 NCSX-CSPEC-121-02-03 incorporates the following changes: Updated standards listing in Section 2.1 to add some omitted standards and their effective dates. Revised Appendix A to reflect the table above |