| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| COVER PAGE (TO BE COMPLETED BY SYSTEMS ENGINEERING SUPPORT MANAGER) |
| Originator: Bob Simmons | Date: October 21, 2005 |
| ECP No: 038 | ECP Title: Change in Modular Coil Winding Form Requirements |
| Required Reviewers |
| Required Reviewers for this ECP: Dave Williamson, Brad Nelson, Wayne Reiersen, Phil Heitzenroeder, Frank Malinowski, Judy Malsbury, Jerry Levine, Mike Zarnstorff |
| ECP Approval Level Expedited ECP? Yes No Change Level: Approving Official: |
| Actions Revise MCWF CSPEC – NCSX-CSPEC-141-03 to Revision 10 by October 31st Revise impacted drawings per ECNs #5016 and 5026 by October 31st Update contract documentation by October 31st |
| APPROVALS (TO BE COMPLETED BY APPROVING OFFICIALS) |
| Change Level | Approving Official | Approval? | Signature |
| 3 | NCSX Project Manager | Yes No |  |
| 3a (Expedited ECP) | NCSX Engineering Manager | Yes No |  |
| 2 | NCSX Federal Project Director | Yes No |  |
| 1 | Associate Director OFES | Yes No |  |
| 0 | Deputy Secretary of Energy | Yes No |  |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) ECP-038 |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: Bob Simmons | Date: October 20, 2005 |
| Overview of Change Type of ECP: EXPEDITED STANDARD Type of Change: TECHNICAL COST SCHEDULE EDITORIAL (Check all that Apply) Reason for Change: Inspection of C-1 Casting identified several issues requiring resolution and/or clarification. Some were errors by MTM and some were design errors. Impacted WBS Elements: WBS 14 Impacts of Change (Briefly Describe): As a result of the inspections, a revision/update to the design requirements are needed to ensure that future castings do not have the same issues. This will involve changes (Revision 10) to the MCWF CSPEC (NCSX-CSPEC-141-03) and to assorted MCWF drawings. The proposed changes are all technical in nature; however, it is possible that resolution by the vendor (MTM) could result in some cost and schedule adjustments. These cost and schedule impacts will not be addressed in this ECP, but will be reserved for a later ECP when the cost and schedule impacts have been identified. Assessment of Other Options: None |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) ECP-038 |
| Originator: Bob Simmons | Date: October 20, 2005 |
| Detailed Description of the Change: (Use Continuation Sheets and/or Attach Information/Sketches, As Needed) List Attachments, Impacted Documents, etc. Draft MCWF CSPEC Revision 10 (NCSX-CSPEC-141-03) – all the subsequent attachments will be incorporated into this revision ECN-5016 (Approved 8/9/2005) ECN-5026 (Approved ????) RFD-14-005 (Approved 9/15/2005) RFD-14-006 (Approved 9/15/2005) RFD-14-008 (Approved 9/22/2005) RFD-14-009 (Approved 10/18/2005) Description of Change: Changes to CSPEC: Additional FEA indicates that the formerly referenced High Stress Areas do not have to be specifically addressed. Accordingly: Sections 3.1.1.6.3 (Liquid Penetrant Inspection of High Stress Regions), 3.2.3.2.2.3 (Repairs in High Stress Area), 4.2.7.2.3 (Liquid Penetrant Inspection of High Stress Regions), and 4.2.8.2 (Post Machining Inspection for High Stress Regions) were deleted; in Section 3.1.1.7 (Radiographic Inspection ) special requirements for high stress inspections were deleted (i.e., there will not be a post-machining radiographic inspection), but the requirements for radiographic inspection were changed to specify that elliptical flaws were on to exceed 0.180” x 0.060” in all locations; and Section Appendix A which defined the former High Stress Regions was deleted. Revised Section 3.1.1.5 on magnetic permeability: now in two sub-sections, 3.1.1.5.1 which addresses the casting, including upgrades, and 3.1.1.5.2, which addresses fasteners and hardware. Revised Section 4.2.4accordingly. Revised Section 3.1.1.6.1 to delete the reference to SCRATA graded references for machined surfaces. Revised Section 4.2.3.1 and 4.2.3.2 concerning electrical testing. Revised Section 4.2.4 to add the requirement for separate reporting of surface finish inspections. Revised Section 4.2.5 and expanded into four subparagraphs (Sections 4.2.5.1, 4.2.5.2, 4.2.5.3, and 4.2.5.4) added to clarify requirements. Revised Section 4.2.6 to increase coverage of flange of the tee. Revised Sections 4.2.7.2.1 and 4.2.7.2.2 to add Level I for post-machining acceptance criteria. Revised Section 4.2.8 to delete references to “pre-machining.” Revised Table 6-1 to provide updated listing of zip files for ProE, STEP, and pdf files. Appendix B and Read Me file on Supplier FTP Site provide most recent revision for all drawings. Revised Table 6-2 to list all approved Requests for Deviation. Added RFD-14- 005, RFD-14-006, RFD-14-008, and RFD-14-009. |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) ECP-038 |
| Originator: Bob Simmons | Date: October 20, 2005 |
| Continuation Sheet: (Use Continuation Sheets and/or Attach Information/Sketches, As Needed) Updated Appendix B to provide complete listing of drawings and their applicable revisions. ECN-5016 Affected Drawing(s) New Revision Number Title SE142C-134 1 Type-C Side-A Lower Lead Block Correction of Drafting Error: Quad C7 - The drawing dimension, 7.97-in, mistakenly extends from the edge of the block to the centerline of the adjacent hole. The correct dimension for the width of block is 7.44 +/- .01-in. (3) ECN-5026 (STILL NEED THIS ECN) Affected Drawing(s) New Revision Number Title |