| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| COVER PAGE (TO BE COMPLETED BY SYSTEMS ENGINEERING SUPPORT MANAGER) |
| Originator: Dave Williamson | Date: February 3, 2005 |
| ECP No: 022 Rev 1 | ECP Title: Twisted Racetrack Design Changes Since FDR |
| Required Reviewers |
| Required Reviewers for this ECP: W. Reiersen, H. Neilson, B. Nelson, J. Chrzanowski, J. Malsbury, J. Levine, F. Malinowski, M. Zarnstorff, L. Dudek, T. Meighan |
| ECP Approval Level Expedited ECP? Yes No Change Level: Approving Official: |
| Actions Adopt proposed chill plate design with changes as noted in the chits Adopt the revised production coil clamp design for the TRC Replace prototype and other drawings with new drawings to reflect these design changes. Approved for fabrication drawings for the TRC should be generated per the following schedule: Side B (top and side) by 2/4/2005 Side A (top and side) by 2/11/2005 Clamps by 2/25/2005 See attached TRC chits for additional action items Update drawings for production coils accordingly ECN-4953 added by revision 1 – incorporate ECN 4953 by 2/11/2005 |
| APPROVALS (TO BE COMPLETED BY APPROVING OFFICIALS) |
| Change Level | Approving Official | Approval? | Signature |
| 3 | NCSX Project Manager | Yes No |  |
| 3a (Expedited ECP) | NCSX Engineering Manager | Yes No |  |
| 2 | NCSX Federal Project Director | Yes No |  |
| 1 | Associate Director OFES | Yes No |  |
| 0 | Under Secretary of Energy | Yes No |  |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: Dave Williamson | Date: February 3, 2005 |
| Overview of Change Type of of ECP: EXPEDITED STANDARD Type of Change: TECHNICAL COST SCHEDULE EDITORIAL (Check all that Apply) Reason for Change: Feasibility and cost and schedule considerations prompted the project to develop an improved design concept for the chill plates. The revised chill plate design required a re-design of the winding clamps. The revised chill plate design and clamp design will be used on both the TRC and the production coils. Impacted WBS Elements: WBS 142: Job 1403 – Modular Coil Final Design and Job 1410 – Twisted Racetrack Coil Fabrication Impacts of Change (Briefly Describe): TRC Cost and Schedule - Estimate at Completion (EAC) and schedule will be updated by 2/1/2005. Schedule impact should be strongly favorable. Impact of this EAC will be factored into PMB when risks are retired (March). Production Coils Cost and Schedule – EAC and schedule will be updated upon completion of the TRC. No significant impact in cooldown time is anticipated. Assessment of Other Options: Staying with the current baseline would have incurred unnecessary cost and schedule penalties IF the current baseline could have been fabricated. |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: Dave Williamson | Date: February 3, 2005 |
| Detailed Description of the Change: (Use Continuation Sheets and/or Attach Information/Sketches, As Needed) List Attachments, Impacted Documents, etc. Twisted Racetrack Coil Design Update (January 27, 2005) CHITs from CCB Meeting (table) Sketch of retention feature for clamps ECN-4953 => added by Revision 1 Description of Change: Cooling tube soldered to chill plates after installation of chill plates. This is a change from the current baseline in which the cooling tubes are pre-attached to fringe which is placed adjacent to the chill plates. The 3-piece clamp design is replaced with a 1-piece clamp design to allow adequate space for the two coolant tubes. (Previously, there was a single cooling tube.) |