| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| COVER PAGE (TO BE COMPLETED BY SYSTEMS ENGINEERING SUPPORT MANAGER) |
| Originator: Mike Viola | Date: March 10, 2005 |
| ECP No: 025 | ECP Title: RFD-12-001 - |
| Required Reviewers |
| Required Reviewers for this ECP: M. Viola, P. Goranson, B. Nelson, J. Malsbury, F. Malinowski, J. Levine, |
| ECP Approval Level Expedited ECP? Yes No Change Level: Approving Official: |
| Actions Approve RFD-12-001 Issue Contract Addendum to incorporate RFD-12-001 |
| APPROVALS (TO BE COMPLETED BY APPROVING OFFICIALS) |
| Change Level | Approving Official | Approval? | Signature |
| 3 | NCSX Project Manager | Yes No |  |
| 3a (Expedited ECP) | NCSX Engineering Manager | Yes No |  |
| 2 | NCSX Federal Project Director | Yes No |  |
| 1 | Associate Director OFES | Yes No |  |
| 0 | Under Secretary of Energy | Yes No |  |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: Mike Viola | Date: March 10, 2005 |
| Overview of Change Type of of ECP: EXPEDITED STANDARD Type of Change: TECHNICAL COST SCHEDULE EDITORIAL (Check all that Apply) Reason for Change: CSPEC calls out a different ASTM standard. MTM has identified an alternate ASTM standard to follow. Specifically, MTM has stated: “For some time now, we have been working with our material suppliers in developing the tubing and pipe requirements for the Port Extensions. We can now confirm the best approach (considering delivery and quality) will be to manufacture the 6", 8", and 10" tubing (roll and weld from plate). We are still researching the 2.5" and 3.5" pipe. We plan to follow ASTM B705 as a guideline during production, but the material certification will be for ASTM B443.” The requested deviation will be to manufacture the 6", 8", and 10" tubing (roll and weld from plate). Follow ASTM B705 as a guideline during production. The material certification will be for ASTM B443. Impacted WBS Elements: 12, Vacuum Vessel Impacts of Change (Briefly Describe): No cost, schedule, or performance impacts. Project has determined that there is no need to revise the CSPEC. PTR, WBS Manager, and RLM have concurred in this RFD. Assessment of Other Options: None List Attachments, Impacted Documents, etc. (1) Request for Deviation NCSX-RFD-12-001 submitted March 7, 2005 |