| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| COVER PAGE (TO BE COMPLETED BY SYSTEMS ENGINEERING SUPPORT MANAGER) |
| Originator: Bob Simmons | Date: July 6, 2005 |
| ECP No: 034 | ECP Title: Changes to MCWF Technical Requirements |
| Required Reviewers |
| Required Reviewers for this ECP: Dave Williamson, Mike Viola, Phil Heitzenroeder, Wayne Reiersen, Brad Nelson, Ron Strykowsky, Judy Malsbury, Jerry Levine |
| ECP Approval Level Expedited ECP? Yes No Change Level: Approving Official: |
| Actions Incorporate into Rev 8 of CSPEC (NCSX-CSPEC-141-03) the requirement for stress relieving for each MCWF casting, change the surface finish requirement to <250 micro-inches in non-critical areas, and revise weld repair requirements to reflect the addition of stress relieving. Issue contract modification to EIO by July 15th specifying NCSX-CSPEC-141-03-Rev. 8 Update cost and schedule baseline by July 15th. |
| APPROVALS (TO BE COMPLETED BY APPROVING OFFICIALS) |
| Change Level | Approving Official | Approval? | Signature |
| 3 | NCSX Project Manager | Yes No |  |
| 3a (Expedited ECP) | NCSX Engineering Manager | Yes No |  |
| 2 | NCSX Federal Project Director | Yes No |  |
| 1 | Associate Director OFES | Yes No |  |
| 0 | Deputy Secretary of Energy | Yes No |  |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: Bob Simmons | Date: July 6, 2005 |
| Overview of Change Type of of ECP: EXPEDITED STANDARD Type of Change: TECHNICAL COST SCHEDULE EDITORIAL (Check all that Apply) Reason for Change: PPPL intends to add a requirement to heat treat each MCWF casting to ensure adequate stress relief PPPL clarified surface finish requirements and weld repair requirements. Impacted WBS Elements: WBS 141 Impacts of Change (Briefly Describe): There are not cost or schedule impacts associated with the change in surface finish and weld repair requirements. These changes are more clarifications and agreements reached with EIO on clarifications. Cost impact to add the requirement of heat treating each MCWF casting is $28.8K and should not impact EIO delivery schedule. Heat treatment was already a requirement to develop the strength required. What is added is a final, lower temperature stress relieving cycle under heat treatment to relax the residual stress in the weld repair area. It is this additional requirement that resulted in a cost increase. Net impact is a required drawdown of contingency of $28.8K from $12,804K to $12, 775.2K. Assessment of Other Options: None List Attachments, Impacted Documents, etc. (1) Updated cost and schedule baseline |