| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| COVER PAGE (TO BE COMPLETED BY SYSTEMS ENGINEERING SUPPORT MANAGER) |
| Originator: Bob Simmons | Date: July 30, 2007 |
| ECP No: 055 | ECP Title: Updated Modular Coil and GRD Requirements |
| Required Reviewers |
| Required Reviewers for this ECP: J.L. Anderson, Hutch Neilson, W. Reiersen, B. Nelson, L. Dudek, A. vonHalle, E. Perry, M. Zarnstorff, J. Levine, J. Malsbury, D. Williamson, J. Chrzanowski |
| ECP Approval Level Expedited ECP? Yes No Change Level: Approving Official: |
| Actions Updated CSPEC-142-05 - will be Rev 1; and GRD (ASPEC-GRD) – will be Rev 5. |
| APPROVALS (TO BE COMPLETED BY APPROVING OFFICIALS) |
| Change Level | Approving Official | Approval? | Signature |
| 3 | NCSX Project Manager | Yes No |  |
| 3a (Expedited ECP) | NCSX Engineering Manager | Yes No |  |
| 2 | NCSX Federal Project Director | Yes No |  |
| 1 | Associate Director OFES | Yes No |  |
| 0 | Deputy Secretary of Energy | Yes No |  |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) ECP- 055 |
| Originator: Bob Simmons | Date: July 30, 2007 |
| Overview of Change Type of ECP: EXPEDITED STANDARD Type of Change: TECHNICAL COST SCHEDULE EDITORIAL (Check all that Apply) Reason for Change: Updated GRD requirements to reflect most recent design requirements and updated Modular Coil Assembly CSPEC to include Type A and Type B modular coil requirements. Impacted WBS Elements: All Impacts of Change (Briefly Describe): CSPEC-142-05 to add in Type A and B Modular Coil Assembly requirements GRD to: Section 3.2.3.1.2 - Increased maximum lift from 30 tons to 45 tons to reflect the crane upgrade in the test cell; Section 3.2.1.5.3.3.2 – modified requirements to reflect use of PF1A uin the initial configuration. Appendix A – revised technical data sheet for initial operation consistent with the use of PF1A coils, limiting the power supply I2t to less than 1.5s. Section 3.3.1.1 – added permeability requirements for materials, welds, and attaching hardware outside the cryostat. Does this Change Impact Material Already Procured or Parts/Assemblies Already Assembled/Manufactured using this Material: Yes No If “Yes”, what is the recommended disposition of this material/part/assembly? Use as is. Specs updated to reflect designs already implemented. Assessment of Other Options: None |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) ECP-055 |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: Bob Simmons | Date: July 30, 2007 |
| Detailed Description of the Change: (Use Continuation Sheets and/or Attach Information/Sketches, As Needed) List Attachments, Impacted Documents, etc. CSPEC-142-05-01 ASPEC-GRD-05 |