| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| COVER PAGE (TO BE COMPLETED BY SYSTEMS ENGINEERING SUPPORT MANAGER) |
| Originator: Bob Simmons | Date: February 22, 2008 |
| ECP No: 059 | ECP Title: Update of VV & Station 1 FPA Requirement Documents |
| Required Reviewers |
| Required Reviewers for this ECP: D. Rej, H. Neilson, P. Heitzenroeder, P. Goranson, M. Viola, L. Dudek, J. Malsbury, J. Levine, M. F. Malinowski, W. Reiersen, B. Nelson |
| ECP Approval Level Expedited ECP? Yes No Change Level: Approving Official: |
| Actions Update NCSX-CSPEC-185 (Station 1 Field Period Assembly) by 2/29/2008 |
| APPROVALS (TO BE COMPLETED BY APPROVING OFFICIALS) |
| Change Level | Approving Official | Approval? | Signature |
| 3 | NCSX Project Manager | Yes No |  |
| 3a (Expedited ECP) | NCSX Engineering Manager | Yes No |  |
| 2 | NCSX Federal Project Director | Yes No |  |
| 1 | Associate Director OFES | Yes No |  |
| 0 | Deputy Secretary of Energy | Yes No |  |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) ECP- 059 |
| Originator: Bob Simmons | Date: February 22, 2008 |
| Overview of Change Type of ECP: EXPEDITED STANDARD Type of Change: TECHNICAL COST SCHEDULE EDITORIAL (Check all that Apply) Reason for Change: Station 1 FPA CSPEC – need to clarify testing requirement relative to normal operating pressure of 300 psig. Station 1 FPA Run Procedure - need to clarify testing requirement relative to normal operating pressure of 300 psig.. Impacted WBS Elements: WBS 12 & WBS 18 Impacts of Change (Briefly Describe): Update both Station 1 CSPEC and Run Procedure to reflect requirement to perform test at 120% of the operating pressure of 300 psig (i.e., 360 psig) Does this Change Impact Material Already Procured or Parts/Assemblies Already Assembled/Manufactured using this Material: Yes No If “Yes”, what is the recommended disposition of this material/part/assembly? – Assessment of Other Options: None. List Attachments, Impacted Documents, etc. None. |