| NCSX RFD Part I | Number: 12-023 | RFD Description: Rearrangement of VV1 Cooling Tubes |
| --- | --- | --- |
| Initiator: M. Viola | Organization: PPPL |
| List of Impacted Documents: (Specification, MIT/QA Plan, SOW, drawing, etc.): None |
| Cost Impact: (If none, so state): Minimal |
| Schedule Impact: (If none, so state: None |
| Quality Impact: (If none, so state): None |
| State Requirement Deviation is Requested For: (Specification, MIT/QA Plan, SOW, drawing, etc.): Drawing SE121-008-r1 (VVSA1 Assembly Station 1, Phase 2) – authorized to move selected cooling tubes to maximize cooling coverage. |
| Full Description of the Deviation Requested: (Use continuation pages, e-mails, letter, sketches, etc. as needed and include amplifying information as appropriate to support deviation request.) Current layout of cooling tubes leaves some relatively large areas not covered. This deviation permits minor relocation of selected cooling tubes (see Attachment) to maximize cooling coverage. |
| Attachments: Annotated picture of VV 1 cooling tubes. |
| Initiator Signature: |

| NCSX RFD Part II | Number: 12-023 | RFD Description: Rearrangement of VV1 Cooling Tubes |
| --- | --- | --- |
| RLM(s): Design: Brad Nelson Manufacturing: Larry Dudek | Organization: Design: ORNL Manufacturing: PPPL |
| Impact on Interfaces with Other WBS Elements/Items: (If none, so state): NONE |
| Design RLM Recommendations: Manufacturing RLM Rcommendations: Approve Do Not Approve Approve Do Not Approve Additional remarks: Although this RFD only applies to VV1, the same philosophy is applicable to the other VV segments. However, individual RFDs will be required to document the specific rearrangements. Should the impacted drawings be formally revised or should the “stamp” process outlined in NCSX Procedure PROC-007 be utilized and should the specification (or other documents) be updated? No, a formal revision required to the drawing or specification is required “Stamp” process outlined in PROC-007 is authorized. If the change is substantial, a revision to the impacted drawings will be required after the third RFD stamp marking a substantial revision is placed on the drawing. This change is NOT substantial and no update to the drawing will ever be required => in this case the “3” RFD stamp process does NOT apply. Does this Change Impact Material Already Procured or Parts/Assemblies Already Assembled/Manufactured using this Material: Yes No If “Yes”, what is the recommended disposition of this material/part/assembly and what is the impact? Only rearrangement of existing cooling tubes – use “as is”. |

| NCSX RFD Part II | Number: 12-023 | RFD Description: Rearrangement of VV1 Cooling Tubes |
| --- | --- | --- |
| RLM: Brad Nelson (ORNL) & Larry Dudek (PPPL) | Organization: ORNL & PPPL |
| Design RLM Signature: Manufacturing RLM Signature: |
| Project Disposition: Approved. No ECP required. NCSX Systems Engineering Support Manager Approved. ECP - assigned and processed. Not Approved. Reason(s) for disapproval: |

# Text boxes

Impacted Areas