| NCSX RFD Part I | Number: NCSX-RFD-14-003 | RFD Description: Material Testing |
| --- | --- | --- |
| Initiator: C. Rudd | Organization: MetalTel |
| List of Impacted Documents: (Specification, MIT/QA Plan, SOW, drawing, etc.) NCSX-CSPEC-141-03-07 Section 4.2.2 |
| Cost Impact: (If none, so state) NONE |
| Schedule Impact: (If none, so state) NONE |
| Quality Impact: (If none, so state) NONE |
| State Requirement Deviation is Requested For: (Specification, MIT/QA Plan, SOW, drawing, etc.): Relaxation of material testing requirement of CSPEC Section 4.2.2 which requires that the material be tested in the transverse and longitudinal directions. |
| Full Description of the Deviation Requested: (Use continuation pages, e-mails, letter, sketches, etc. as needed and include amplifying information as appropriate to support deviation request.) This section requires that material be tested in the transverse and longitudinal directions. This is performed when testing wrought materials, but is typically not performed in cast materials as it offers no significant information. The primary reason is that in cast materials, the grain structure is equiaxed, uniform, and has no directionality. This deviation request will apply to all 18 coil castings. |
| Attachments: MetalTek letter (C. Rudd to Peter Djordjevich of EIO) dated May 29, 2005 |
| Initiator Signature: On Record in the Attached Letter Date: May 29, 2005 |

| NCSX RFD Part II | Number: NCSX-RFD-14-003 | RFD Description: Material Testing |
| --- | --- | --- |
| RLM: Brad Nelson | Organization: Oak Ridge |
| Impact on Interfaces with Other WBS Elements/Items: (If none, so state) NONE |
| RLM Recommended Disposition: Approve Do Not Approve (If recommendation is to approve, ECP will be assigned) Additional remarks: Cognizant Engineer Comments: Our projected factors of safety on allowables (based on the spec properties required, not actuals, which are typically much higher at 77K and would make these factors even higher) are in the range of 2-3. Deviations in properties in transverse and longitudinal directions are estimated to be in the range of 20%. Therefore adopting this change will simplify testing requirements without putting our strength requirements at risk. The spec. will be revised accordingly. RLM Disposition: There is no reason to take the measurements in both directions in a casting. |
| RLM Signature: |
| Project Disposition: (Include ECP Number): NONE |