| NCSX RFD Part I | Number: 14-010 | RFD Description: Material Substitution |
| --- | --- | --- |
| Initiator: Larry Dudek | Organization: PPPL |
| List of Impacted Documents: (Specification, MIT/QA Plan, SOW, drawing, etc.) Drawings SE142C-005 and SE142C-056 |
| Cost Impact: (If none, so state): NONE |
| Schedule Impact: (If none, so state): NONE |
| Quality Impact: (If none, so state): NONE |
| State Requirement Deviation is Requested For: (Specification, MIT/QA Plan, SOW, drawing, etc.): Material specified is C10100 or C10200, ¼ hard |
| Full Description of the Deviation Requested: (Use continuation pages, e-mails, letter, sketches, etc. as needed and include amplifying information as appropriate to support deviation request.): Substitute C11000, ¼ hard due lack of availability for specified material (neither C10100 or C10200 cold rolled plate is readily available. |
| Attachments: |
| Initiator Signature: |

| NCSX RFD Part II | Number: 14-010 | RFD Description: Material Substitution |
| --- | --- | --- |
| RLM: Brad Nelson | Organization: ORNL |
| Impact on Interfaces with Other WBS Elements/Items: (If none, so state): None – WBS 14 only |
| RLM Recommendation: Approve Do Not Approve Additional remarks: Changing from OFHC to ETP copper does not change electrical or structural performance. Does this Change Impact Material Already Procured or Parts/Assemblies Already Assembled/Manufactured using this Material: Yes No If “Yes”, what is the recommended disposition of this material/part/assembly? |
| RLM Signature: |
| Project Disposition: Approved. No ECP required. NCSX Systems Engineering Support Manager Approved. ECP - assigned and processed. Not Approved. Reason(s) for disapproval: |