| NCSX RFD Part I | Number: 14-018 | RFD Description: Type A MCWF Flange Hole Modifications |
| --- | --- | --- |
| Initiator: Mike Griffith | Organization: Major Tool |
| List of Impacted Documents: (Specification, MIT/QA Plan, SOW, drawing, etc.): SE141-114 |
| Cost Impact: (If none, so state): NONE |
| Schedule Impact: (If none, so state: NONE |
| Quality Impact: (If none, so state): NONE |
| State Requirement Deviation is Requested For: (Specification, MIT/QA Plan, SOW, drawing, etc.): SE141-114 |
| Full Description of the Deviation Requested: (Use continuation pages, e-mails, letter, sketches, etc. as needed and include amplifying information as appropriate to support deviation request.): Major Tool noted casting interference at the bolt locations as shown in the attached figures for the Type A castings – see Attachment (1). For the A1 casting details shown on SE141-114, the two holes will be changed from clearance holes to tapped holes. This casting interference is similar to what was noted on the Type C winding forms, but more are severe in these areas for the Type A MCWFs. Per Attachment (2), MTM proposes to change the existing clearance holes to tapped holes with the insert shown. NCSX reviewed the remaining flange holes all the Type A castings and developed the concept shown on Attachment (3) in which a number of the clearance holes have been changed to tapped holes. All Type A MCWFs -- including A1 with the exception of the two holes addressed in Attachment (2) -- shall be manufactured per this. |
| Attachments: Pictures showing interference details. Annotated SE141-114 all the proposed changes to the Type A1 MCWF. Proposed changes to all Type A MCWFs |
| Initiator Signature: Mike Griffith/Phil Heitzenroeder |

Attachment (1)

Type A MCWF Interferences

Relief area cut into cast wall

The pictures below illustrate how much casting wall interference there will be on the type A casting.  The current machining models for all three winding forms have this interference problem to some degree.  The models have a 3” counterbore that extends .75” from the face and the remainder of the feature is a 1.5” radius (see below).  This is why Major Tool had to perform the grinding around the counterbores on C4 in order to get the 3” diameter gage to fit.

Attachment (2)

Proposed Resolution to Type A MCWFs

Attachment (3)

Definition of Holes to be Modified for ALL Type A MCWFs

(Reference: D.Williamson e-mail of May 4, 2006)

\

| NCSX RFD Part II | Number: 14-018 | RFD Description: Type A MCWF Flange Hole Modifications |
| --- | --- | --- |
| RLM: Brad Nelson | Organization: ORNL |
| Impact on Interfaces with Other WBS Elements/Items: (If none, so state): NONE |
| RLM Recommendation: Approve Do Not Approve Additional remarks: This RFD also includes a modification by the NCSX Project for the identified Type A MCWF flange holes - See Attachment (3). The minimum stud clearance required behind the tapped holes shall not be less than ¼” to ensure full thread engagement. These modifications will be incorporated in a future revision to this drawing. In the interim that “stamp” process will be used to annotate SE141-114. Does this Change Impact Material Already Procured or Parts/Assemblies Already Assembled/Manufactured using this Material: Yes No If “Yes”, what is the recommended disposition of this material/part/assembly? A1 Casting will be accepted “as is” with the exception of the two holes shown. |
| RLM Signature: |
| Project Disposition: Approved. No ECP required. NCSX Systems Engineering Support Manager Approved. ECP will be assigned and processed. Not Approved. Reason(s) for disapproval: |