| NCSX RFD Part I | Number: 14-022 | RFD Description: Reorientation of Type B MCWFs Lead Slots |
| --- | --- | --- |
| Initiator: Phil Heitzenroeder | Organization: PPPL |
| List of Impacted Documents: (Specification, MIT/QA Plan, SOW, drawing, etc.) |
| Cost Impact: (If none, so state): NONE |
| Schedule Impact: (If none, so state: NONE |
| Quality Impact: (If none, so state): NONE |
| State Requirement Deviation is Requested For: (Specification, MIT/QA Plan, SOW, drawing, etc.): SE141-115, Sheet 7, Quad B4 |
| Full Description of the Deviation Requested: (Use continuation pages, e-mails, letter, sketches, etc. as needed and include amplifying information as appropriate to support deviation request.) A NCSX Project-initiated modification to improve the lead block positioning resulted in a slight reorientation (2.2° horizontal change at the top and 0.114” vertical change) of the lead slots as shown on Attachment (1). |
| Attachments: (1) Rapid response transmittal Concerning the Type B Lead Slots (May 24, 2006) |
| Initiator Signature: Dave Williamson |

Attachment (1)

Rapid Response Transmittal Concerning the Type B Lead Slots

Date:  May 24, 2006

A NCSX Project-initiated change resulted in a reorientation of the lead slots in the Type B MCWFs as shown below.  EIO is requested to immediately implement this change.  A drawing change is in progress and a formal Request for Deviation will be issued within 2 days.

| NCSX RFD Part II | Number: 14-022 | RFD Description: Reorientation of Type B MCWFs Lead Slots |
| --- | --- | --- |
| RLM: Brad Nelson | Organization: ORNL |
| Impact on Interfaces with Other WBS Elements/Items: (If none, so state): NONE |
| RLM Recommendation: Approve Do Not Approve Additional remarks: NCSX Project issued a “fast response” authorization on May 24, 2006 [(Attachment (1)]. Should the impacted drawings be formally revised or should the “stamp” process outlined in NCSX Procedure PROC-007 be utilized? Formal revision required (Note if > 3 RFDs, then a formal revision via ECN is required) “Stamp” process outlined in PROC-007 is authorized. Drawing will be updated at a later date. Does this Change Impact Material Already Procured or Parts/Assemblies Already Assembled/Manufactured using this Material: Yes No If “Yes”, what is the recommended disposition of this material/part/assembly? |
| RLM Signature: |
| Project Disposition: Approved. No ECP required. NCSX Systems Engineering Support Manager Approved. ECP - assigned and processed. Not Approved. Reason(s) for disapproval: |