| EIO RFD | Number: RFD-14-026 (EIO RFD #110806-1P dated November 8th, 2006) | RFD Description: Remaining B Castings (B2 thru B6) Thin Wall Condition |
| --- | --- | --- |
| Initiator: Peter Djordjevich | Organization: Energy Industries of Ohio |
| List of Impacted Documents: Drawing wall thickness dimensions shown on NCSX drawing: SE141-115 (Type-B Modular Coil Winding Form) |
| Quality Impact: None per PPPL evaluation of stress regions. Per previous agreement on 1.21” minimum wall for B-1 casting (see CAR 1538 approved by NCSX Project on 2/7/2006) |
| State Requirement Deviation is Requested For: Drawing wall thickness specifications shown on NCSX drawing SE141-115 (Type-B Modular Coil Winding Form) |
| Full Description of the Deviation Requested Allow thin wall condition on B castings, which was discovered on casting B1. Actual drawing specification wall thickness = 1.5” + .25” – 0 Requested dimensional deviation 1.5” +0 .25”/ -0 .29” max Lowest dimension observed 1.21” wall B1, balance of B castings range 1.3”-1.4” wall after Evaluation. |
| Attachments: (1) CAR 1538 for B-1 casting. |
| Initiator Signature: Peter A Djordjevich Date: 11/08/06 EIO QA |

| NCSX RFD Part II | Number: RFD-14-026 (EIO RFD #110806-1P dated November 8th, 2006) | RFD Description: Remaining B Castings (B2 thru B6) Thin Wall Condition |
| --- | --- | --- |
| RLM(s): Design: Brad Nelson Manufacturing: Larry Dudek | Organization: Design: ORNL Manufacturing: PPPL |
| Impact on Interfaces with Other WBS Elements/Items: (If none, so state) |
| Design RLM Recommendations: Manufacturing RLM Rcommendations: Approve Do Not Approve Approve Do Not Approve Additional remarks: Deviation Request is modified to state dimensions as 1.5” +0 .25”/ -0 .20” max (vs. -0.29” max since only B-1 casting (addressed by CAR 1538) has the 1.21” dimension. Should the impacted drawings be formally revised or should the “stamp” process outlined in NCSX Procedure PROC-007 be utilized and should the specification (or other documents) be updated? No, a formal revision required to the drawing or specification is required – THIS CHANGE WILL BE INCORPORATED WITH CHANGES BEING PROCESSED FOR ECN-5185. “Stamp” process outlined in PROC-007 is authorized. If the change is substantial, a revision to the impacted drawings will be required after the third RFD stamp marking a substantial revision is placed on the drawing. This change is NOT substantial and no update to the drawing will ever be required => in this case the “3” RFD stamp process does NOT apply. Does this Change Impact Material Already Procured or Parts/Assemblies Already Assembled/Manufactured using this Material: Yes No If “Yes”, what is the recommended disposition of this material/part/assembly and what is the impact? B2 through B6 castings will be accepted if within the stated dimensional tolerance band of 1.5” +0.25”/-0.20” |
| Design RLM Signature: Manufacturing RLM Signature: |
| Project Disposition: Approved. No ECP required. NCSX Systems Engineering Support Manager Approved. ECP - assigned and processed. Not Approved. Reason(s) for disapproval: |