| NCSX RFD Part I | Number: RFD14-027 | RFD Description: Radiographic Waiver For Weld Upgrade To C6 |
| --- | --- | --- |
| Initiator: Peter Djordjevich | Organization: Energy Industries of Ohio |
| List of Impacted Documents: (Specification, MIT/QA Plan, SOW, drawing, etc.) MIT/QA plan repair welding radiographic requirement |
| Cost Impact: (If none, so state) None |
| Schedule Impact: (If none, so state:None |
| Quality Impact: (If none, so state): None |
| State Requirement Deviation is Requested For: (Specification, MIT/QA Plan, SOW, drawing, etc.) MIT/QA,SOW waive radiographic inspection C6 leadblock upgrade repair |
| Full Description of the Deviation Requested: (Use continuation pages, e-mails, letter, sketches, etc. as needed and include amplifying information as appropriate to support deviation request.) NC submitted #NC21114 Major Tool - C6 leadblock raised pad over ground during foundry trimming operations, resulting in a lack of sufficient material to machine pad and incorporate threaded holes. Since this was an addition of material to fully form the pad rather than a excavation to repair a defect, it was requested that radiographic inspection of the area be waived. This was NOT addressed in the NCR. Area will be visually inspected, and penetrant inspected to alleviate any concerns. |
| Attachments:None. NC21114 already on file. |
| Initiator Signature: Peter Djordjevich Date: 03/1/2007 |

NCSX RFD Part II Number: RFD14-027 RFD Description: Radiographic Waiver For Weld Upgrade To C6 RLM(s): Design: B. Nelson Manufacturing: L. Dudek Organization: Design: ORNL Manufacturing: PPPL Impact on Interfaces with Other WBS Elements/Items: (If none, so state): NONE Design RLM Recommendations: Manufacturing RLM Rcommendations: Approve Do Not Approve Approve Do Not Approve Additional remarks: NCR #NC21114 Major Tool - C6 leadblock raised pad over ground during foundry trimming operations, resulting in a lack of sufficient material to machine pad and incorporate threaded holes. However this only addressed the repair and not the waiver of the radiographic inspection (per CSPEC). This RFD confirms verbal authorization provided by PPPL. Should the impacted drawings be formally revised or should the “stamp” process outlined in NCSX Procedure PROC-007 be utilized and should the specification (or other documents) be updated? No, a formal revision required to the drawing or specification is required “Stamp” process outlined in PROC-007 is authorized. If the change is substantial, a revision to the impacted drawings will be required after the third RFD stamp marking a substantial revision is placed on the drawing. This change is NOT substantial and no update to the drawing will ever be required => in this case the “3” RFD stamp process does NOT apply. Does this Change Impact Material Already Procured or Parts/Assemblies Already Assembled/Manufactured using this Material: Yes No If “Yes”, what is the recommended disposition of this material/part/assembly and what is the impact?

| NCSX RFD Part II | Number: 14-027 | RFD Description: Radiographic Waiver For Weld Upgrade To C6 |
| --- | --- | --- |
| RLM(s): Design: B. Nelson Manufacturing:L. Dudek | Organization: Design: ORNL Manufacturing: PPPL |
| Design RLM Signature: Manufacturing RLM Signature: |
| Project Disposition: Approved. No ECP required. NCSX Systems Engineering Support Manager Approved. ECP - assigned and processed. Not Approved. Reason(s) for disapproval: |