| NCSX RFD Part I | Number: 14-028 | RFD Description: Minimum Wall Thickness for Nut Clearance on Type C Modular Coils |
| --- | --- | --- |
| Initiator: Steve Langish | Organization: PPPL |
| List of Impacted Documents: (Specification, MIT/QA Plan, SOW, drawing, etc.) SE141-116G |
| Cost Impact: (If none, so state): NONE |
| Schedule Impact: (If none, so state: NONE |
| Quality Impact: (If none, so state): NONE |
| State Requirement Deviation is Requested For: (Specification, MIT/QA Plan, SOW, drawing, etc.) SE141-116G |
| Full Description of the Deviation Requested: (Use continuation pages, e-mails, letter, sketches, etc. as needed and include amplifying information as appropriate to support deviation request.) Drawing SE141-116G requires a 0.74” wall thickness at “ Section H26-H26 at Hole 26 “ (see attached drawing). However ~1.1” of wall thickness exists at 3.375” above spotface and about 1” of material is required to provide ample nut clearance. This RFD permits elimination of the wall thickness requirement at Hole 26 for the Type C Modular Coils. |
| Attachments: Annotated copy of SE141-116G |
| Initiator Signature: |

| NCSX RFD Part II | Number: 14-028 | RFD Description: Minimum Wall Thickness for Nut Clearance on Type C Modular Coils |
| --- | --- | --- |
| RLM(s): Design: Manufacturing: | Organization: Design: Manufacturing: |
| Impact on Interfaces with Other WBS Elements/Items: (If none, so state): NONE |
| Design RLM Recommendations: Manufacturing RLM Rcommendations: Approve Do Not Approve Approve Do Not Approve Additional remarks: Should the impacted drawings be formally revised or should the “stamp” process outlined in NCSX Procedure PROC-007 be utilized and should the specification (or other documents) be updated? No, a formal revision required to the drawing or specification is required “Stamp” process outlined in PROC-007 is authorized. If the change is substantial, a revision to the impacted drawings will be required after the third RFD stamp marking a substantial revision is placed on the drawing. This change is NOT substantial and no update to the drawing will ever be required => in this case the “3” RFD stamp process does NOT apply. Does this Change Impact Material Already Procured or Parts/Assemblies Already Assembled/Manufactured using this Material: Yes No If “Yes”, what is the recommended disposition of this material/part/assembly and what is the impact? Use as is with this authorized deviation |

| NCSX RFD Part II | Number: 14-028 | RFD Description: Minimum Wall Thickness for Nut Clearance on Type C Modular Coils |
| --- | --- | --- |
| RLM: Design: Brad Nelson Fabrication: Larry Dudek | Organization: Design: ORNL Fabrication: PPPL |
| Design RLM Signature: Manufacturing RLM Signature: |
| Project Disposition: Approved. No ECP required. Stamp to be applied. NCSX Systems Engineering Support Manager Approved. ECP - assigned and processed. Not Approved. Reason(s) for disapproval: |