Assembly Steps

Plans for Addressing Potential Issues

| Potential Issue | Possible Recovery/Mitigation Plan |
| --- | --- |
| Set Up Activities |  |
|  | Tooling not rigid enough | Reinforce tooling Redesign tooling – add to Risk Register |
|  | Coils still to flexible | Reinforce coils |
|  | Alignment not within tolerances bars | Redo alignment until meet requirements |
|  | Shim sizes not consistent and cannot be reproduced | Redesign & order new shims |
| A-B Coil Assembly |  |
|  | Alignment not within tolerances | Redo alignment until meet requirements |
|  | Weld distortion excessive | Rack coils into shape (?) Remove weld and redo until meet requirements |
| A-B Coil Assembly to C Coil |  |
|  | Alignment not within tolerances | Redo alignment until meet requirements |
|  | Weld distortion excessive | Rack coils into shape (?) Remove weld and redo until meet requirements |
| Inflate All Shim Bags |  |
|  | Shim bags rupture when filling | Cleanup coil and replace shim bag ?? |
| Complete Local Services & Interface Details |  |
|  | ?? | ?? |
| Final Measurements & Transfer MCHP to Holding Area |  |
|  | Alignment not within tolerances | Stiffen supports. |
|  | ??? | ?? |

# Text boxes

- MC Fit-up Check & Surface Insulation

- Pre-Measurement of MHCP Type A/B/C Coil Flanges & Interfacing Type Type A Coil Flange

- Alumina Shim Sizing & Preparation

- Pre-Installation Station 2 Set-up (for First Article Only

- Pre-Assembly A-A (DELETED)

- Verify MC’s of MCHP will come together.

- Verify that the individual coils can be racked into proper shape.

- Verify that metrology measurements can be accurately taken and reproduced.

- Define shim sizes and compress to arrive at satisfactory shim set for MCHP assembly.

- Tooling/fixtures setup.

Potential Issues

- Tooling not rigid enough

- Coils still to flexible

- Alignment not within tolerances bars

- Shim sizes not consistent and cannot be reproduced

- Rack A coil & measure.

- Locate nose shim locations on A nose region & install set of shims.

- Install shim bags in wing areas.

- Lower B & measure – install remaining shims, studs, supernuts and torque to 50%.

- Adjust B coil to install nose shims and measure.

- Recheck A alignment during these processes

- Weld A & B nose shims – measure alignments.

- Once initial A & B welding & alignment efforts completed, determined hole eccentricity and then rebolt  and tighten to full torque.

6.0 A-B Modular Coil Assembly

Potential Issues

- Alignment not within tolerances

- Weld distortion excessive

1

1

- Attach A-B assembly & fixture to another 20° wedge.

- Locate nose shim locations on B nose region & install set of shims.

- Install shim bags in wing areas.

- Lower C & measure – install remaining shims, studs, supernuts and torque to 50%.

- Adjust C coil to install nose shims and measure.

- Recheck A-B assembly alignment during these processes

- Weld C nose shims – measure alignments.

- Once initial C welding & alignment efforts completed, determined hole eccentricity and then rebolt  and tighten to full torque.

7.0 A-B Coil Assembly to C Coil

Potential Issues

- Alignment not within tolerances

- Weld distortion excessive

11.0 Final Measurements & Transfer MCHP to Holding Area

Potential Issues

- Shim bags rupture when filling

8.0 Inflate All Shim Bags

Fill wing bladders & cure.

Repeat for each subsequent MCHP.

END

Potential Issues

- Alignment not within tolerances

- ???

- Measure all tooling balls & record/save data & run copies of installation procedures.

- Install/identify 3 primary fiducials to be used on Station 3.

- Do final measurements & record results. Measure bolt lengths on all tension fasteners & record/save results.

- Mark part, install base supports, remove from stand & measure weight of completed MCHP.  Remove to holding area.

Potential Issues

- ???

Inject Stycast or other suitable compound to fill all shim spaces to trap VV/MC insulation.

10.0 Complete Local Services  & Interface Details

9.0 Install Trim Coils (Moved to Station 3)