Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

# Text boxes

- MC Fit-up Check & Surface Insulation

- Pre-Measurement of MHCP Type A/B/C Coil Flanges & Interfacing Type Type A Coil Flange

- Alumina Shim Sizing & Preparation

- Pre-Installation Station 2 Set-up (for First Article Only)

- Pre-Assembly A-A (DELETED)

Major Activities

- Verify MC’s of MCHP will come together (Gross Fitup)

- Verify that the individual coils can be racked into proper shape.

- Verify that metrology measurements can be accurately taken and reproduced.

- Define shim sizes and compress to arrive at satisfactory shim set for MCHP assembly.

- Tooling/fixtures setup.

- Define shim sizes and compress to arrive at satisfactory shim set for MCHP assembly

- A-B Modular Coil Assembly

Major Activities

- Rack A coil & measure.

- Locate nose shim locations on A nose region & install set of shims.

- Install shim bags in wing areas.

- Lower B & measure – install remaining shims, studs, supernuts and torque to 50%.

- Adjust B coil to install nose shims and measure.

- Recheck A alignment during these processes

- Weld A & B nose shims – measure alignments.

- Once initial A & B welding & alignment efforts completed, determine hole eccentricity and then rebolt  and tighten to full torque.

- Tooling not rigid enough - RETIRED

- Coils still to flexible - RETIRED

- Alignment not within tolerances bars- RETIRED

- Shim sizes not consistent and cannot be reproduced

- Alignment – iterated until met requirements

- Shims – redesign/order new shims

- Alignment not within tolerances

- Weld distortion excessive

Stiffen supports.

- Alignment – iterate until meet requirements

  - Weld distortions  - Internally Reinforce/Rack MC

- A-B Coil Assembly to C Coil

Major Activities

- Attach A-B assembly & fixture to another 20° wedge.

- Locate nose shim locations on B nose region & install set of shims.

- Install shim bags in wing areas.

- Lower C & measure – install remaining shims, studs, supernuts and torque to 50%.

- Adjust C coil to install nose shims and measure.

- Recheck A-B assembly alignment during these processes

- Weld C nose shims – measure alignments.

- Once initial C welding & alignment efforts completed, determined hole eccentricity and then rebolt  and tighten to full torque.

- Inflate All Shim Bags

- Install Trim Coils (Moved to Station 5)

- Complete Local Services  & Interface Details

Major Activities

- Fill wing bladders & cure

- Inject Stycast or other suitable compound to fill all shim spaces to trap VV/MC insulation.

- Alignment not within tolerances

- Weld distortion excessive

- Alignment – iterate until meet requirements

- Weld distortions  - Internally Reinforce/Rack MC

- Shim bags rupture when filling

- ???

- Cleanup coil and replace shim bag

- ???

- Final Measurements & Transfer MCHP to Holding Area

Major Activities

- Measure all tooling balls & record/save data & run copies of installation procedures.

- Install/identify 3 primary fiducials to be used on Station 3.

- Do final measurements & record results. Measure bolt lengths on all tension fasteners & record/save results.

- Mark part, install base supports, remove from stand & measure weight of completed MCHP.  Remove to holding area.

REPEAT FOR EACH SUBSEQUENT MCHP

- Alignment not within tolerances

- ???