# Text boxes

- Pre-Installation Set-Up

- Pre-Assembly of Left MCHP

- Pre-Assembly of Right MCHP

- Anchor tooling (floor mounted tracks, support carts, adjuster bar, AirLoc Wedgemounts, temporary scaffolding, etc.

  - Measure CG of MCHPs

- Establish global coordinate system and install laser screens.

- Perform Metrology for  alignment

  - Install Station 3 site monuments as needed to perform metrology measurements.

  - Measure alignment of left & right MCHPs

10.0 Transfer Period to NSTX Test Cell

Potential Issues

- Tooling not rigid enough

- Alignment not within tolerances bars

Potential Issues

- Vertical and lateral supports do not provide sufficient stiffness

- Unable to achieve desire tolerances

- Install VV NBI support stand & install VVSA to base support structure

- Using metrology, take tooling ball readings to properly position VVSA to global coordinate system.

5.0 Pre-Assembly Right MCHP

Potential Issues

- Lasers do not provide accurate positioning

- Screens too far or too close

- A-A fitup indicates too much deformation in MCHP

- Establish required assembly path and mark on screens.

- Set up lasers & determine alignment – adjust as needed

- Do dry runs with MCHPs and evaluate ability of crane to follow path.

4.0 Install Laser Screens/Dry Runs with MCHPs

1

8.0 Weld Inboard Shims

Weld inboard shims and re-measure alignment

Using metro

1

- Attach VV permanent vertical supports at points on Type A MC

- Attach VV temporary vertical supports at points on Type B MC

- Transfer loads VV vertical supports

- Install VV lateral supports & align VVSA to MC

9.0 VVSA Attachments to MC

Potential Issues

- Weld distortions exceed tolerances

Potential Issues

- Alignment of coil to vessel incorrect

- Interferences between vessel and coil

- Move carts out of way & position AirLoc Wedgemount leveler in lowered position

- Using SISSCO crane actuators with laser guidance, move MCHP over the VV.  Bring up AirLoc Wedgemount levelers to stabilize unit and measure alignment.

- When satisfactory, transfer full load to AirLoc Wedgemount leveler.

6.0 Install Left MCHP over VVSA

7.0 Install Right MCHP over VVSA

Potential Issues

- Frame too flexible

- VVSA distorts & makes lockin errors too large

- Transfer period to the transfer support frame

Potential Issues

- Transfer support frame to flexible and causes period distortions

Repeat for other two periods

END