Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

# Text boxes

- Pre-Installation Set-Up

- Pre-Assembly of Left MCHP

- Pre-Assembly of Right MCHP

Major Activities

- Anchor tooling (floor mounted tracks, support carts, adjuster bar, AirLoc Wedgemounts, temporary scaffolding, etc.

  - Measure CG of MCHPs

- Establish global coordinate system and install laser screens.

- Perform Metrology for  alignment

  - Install Station 3 site monuments as needed to perform metrology measurements.

  - Measure alignment of left & right MCHPs

4.0 Install Laser Screens/Dry Runs with MCHPs

Major Activities

- Establish required assembly path and mark on screens.

- Set up lasers & determine alignment – adjust as needed

- Do dry runs with MCHPs and evaluate ability of crane to follow path.

- Pre-Assembly Right MCHP

Major Activities

- Install VV NBI support stand & install VVSA to base support structure

- Using metrology, take tooling ball readings to properly position VVSA to global coordinate system.

- Tooling not rigid enough

- Alignment not within tolerances bars

- Tooling

  - Reinforce tooling – add to Risk Register

  - Redesign tooling – add to Risk Register

- Alignment tolerances -Adjust coils until meet tolerance bands

- Frame too flexible

- VVSA distorts & makes lockin errors too large

- Lasers do not provide accurate positioning

- Screens too far or too close

- Laser screens move – not ridid

- A-A fitup indicates too much deformation in MCHP

- Lasers

  - Ensure lasers operating properly – as shown  during prototyping of  principle

  - Revert to original fixture scheme – add to Risk Register

  - Sceens - Adjust position of screens/reinforce

  - A-A fitup indicates too much deformation in MCHP  - Reinforce MCHP (unlikely feasible)

  - Frame - Reinforce frame with I-beams, etc.

  - VVSA distortion - Internally Reinforce/Rack VV

6.0 Install Left MCHP over VVSA

7.0 Install Right MCHP over VVSA

Major Activities

- Move carts out of way & position AirLoc Wedgemount leveler in lowered position

- Using SISSCO crane actuators with laser guidance, move MCHP over the VV.  Bring up AirLoc Wedgemount levelers to stabilize unit and measure alignment.

- When satisfactory, transfer full loadto AirLoc Wedgemount leveler

8.0 Weld Inboard Shims

Major Activities

- Weld inboard shims and re-measure alignment

9.0 VVSA Attachments to MC

Major Activities

- Attach VV permanent vertical supports at points on Type A MC

- Attach VV temporary vertical supports at points on Type B MC

- Transfer loads VV vertical supports

- Install VV lateral supports & align VVSA to MC

10.0 Transfer Period to NSTX Test Cell

Major Activities

- Transfer period to the transfer support frame

REPEAT FOR OTHER TWO PERIODS

- Alignment of coil to vessel incorrect

- Interferences between vessel and coil

- Components damaged during assembly.

- Vessel Alignment - Redo alignment until meet requirements

- Interferences between coil to vessel incorrect - Likely a clamp or support which has possibility of removing or relocating

- Damage to component???

  - Redesign tooling – add to Risk Register

- Alignment tolerances -Adjust coils until meet tolerance bands

- Weld distortions exceed tolerances

- Adjust with wing support

- Perform Physics review and adjust via trim coils

- Vertical and lateral supports do not function properly

- Unable to achieve desired tolerances

- Vertical and lateral supports do not function properly - Redesign supports. – add to Risk Register

- Unable to achieve desired tolerances - ???

Transfer support frame too flexible and allows components to clash during transport

- Buffer and protect individual components

- Install physical stops to prevent motion