Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

# Text boxes

- Component Preparations

- Cut-off short dome port & install insulation system & heater tape/thermocouples system around all ports

- Pre-Installation Set-Up

- Install period support fixture.

- Install FPA on support stand & engage base of MC.

- Install internal & external working platforms

- VV Port Installation

- Install domes, inserting the long port through the MC hole opening & weld dome shell to VV.

- Install small dome ports & remaining circular ports. Leak check after each port is welded.

- Port Boot Seal Assembly Installation

- Install boots on all ports (except Port 4)

Support fixture not stiff enough for personnel access

Reinforce support fixture with I-beams, etc

Final measurements not within tolerances

Boots do not fit.

- Trim coil assembly concepts not supported by detailed drawings

- Existing hardware on MC interferes with trim coil supports

- Cannot reach to weld support clamps

Custom fit boots as needed

6.0 Install MC Lead/Coolant Connections

- Install MC coolant  lines on each MC & position for TF coil installation & routing through PF structure

- Move working platforms as necessary for TF coil installation

- Install Right TF Coil Assemblies

- Install Left TF Coil Assemblies\

Note: 6.0 & 7.0 have identical processes

- Rotate 2 individual coils over MC & temporarily support off B & C coils. (Note: final TF coil for this side and left side of FPA cannot be installed until Station 6)

- Attach temporary supports as needed, disengage base of MC, & install TF support brackets

- Slide TF assemblies against TF support brackets one at a time

- Install machine support plates & re-engage base of MC

- TF Fit-Up Checks

- Perform a fit-up check of the 4 TF coils

- Tack Port 4’s

- Tack weld Port 4’s & install boots

Concepts not fully supported by detail drawings of routings

Design still evolving – schedule supports time to develop detailed plans and procedures.

- Concepts not fully supported by detailed drawings

- Interferences preclude installation of TF coil assemblies

- Damage components during assembly (higly unlikely)

- Buffer and protect individual components

- Install physical stops to prevent motion

NONE IDENTIFIED

NONE IDENTIFIED

- Concepts not fully supported - design still evolving – schedule supports time to develop detailed plans and procedures.

- Interferences – reassess options to resolve interferences => may require some disassembly

- Damage to component – remove TF coil assemblies from Period & repair damaged component with existing spare

- Install Right TF  Assemblies

Major Activities

- Transfer completed period to Station 6

REPEAT FOR PERIODS 2 & 3

Transfer support frame too flexible and allows components to clash during transport

NONE IDENTIFIED

Diagnostic lead routing concepts not fully supported by detail drawings of routings

- Tolerances a problem at W-7X – revisit NCSX tolerances (NCSX VV ports have 1” radial tolerance/port holes have ½” TPT)

- Support structure may interfere with  lower ports installation

- Leak check fails on one or more ports

- Install PF Structural Members & rout MC leads and coolant lines

- Install PF support structure around TF coils and rout MC leads and coolant lines

- Install MC Coolant Manifold

- Install MC coolant manifold outside the PF coils (in area of PF-6) & connect all MC coolant lines (40 top and bottom each)

- Install Rogowski Coils

- Install Rogowski coils on each end of VV (left side) & route leads initially between space by Port 8 & spool piece opening

- Final Measurements

- Obtain set of Period 1 alignment fiducials for lacatin VV within the MC

- Using laser, align tooling balls on each MCHP

- Using monuments on VV  for alignment, bring VV  into proper alignment, adjusting VV supports as necessary.

- Install/verify three primary fiducials to be used in positioning the period in Station 6.

- Make final measurement of all fiducials, VV end flanges, & Type C end flanges

- Perform final checks and acceptance tests.

- Install port within radial clearance with port hole as-built – may require physics evaluation to understand impact on diagnositics.

- Review support structure/lower port clearance in advance & provide installation tooling as needed

- Identify leak point(s) and repair weld and re-test

\

- Trim Coil Installation

- Install trim coil supports onto MC

NEED TOM BROWN INPUT HERE!

- Trim coil assembly concepts - design still evolving – schedule supports time to develop detailed plans and procedures

- MC interferences - designing trim coil supports earlier in schedule to provide location template to review positioning in advance.

- Support clamp inaccessibility - ????

MC leads and coolant line routing concepts not fully supported by detail drawings of routings

NONE IDENTIFIED

MC leads and coolant line routing concepts not fully supported by detail drawings of routings

Concepts not fully supported - design still evolving – schedule supports time to develop detailed plans and procedures.

Concepts not fully supported - design still evolving – schedule supports time to develop detailed plans and procedures.

Concepts not fully supported - design still evolving – schedule supports time to develop detailed plans and procedures.

- Physics determine impact of out-of-tolerances o performance

- Project assess steps necessary to recover tolerances if unable to accept out-of-tolerance conditions