| Princeton Plasma Physics Laboratory Procedure |
| --- |
| ‘ Procedure Title: Field Period Assembly Station 1 (VVSA) Activities |
| Number: D-NCSX-FPA-001 | Revision: 00 | Effective Date: December 14, 2005 Expiration Date: (2 yrs. unless otherwise stipulated) |
| Procedure Approvals |
| Author: Tom Brown |
| ATI: Mike Viola |
| RLM: Larry Dudek |
| Responsible Division: NCSX Project |
| Procedure Requirements Designated by RLM LABWIDE: |
| X | Work Planning Form # WP-???? (ENG-032) |  | Lockout/Tagout (ESH-016) |
|  | Confined Space Permit (5008,SEC.8 Chap 5) |  | Lift Procedure (ENG-021) |
|  | Master Equip. List Mod (GEN-005) | X | ES&H Review (NEPA, IH, etc.) NEPA 1283 |
|  | RWP (HP-OP-20) |  | Independent Review |
|  | ATI Walkdown | X | Pre-Job Brief |
| X | Post-job Brief * |  |  |
| D-SITE SPECIFIC: |
| X | D-Site Work Permit (OP-AD-09) |  | Door Permit (OP-G-93) |
|  | Tritium Work Permit (OP-AD-49) |  | USQD (OP-AD-63) |
| X | Pre-Job Brief (OP-AD-79) |  | T-Mod (OP-AD-03) |
|  | ** DCA/DCN (OP-AD-104) # |  |  |

* Required for installations involving internal vacuum installations, critical lifts, and for the initial installation of repetitive work.

** 	OP-AD-104 was voided by procedure ENG-032. However, DCA’s that were open at the time of adoption of ENG-032 are still considered valid for work approval purposes.

REVIEWERS (designated by RLM) Rec’d/ Incorp. Comments

Accountable Technical Individual. …………Mike Viola

Test Director

Independent Reviewers George Labik , Buddy Kearns,

D-Site Shift Supervisor

Independent

NCSX Dimensional Control Coordinator ……………………….Brent Stratton X

Vacuum

NCSX Field Supervisors… Steve Raftopoulos, Tom Meighan

Project Engineer for Stellerator Systems (WBS 1) Manager……Brad Nelson (ORNL) X

WBS Manager for Modular Coils (WBS12).. …………………Paul Goranson (ORNL)

Quality Assurance/Quality Control. ……Judy Malsbury, J. Boscoe, Colin Phelps XX

Maintenance and Operations Division

Energy Conversion System/Motor Control Division

Engineering ……………………………………..

Environmental Restoration & Waste Management Division

Environmental, Safety & Health……………………………………Jerry Levine X

Industrial Hygiene………………………………………………... Bill Slavin X

Health Physics…………………

RLM ………………………………………………………………..Larry Dudek X

| TRAINING (designated by RLM) |
| --- |
| No training required ______________ | Instructor Mike Viola |
| Personnel (group, job title or individual name) | Read Only | Instruction Pre-job Briefing | Hands On |
| Lead Tech. |  | X |  |
| Technicians performing task |  | X |  |
| Field Supervisors |  | X |  |
| Quality Control Representative |  | X |  |
| Training Rep. |
| RLM: Larry Dudek |

RECORD OF CHANGE

| Revision | Date | Description of Change |
| --- | --- | --- |
| 00-dA | 12/14/05 | Initial release (Draft A) |

TABLE OF CONTENTS

1	Scope	1

1.1	Introduction	1

1.2	Scope	1

1.3	Identification of Coil being manufactured:	Error! Bookmark not defined.

2	Applicable Documents	1

2.1	NCSX-MIT/QA-142-01:	1

2.2	NCSX-PLAN-CMFOP-00:	1

2.3	D-L-NCSX-983 Lifting Modular Coil Winding Forms	1

2.4	D-L-NCSX-984 Lifting Modular Coil/ Ring Assemblies	Error! Bookmark not defined.

2.5	D-NCSX-MCF-005 Dimensional Control & Metrology for the NCSX MC	Error! Bookmark not defined.

2.6	D-NCSX-PLAN-MCWDC     Modular Coil Dimensional Control Plan	Error! Bookmark not defined.

3	Safety Requirements:	1

3.1	Job Hazard Analysis:	2

4	Prerequisites & Conditions:	2

4.1	Pre-Job Briefing:	2

4.2	Daily Operations Startup and Shutdown:	2

4.3	Reference Torque Values:	2

5	Materials and Parts for this station	2

6	Fabrication Process	3

6.1	Daily Startup Activities:	3

6.2	Daily Shutdown Activities:	3

6.3	Transporting MCWF from Casting Prep Station to Winding Station:	3

6.4	Install MCWF in Winding Station Turning Fixture:	4

6.5	Inspect Cladding:	6

6.6	Conductor Payout Spool:	6

6.7	Installation of Inner Groundwrap Insulation	6

6.8	Install Lower G-11CR Winding Blocks	8

6.9	Installation of Winding Clamp Side Bars	8

6.10	Dimensional Inspection	9

6.11	Positioning Lacing bands onto Winding Form	10

6.12	Position Leads for Side “A” Winding	11

6.13	Brazing Side “A” Lower Lead Connectors:	11

6.14	Fitup of Leads- Side “A”	15

6.15	Insulate Lower Leads- Side “A”	16

6.16	General Winding Notes:	16

6.17	Metrology Measurements/Tolerance Control:	18

6.18	Winding Operation- Side “A”	18

6.19	Upper Side “A” Leads	22

6.20	Preparation for Winding Side “B”	22

6.21	Inspect Cladding:	23

6.22	Positioning of lower leads for side “B” winding	24

6.23	Brazing Side “B” Lower Lead Connectors:	24

6.24	Fitup of Leads- Side “B”	27

6.25	Insulating Side “B” Lower Leads	27

6.26	General Winding Notes:	27

6.27	Winding Operation Side “B”	27

6.28	Upper Side “B” Leads	31

6.29	Winding Pack Adjustments	31

6.30	Completion of Groundwrap Installation	32

6.31	Installation of Diagnostic Loops	34

6.32	General Procedure- Outer Chill Plate/Cooling Tube Assembly:	35

6.33	Chill Plate Installation:	39

6.34	Final Positioning of Upper Leads sides “A” and “B”	40

6.35	Brazing Side “A” and “B” Upper Leads:	41

6.36	Fitup of Leads- Sides “A” and “B”	45

6.37	Insulate Upper Leads- Side “A” and “B”	45

6.38	Lead Area-Upper Chill Plates	46

6.39	Hydrostatic Tests:	47

6.40	Flow Check:	48

6.41	Winding Block Filler Strips	49

6.42	Outer Lead Chill Plate and Side Plates	49

6.43	Install Top Plate	50

6.44	Completion of Sides “A” and “B”:	50

6.45	Pre-VPI Electrical Insulation Tests:	51

6.46	Installation of Bag Mold:	53

7	Completion of Activities at Winding Station:	58

7.1	Document Verification:	58

7.2	Field Package:	58

7.3	Approval:	59

Index of Figures

Figure 1- Turning Fixture	5

Figure 2- Upper Support Plates	5

Figure 3- Orientation of Copper spools	6

Figure 4- Groundwrap scheme	7

Figure 5- Winding Clamp-Groundwrap Storage	8

Figure 6- Re-installation of Lower Winding Blocks	8

Figure 7-Location of Side Bar Shims	9

Figure 8- Position of Lacing Straps	10

Figure 9-Cross-section of Lacing straps position	11

Figure 10- Conductor w/Phenolic Blocks	12

Figure 11- Conductor in Forming Blocks	12

Figure 12- Removing Nylon Serve from conductor	12

Figure 13- Conductor in Connector	12

Figure 14- Cable Connector	13

Figure 15- Front Face-“Nibco” Braze Unit Control	13

Figure 16-Feeding the Lead Connector w/Sil-Fos	14

Figure 17- Positioning leads	16

Figure 18-Schematic of Turn Insulation Tester	17

Figure 19- Groundwrap Overlap Scheme	33

Figure 20-Diagnostic Loops	34

Figure 21- Outer Chill Plates	36

Figure 22- Staking Chill Plates	36

Figure 23- Setting Chill Plate and Tubing	37

Figure 24- Front Face- "Nibco Soldering Unit Control	38

Figure 25- Soldering Cooling Tube (photos a & b)	38

Figure 26- Cleaning of Soldered Chill Plates	39

Figure 27- Chill Plates in Lead Area	39

Figure 28- Outer Chill Plates	39

Figure 29- Upper Lead Winding Block	40

Figure 30- Upper Lead Blocks and Leads	45

Figure 31- Final Terminal Connections	45

Figure 32-Upper Lead Area Chill Plates	46

Figure 33- Winding Block Filler Strips	49

Figure 34- Outer Lead Area Chill Plate	50

Figure 35- Lead Area Side Plates	50

Figure 36-Top Plate Bushing	51

Figure 37- Lead Area Top Plate	51

Figure 38- Glass Roving Between Cooling Tubes	53

Figure 39- Installation of Bag Mold	54

Figure 40- Silicone Bag Mold	54

Figure 41- Sprue washers and extensions	55

Figure 42-Epoxy/Glass Mixture- "Cotton Candy"	57

Figure 43-Application Epoxy Glass Shell	57

Figure 44- Epoxy/Glass shell	58

Index of Tables

Table 1-Cooling Tube Hydrostat Results	47

Table 2-Cooling Tube Flow Results	48

Table 3- Pre-VPI Megger Test Results	Error! Bookmark not defined.

Table 4- Type "C" Coil Drawings	60

# Scope

## Introduction

The Field Period Assembly process consists of the following steps:

- Vacuum Vessel Assembly (Stage 1)

- Assembly of the Modular Coils

- Installation of Vacuum Vessel Support Hardware

- Assembly of the TF Coils

- Assembly of the External Trim Coils

- Assembly of the Ports

- Vacuum Vessel Final Support Adjustment

## Scope

This procedure is used to assembly the vacuum vessel. It includes:

- Vacuum Vessel receipt and inspection

- Replacement of Port Flanges with Stage 1 assembly flanges

- Checking the Center of Gravity and then mounting the Vacuum Vessel segment on the preparation fixture

- Metrology Set-Up and Initial Vessel Measurements

- Marking of Magnetic Loop and Coolant Line Locations on the Vessel

- Vertical Port Component Installations

- Installation of Magnetic Flux Templates and Flux Loops on the Vessel

- Final Loop Measurements and Heating and Cooling Line Installation

- Termination of Loops and Verification Checks

- Preparation and Transfer of Completed Vacuum Vessel to Holding Area

- Mounting Completed Vacuum Vessel Assembly on the Stage 3 Stand

## Identification of Vacuum vessel Segment Being Prepared:

Station Number:  				  (Location Where Work Will be Performed)

Vacuum Vessel Segment #:  _________________ (Segment 1, 2, or 3)

Vacuum Vessel Segment #:  ___________  Vacuum Vessel Identification #:  _________

# Applicable Documents

## NCSX-MIT/QA-185-01:

All applicable documents associated with this procedure, are identified in the MIT/QA Plan, document number NCSX-MIT/QA-185-00.

## NCSX-PLAN-FPA1DC-00:

All FPA Stage 1 dimensional work processes are governed by the “NCSX Field Period Assembly Station 1 Dimensional Control Plan”, document number NCSX-PLAN-FPA1DC-00.

## D-L-NCSX-???:

## Procedure for lifting vacuum vessel assemblies.

## Others????

# Safety Requirements:

All work will be performed in a safe manner in accordance with PPPL Environmental Safety & Health Directives ES&H 5008 and the “Integrated Safety Management” (ISM) policy.

## Job Hazard Analysis:

A JHA will be generated for each winding station, identifying existing or potential workplace hazards and to evaluate the risk of worker injury or illness associated with job tasks. (Reference document ESH-004 “Job Hazard Analysis”)  The IH representative will review the JHAs for accuracy as well as completeness.  It will be reviewed with all activity participants at the Pre-Job briefings.

# Prerequisites & Conditions:

## Pre-Job Briefing:

A pre-job briefing will be held, describing the processes and safety issues prior to starting any part of this procedure.	  Attendance shall be documented via training sign-in sheet.

Pre job Briefing complete: _______________________________ _________________

MC Field Supervisor                           Date

## Daily Operations Startup and Shutdown:

Each working day, it is required to complete and initial the daily operations startup log to ensure that the station is ready to commence work activities for the day.  The signoff log is located in the Daily Station Log.  See section 6.1 and 6.2 for details.

## Reference Torque Values ???:

Unless a torque value is specified, the following values shall be used whenever the procedure requires a torquing operation: (Low carbon steel hardware)

3/8-16UNC ……	18 ft-lbs		3/8-24UNF ……	19 ft-lbs 	½-13 UNC ……	38 ft-lbs		½ -20 UNF ……	40 ft-lbs		5/8-11 UNC….	83 ft-lbs		5/8-18 UNF…	95 ft-lbs

¾-10 UNC..……	105 ft-lbs	¾-16 UNF …….	102 ft-lbs	1-8 UNC …       236 ft-lbs	1-14 UNF ……..	212 ft-lbs	1 1/4 UNC ……	432 ft-lbs	1 ½-6 UNC …...732 ft-lbs

# Materials and Parts for this station

The following materials and/or equipment will be used with this procedure.

| General Description | Material | Reference Document/Product No. |
| --- | --- | --- |
| Conductor | CDA 101 compacted copper rope | NCSX-CSPEC-142-03-01 |
| Turn Insulation- glass tape | S-2 Dry glass 0.004 in. thick |  |
| Ground insulation-glass tape | S-2 Dry glass 0.007 in. thick |  |
| Ground insulation | Kapton- 5mil Type HN |  |
| Ground insulation | Kapton- 2mil Type HN |  |
| Diagnostic Flux loops | 316 SS Mineral cable insulated with Teflon heat shrink tubing | A.R.i. Incorp. [0.032 dia. w/ 0.006 in. thk. sleeve] |
| Solvent | Chlor-Free Degreaser | CRC Product No. 03185 [MSDS #05032] |
| Solvent | Acetone | MSDS# 00561 |
| Lead winding and enclosure fillers | G-11CR | Drawing list to be added as addendum for each coil type as approved |
| Chill Plates | C10100 Copper | Drawing list to be added as addendum for each coil type as approved |
| Cooling tubes | Copper |  |
| Lead support structures (winding blocks) | G-11CR | Drawing list to be added as addendum for each coil type as approved |
| Lead terminal Assembly | Copper and G-11CR | SE142C-050 |
| Cable connector | OFS Copper | SE142C-059 |
| Braze material | Sil-Fos | MSDS # 03437 |
| Turning Fixture | Equipment | Drawing no. SE144-008 |
| Conductor payout spool | Equipment | Drawing no. SE144-120 |
| Winding clamps | Equipment | Drawing SE144-080 |
| Bag sealing agent | 2-part RTV 11 (white) | MSDS #02214 |
| Bag mold material | Self-fusing Tape | Product no.7643A24 2 in. wide gray silicone tape |
| Bag mold shell material | chopped glass tape w/ epoxy* |  |
| Epoxy system for shell mold | *Resin/hardener 3561/2039 | MSDS # 03516 & 03515 |
| Bag sealing | RTV 108 (caulking) | MSDS #01525 |
| Braze inhibitor | Nicrobraz Green Stop-Off | MSDS #4748 |
| Adhesive Tape for Lacing | 3M High Performance tape | Product no. 3M9485PC |
| Solder for chill plate tubes | Stay-Brite Rosin Core solder | MSDS# 05160 [J.W. Harris] |

# Fabrication Process

This fabrication procedure is to be used as guide to complete the station no. 1 activities.  Deviation from this procedure for processes that DO NOT affect the design of the coil can be made during the winding process with the concurrence of the VV Field Supervisor.  All deviations shall be documented in the procedure and initialed by the VV Field Supervisor prior to implementing the deviations.  Deviations that may effect the design of the coil requires a Request for Deviation “RFD” approval.  The RFD must be approved prior to proceeding.  Procedure changes need to be incorporated into the document via “Minor Procedure Changes” or “Revisions”.

## Daily Startup Activities:

### Check all daily supplies needed:

### Verify operation of all equipment needed that day.

### Check station for cleanliness

### Check that safety guards are intact

### Check that safety equipment needed for day’s activities are available

### Check that the day’s travelers and procedures are in their document holder.

### Once completed, date and initial daily log at the back of the Station Log Book.

## Daily Shutdown Activities:

### Turn off power to equipment not in use.

### Clean entire workstation area.

### Verify that all Traveler and data sheet information is complete.

### The Lead Technician shall verify that the Station’s Log Book has been completed and signed for the day.

### Once completed, date and initial daily log at the back of the Station Log Book.

## Receipt and Inspection of the Vacuum Vessel Segment:

### Receive and perform visual inspections. Take metrology measurements.  Resolve impact of out of tolerance conditions.

Verified by: _________________________ Date: __________________

Lead Technician

### Verify all tooling ball locations with respect to MTM data packages and resolve any differences.

### Measure end flanges and compare with theoretical position (practice for matching spacer).

Verified by: _________________________ Date: __________________

Field Supervisor

## Replace Port Flanges with Station 1 Assembly Flanges:

Reference Drawing:  SE184-001

### Remove two horizontal port flanges and hardware (if attached). Note: Horizontal ports have 32 bolt assemblies and the should be bagged for future use.  See Figure 6-1.

Figure 6-1 Station 1 Port Horizontal Flange

### Remove NB port flange and hardware (if attached).  Note: NB ports have 34 bolt assemblies and the should be bagged for future use.

### Slip VV heating/cooling cryostat interface flanges over each vertical port. The VV heating/cooling cryostat interface flanges need to be temporarily located on the vertical ports as the Station 1 support fixture will inhibit there installation.  Reference drawing: se123-164.  See Figure 6-2

Figure 6-2 Heating and Cooling Cryostat Interface Flanges

### Attach Station 1 port flanges with "O-Ring cord" seal material cut to length to protect sealing surface.  Insert bolt assemblies into every other hole.  The support axle Weldment and hoist rings should be preassembled to the vertical port flanges.  It is assumed that the vessel will be cleaned at a later stage so vessel cleanliness is not an issue.

Verified by: _________________________ Date: __________________

Lead Technician

## Check Center of Gravity and Mount of Station 1 Preparation Fixture:

Reference Drawing:  SE184-001

### Lubricate support axle and axle support cradle. Add lubricate to the support axle Weldment and support axle cradle components (cradle top and cradle base) to reduce VV rotation friction.

### Check VV CG using crane with attachment to hoist rings lift from a horizontal position and rotate vessel to a vertical position. [Need a procedure here???] Check to see if the part is in a near vertical position.  Mark CG location.

### If CG is found to be off by a value greater than 2.0" return VV to its original position.  Remove and relocate support axle Weldment to the proper CG location.

Verified by: _________________________ Date: __________________

Lead Technician

### Mount VV on VV Prep fixture. Set VV on the Station 1 Prep station support fixture in a horizontal position.  Secure in place by bolting down support axle cradle top support blocks.  Install quick release pin. See Figure 6-3 and Figure 6-4.

Figure 6-3 Vacuum Vessel in Horizontal Position

### Install worm gear.  Remove the hoist ring from the VV on the side with the worm gear support.  Install worm gear axle Weldment and worm gear, engaging worm wheel.  See Figure 6-4.

Figure 6-4 Installation Details

Verified by: _________________________ Date: __________________

Lead Technician

## Metrology Set-up and Initial Vessel Measurements:

### Using a marker mark the positive toroidal field direction on the front an back surface of the vacuum vessel.  Note that the worm gear system is identified as the VV down direction.  See Figure 6-5 for field direction marking.

Figure 6-5 - Arrows Mark Toroidal Direction

### Set up measurement fiducials provided by MTM plus add additional monuments as specified in FP Dimensional Control Plan for Station 1 (NCSX-PLAN-FPA1DC-00).  Rotate vessel to convenient access positions.  Note that some monuments will be located on the body of the VV.

### Perform a best fit to the  fiducial measurements using the monuments on the VV body.  Settings will be made with the vessel NBI port at a +/- 60° off vertical position as indicated in Figure 6-6 and Figure 6-7. Secure vessel position by inserting release pin and tighten support axle cradle bolts. Verify that the mounting system is rigid enough to meet FP Dimensional Control Plan metrology requirements. Add additional bracing if required.

Figure 6-6 Vacuum Vessel 60º Off Vertical Position

Figure 6-7  Vacuum Vessel in Rotated Position

Verified by: _________________________ Date: __________________

Lead Technician

## Marking of Magnetic Loop and Coolant Line Locations on the Vessel:

### Secure vessel position with the  in the 60º NBI port at a +/- 60° off vertical position by inserting release pin and tighten support axle cradle bolts.

### Mark surface for 138 loop placement with the vessel NBI port at a +/- 60° off vertical position.  It is expected that three Leica positions will be required on each side to accurately mark the vessel.  The Leica metrology system will be used to accurately define four marks (within +/- 0.040") for each of 138 loops except for the loops at the symmetry points which shall be positioned within +/- 0.010".  The magnetic loop points shall be marked using an "X" to indicate the locating point.  For ease of locating templates mark template number at the center of four points.  See Figure 6-8 below and Reference drawing XXXXX and ProE model XXXXX for loop designation, point marking details and model geometry data

Figure 6-8 - Template Numbering

### Mark surface for coolant line stud placement with the vessel NBI port at a +/- 60° off vertical position. The Leica metrology system will be used to locate 300 studs per half period at ~ 8" spacing. Fine accuracy is NOT important. The stud locations shall be marked with a circle with a name designation added (A1, A2, A3...) to define the stud series.  An outline of the coolant hold-down bracket shall also be marked.  See Figure 6-9 below and Reference drawing se121-008 Sheet 4 for loop designation, point marking details. Note that the overlay o  the coolant lines over the diagnostic loops with the red spheres indicating the size of the coolant line attachment brackets.

Figure 6-9  Overlay of the Coolant Lines Over the Diagnostic Loops

Verified by: _________________________ Date: __________________

Lead Technician

## Vertical Port Component Installations

### Mark heating/cooling support bracket A and B attachment studs and mark bracket clip outline.

### Install cryostat interface mounting flange on vertical ports.  Before welding the interface flange on the vertical ports the cryostat interface flange must be moved to the proper assembly position (see Figure 6-10).

Figure 6-10  Cryostat Interface Flange

### Install cryostat interface flange on vertical ports.

### Install heating/cooling header brackets.

### Install thermocouple mount plates and thermocouples to VV vertical ports.  Reference drawing: se121-004.

### Install heating strips on vessel vertical ports.  See Figure 6-11.

Figure 6-11  Installation of Heating Strips

Verified by: _________________________ Date: __________________

Lead Technician

## Installation of Magnetic Flux Templates and Flux Loops

### Rotate VVSA to convenient installation position for installing loop templates.  Each loop template has four locating notches which shall be used be install loops to within ± 0.160" of the marked locations, except for the loops at the symmetry points which shall be positioned within ± 0.020".  The locating direction arrow should be aligned in the general direction of the positive toroidal field direction arrows marked on the vessel surface. See

Figure 6-12  Installing Loop Templates

### Install flux templates.  Note that Templates 2-Th180-1 thru 2-Th180-5 need to be placed and the flux loop wires run before adjacent loops are placed because of local template interferences.  See Figure 6-13.

Figure 6-13 –Installation of Templates

### Install all remaining flux loop templates.  Except for the mentioned wire runs in 6.9.2, all remaining templates shall be installed before any loop wires are run. (May be done earlier with new loop pattern)

### Mark vessel surface showing twisted pair leads path.

### Install loop wires and then remove templates.  ProE model YYYY for guide in running leads.  A.) Use electrical color identifying code to mark wires as twisted wire leaves template, along its path and after it passes through the horse collar.  B.) Lay I leads loosely to accommodate the installation of the H/C tube heat transfer bases. C.) Route excess lead lengths though the 2 3/4  CF and protect the excess length from damage.

### Install voltage loops.  Refer to drawing YYYYYY and ProE model YYYY for guide in running voltage loops.

Verified by: _________________________ Date: __________________

Lead Technician

## Final Loop Measurements and Heating/Cooling Line Installation

### Install H/C tube studs.   The flux loops leads can be temporarily moved to facilitate this process,

### Attach H/C tube clamp hardware used for mounting coolant lines.

### Perform final flux loop lead tie down.  Perform final routing of flux loop leads and hold down with spot-welded shim stock straps spaced approximately 4” apart.  (Is this the correct value?) Note that the radial build of the twisted leads should not exceed 1/8”, except in a few places (not under H/C tube paths) where it may be necessary for one set of leads to cross another.

### Install remaining thermocouple mount plates and thermocouples to VV shell - Reference drawing: se121-004.

### Measure as-built paths of flux loops to within ±0.25 mm (0.010”). This shall be done by tracing the groove between the two turns of each loop using a Laser Tracker probe with a small tip.

### Install H/C tube support brackets.    Install H/C support bracket Weldment A and B and tube mount strap.  See Figure 6-14.  Reference Drawing: se121-008.

Figure 6-14 H/C Support Brackets

### Secure H/C cryostat flange and H/C manifolds - Reference Drawings: se121-008 and  se123-049.  See Figure 6-15.

Figure 6-15  H/C Cryostat Flange, Manifolds and Flex Tubing Installation

### Install H/C flex tube. See Figure 6-15.

### Install H/C hard tubing.  See Figure 6-16.

Figure 6-16 Hard Tubing Installation

### Leak check coolant tubes.

Verified by: _________________________ Date: __________________

Lead Technician

## Loop Termination and Verification Check

### Final installation of twisted leads.

#### Check continuity and resistance to ground of each pair.

#### After H/C line bases are completed dress in cables and install hold down support

### Verify tagging and conductors by by physical check or use oscillator.

### Trim cable length - cut excess length to 1 ft using diamond wheel to cut end flatten.

#### Install gas seal and partial junction box (JB).

#### Insert CF gasket.

#### Route cables thru predrilled holes in CF blank.

#### Route cables thru pre punctured holes of silicon rubber gasket.

#### Route cables thru predrilled holes in JB base.

#### Install CF threaded fasteners thru the JB base and torque to get metal to metal contact between JB base and CF ring.

#### Check the cable configuration and condition in cryostat region.

### Install gas seal and partial junction box (JB).

#### Insert CF gasket.

#### Route cables thru predrilled holes in CF blank.

#### Route cables thru pre punctured holes of silicon rubber gasket.

#### Route cables thru predrilled holes in JB base.

#### Install CF threaded fasteners thru the JB base and torque to get metal to metal contact between JB base and CF ring.

#### Check the cable configuration and condition in cryostat region.

### Terminate cables.

#### Determine length to terminal box (TB).

#### Flat cut cable with diamond wheel.

#### Strip back sheath with tool provided leaving xxxx of conductor exposed.

#### Clean MgO from conductor.

#### Apply moisture barrier seal to MgO.

#### Install Teflon heat shrink tubing ( 4:1 ).

### Strain relieve cables inside JB using spot welded SS shim stock.

### Connect cables to TB by first installing TB/circuit boards into front panel of JB and then installing conductors into TB.

### Complete JB assembly and install conductors into TB.

### Protect D sub Connector by placing a protective cover over the D Subminiature connector.

Verified by: _________________________ Date: __________________

Lead Technician

## Prepare and Transfer Completed VV to Holding Area

### Install NB port temporary cover and NB angle support bracket.  This is done while the completed vessel is on the support stand.  The temporary cover may be installed during step [1.1.5] if it has been fabricated.  The NB angle support bracket must be install at this stage.

### Set for VV removal by first rotating VV to horizontal position.  Secure in place by bolting down support axle cradle top support blocks.  Install quick release pin.  Remove worm gear and install hoist ring.

### Remove completed VV from support stand. Lift VV with crane and reposition to a vertical position with the worm gear side of the vessel in the down position.

### While on the crane install base support plate.  See Figure 6-17.

Figure 6-17  Assembled Vacuum Vessel Segment

Verified by: _________________________ Date: __________________

Lead Technician

## Mount Completed Vacuum Vessel Segment of the Station 3 Stand

### Mount vacuum vessel segment on the  Station 3 support stand.  See Figure 6-18.

Figure 6-18 Completed Vacuum Vessel Segment on Station 3 Support Stand

### Perform metrology alignment to orient the VV on Stage 3 stand.  Details TBD.

Verified by: _________________________ Date: __________________

Lead Technician

# Completion of Activities:

## Document Verification:

Verify that all pertinent data in the procedure and data sheets have been completed.

## Field Package:

Ensure that all data sheets, photographs, QC inspection sheets, etc are included in the Field Package.

## Approval:

Prior to releasing a modular coil to the Vacuum-Pressure-Impregnation station (VPI), it is required that the all-responsible individuals sign the release indicating that all processes at the winding station have been satisfactorily completed.  The release will include signatures from the Station Lead Technician, Field Supervisor and the QC representative.

All winding form preparation activities have been satisfactorily completed.

Lead Technician: ____________________________ Date: ____________________

Field Supervisor: ____________________________ Date: ____________________

QC shall verify completion of documentation:

Quality Control Representative: _________________________ Date: ________

The modular coil with “Bag Mold” is ready for transfer to the VPI station no. 5:

Comments:

Table 7-1- Vacuum Vessel Drawings

| Drawing Numbers | Drawing Description |
| --- | --- |
| Top level assembly and layouts |  |
| se140-103.drw | MODULAR COIL ASSEMBLY TYPE-C |
| se142c-019.drw | TYPE-C WINDING PACK DIMENSIONS |
| se142c-016.drw | TYPE-C ELECTRICAL SCHEMATIC |
| se142c-015.drw | TYPE-C COOLING SCHEMATIC |
| SE141-103 | Winding form assembly, |
| ds141-036.drw | STUD, 1.375-6UNC-2A X 9 LG |
| ds141-038.drw | INSULATING WASHER |
| ds141-060.drw | NUT, 12PT HEX 1.375-6UNC-2B |
| ds141-079.drw | FLAT WASHER |
| se141-078.drw | POL BREAK SHIM ASSEMBLY TYPE-C |
| se141-103.drw | MOD COIL WINDING FORM ASSEMBLY TYPE-C |
| se141-116.drw | PRODUCTION WINDING FORM TYPE-C |
| se141-123.drw | MCWF TYPE-C STUD WELDMENT |
| SE142C-018 | Side-A winding pack assembly, |
| se142c-018.drw | TYPE-C SIDE-A WINDING PACK ASSEMBLY |
| se142c-134.drw | TYPE-C SIDE-A LOWER LEAD BLOCK COMBINED |
| se142c-136.drw | TYPE-C SIDE-A UPPER LEAD BLOCK COMBINED |
| se142c-382-101_105.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-106_110.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-111_115.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-116_120.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-121_125.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-126_130.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-131_135.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-136_140.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-141_145.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-146_150.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-151_155.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-156_160.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-161_165.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-166_170.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-171_175.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-176_180.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-181_185.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-186_190.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-191_195.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-196_200.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-201_205.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-206_210.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-211_215.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-216_220.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-221_225.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-226_230.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-231_235.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-236_240.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-241_245.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-246_250.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-251_255.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-256_260.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-261_265.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-266_270.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-271_275.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-276_280.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-281_285.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-286_290.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-291_295.drw | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-384-101_105.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-106_110.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-111_115.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-116_120.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-121_125.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-126_130.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-131_135.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-136_140.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-141_145.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-146_150.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-151_155.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-156_160.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-161_165.drw | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-386-166_170.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-171_175.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-176_180.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-181_185.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-186_190.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-191_195.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-201_205.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-206_210.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-211_215.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-216_220.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-221_225.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-226_230.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-231_235.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-236_240.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-241_245.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-246_250.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-251_255.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-256_260.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-261_265.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-266_270.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-271_275.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-276_280.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-281_285.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-286_290.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-291_292.drw | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-388-101_105.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-106_110.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-111_115.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-121_125.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-126_130.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-131_135.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-136_140.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-141_145.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-146-150.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-151-155.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-156_160.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-161_165.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-166_170.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-171_175.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-176_180.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-181_185.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-186_190.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-191_195.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-201_205.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-206_210.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-211_215.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-216_220.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-221_225.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-226_230.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-231_235.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-236_240.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-241_245.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-246_250.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-251_255.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-256_260.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-261_265.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-266_270.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-271_275.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-276_280.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-281_285.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-286_290.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-291_292.drw | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| SE142C-017 | Side-B winding pack assembly, |
| se142c-017.drw | TYPE-C SIDE-B WINDING PACK ASSEMBLY |
| se142c-135.drw | TYPE-C SIDE-B LOWER LEAD BLOCK COMBINED |
| se142c-137.drw | TYPE-C SIDE-B UPPER LEAD BLOCK COMBINED |
| se142c-482-101_105.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-106_110.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-111_115.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-116_120.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-121_125.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-126_130.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-131_135.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-136_140.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-141_145.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-146_150.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-151_155.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-156_160.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-161_165.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-166_170.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-171_175.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-176_180.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-181_185.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-186_190.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-191_195.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-196_200.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-201_205.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-206_210.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-211_215.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-216_220.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-221_225.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-226_230.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-231_235.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-236_240.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-241_245.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-246_250.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-251_255.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-256_260.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-261_265.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-266_270.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-271_275.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-276_280.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-281_285.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-286_290.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-291_295.drw | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-484-101_105.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-106_110.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-111_115.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-116_120.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-121_125.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-126_130.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-131_135.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-136_140.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-141_145.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-146_150.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-151_155.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-156_160.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-161_165.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-166_170.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-171_175.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-176_180.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-181_185.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-186_190.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-191_195.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-196_200.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-201_205.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-206_210.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-211_215.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-216_220.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-221_225.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-226_230.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-231_235.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-236_240.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-241_245.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-246_250.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-251_255.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-256_260.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-261_265.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-266_270.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-271_275.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-276_280.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-281_285.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-286_290.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-291_295.drw | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-486-101_105.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-106_110.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-111_115.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-121_125.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-126_130.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-131_135.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-136_140.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-141_145.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-146-150.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-151-155.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-156_160.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-161_165.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-166_170.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-171_175.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-176_180.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-181_185.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-186_190.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-191_195.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-201_205.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-206_210.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-211_215.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-216_220.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-221_225.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-226_230.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-231_235.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-236_240.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-241_245.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-246_250.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-251_255.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-256_260.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-261_265.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-266_270.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-271_275.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-276_280.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-281_285.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-286_290.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-291_292.drw | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-488-101_105.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-106_110.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-111_115.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-121_125.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-126_130.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-131_135.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-136_140.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-141_145.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-146-150.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-151-155.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-156_160.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-161_165.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-166_170.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-171_175.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-176_180.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-181_185.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-186_190.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-191_195.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-201_205.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-206_210.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-211_215.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-216_220.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-221_225.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-226_230.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-231_235.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-236_240.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-241_245.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-246_250.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-251_255.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-256_260.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-261_265.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-266_270.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-271_275.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-276_280.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-281_285.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-286_290.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-291_292.drw | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| SE142C-050 | Leads terminal assembly, |
| se142c-047.drw | TYPE-C JUMPERS BASE BLOCK |
| se142c-049.drw | TYPE-C JUMPERS INSULATOR |
| se142c-050.drw | TYPE-C LEADS TERMINAL ASSEMBLY |
| se142c-051.drw | TYPE-C TERMINAL JUMPER #1 |
| se142c-052.drw | TYPE-C TERMINAL JUMPER #2 |
| se142c-053.drw | TYPE-C TERMINAL JUMPER #3 |
| se142c-054.drw | TYPE-C TERMINAL JUMPER #4 |
| se142c-055.drw | TYPE-C SHORT TERMINAL LUG |
| se142c-056.drw | TYPE-C LONG TERMINAL LUG |
| se142c-057.drw | TYPE-C TERMINAL LUG CONNECTOR |
| se142c-058.drw | TYPE-C TERMINAL LUG CONNECTOR |
| se142c-059.drw | TYPE-C CABLE CONNECTOR |
| se142c-062.drw | WASHER .53 ID 1.25 OD X .06 THK |
| se142c-063.drw | FLAT WASHER |
| se142c-064.drw | 1/2-13unc SCREW |
| se142c-065.drw | .53 ID .875 OD .06 THK FLAT WASHER |
| se142c-068.drw | INSULATING WASHER |
| se142c-069.drw | INSULATING SLEEVE |
| SE142C-233 | Lead blocks enclosure, |
| se142c-226.drw | LEAD BLOCKS WEDGE, SIDE-B |
| se142c-227.drw | LEAD BLOCKS WEDGE, SIDE-A |
| se142c-183.drw | LEAD BLOCKS CHILL PLATE, SIDE-A |
| se142c-241.drw | LEAD BLOCKS CHILL PLATE, SIDE-B |
| se142c-201.drw | LEAD BLOCKS SUPP COOLING TUBE, SIDE-A |
| se142c-202.drw | LEAD BLOCKS SUPP COOLING TUBE, SIDE-A |
| se142c-220.drw | LEAD BLOCKS SIDE PLATE, SIDE-A |
| se142c-221.drw | LEAD BLOCKS SIDE PLATE, SIDE-B |
| se142c-184.drw | LEAD BLOCKS TOP PLATE |
| SE1405-275P | Clamp assembly, |
| se1405-258p.drw | WASHER, BELLEVILLE |
| se1405-261p.drw | SCREW, SET, 15/16-20 UNEF-2A X 3/8 |
| se1405-263p.drw | WASHER, SPERICAL, CONVEX |
| se1405-267.drw | TRC CLAMP PAD |
| se1405-272.drw | CLAMP SWIVEL STUD |
| se1405-273.drw | CLAMP SWIVEL PAD |
| se1405-274.drw | TRC FLAT WASHER 3/4 OD |
| se1405-275p.drw | CLAMP ASSEMBLY, SHORT |
| se1405-276.drw | BAR, CLAMP, HORIZONTAL |
| se1405-277.drw | PISTON, SPHERICAL, CONCAVE |
| se1405-278.drw | CLAMP BUSHING |

# Comments

Step 1.1.5 does not exist. What is the correct step number?

# Text boxes

Base support plate

Direction Arrows

Worm Gear Is VV Down Positon.

Support Axle Cradle Base

Worm Gear

Hoist Ring

Worm Gear Axle Weldment

2j3

Template ID Numbers

Stage 1 Port Horizontal Flange

Heating/Cooling Cryostat Interface Flanges (se123-164)

Support Axle Cradle Top

Templates 2-Th180-1 thru 2-Th180-5

NB Angle Support Bracket

2j4

NB Port Temporary Cover

60°

Quick Release Pin

Support Axle Weldment

Heating/Cooling Support Bracket A and B attachment studs.

Cryostat Interface Mounting Flange

Heating/Cooling Header Bracket

2j5

The Red Dots Are Locating Points on the Vessel That will be Used to Align the Notches of the Loop Flat Patterns.

Arrows Will Be Marked on the Vessel Surface to Indicate the Positive Toroidal Direction.

Temporary Cryostat Interface flange position

and Location Direction

thermocouple mount plates

Flat Pattern Loop Designate

on Four Sides

Heating Strip

0.040” Ø NotchLocated

Heating/Cooling Support Bracket A and B

H/C Support Bracket Weldment and Tube Mounting Straps

Cryostat Interface Flange Bolted to Mounting Flange

H/C Support Bracket Weldment and Tube Mounting Straps

H/C Manifolds

H/C Flex Tubing

Brazetyte Reducer union

Copper tubing

Compression Fittings