| Princeton Plasma Physics Laboratory Procedure |
| --- |
| ‘ Procedure Title: Modular Coil Fabrication-Post VPI Activities |
| Number: D-NCSX-MCF-004 | Revision: 01 | Effective Date: June 6, 2006 Expiration Date: (2 yrs. unless otherwise stipulated) |
| Procedure Approvals |
| Author: James H. Chrzanowski: |
| ATI: James H. Chrzanowski: |
| RLM: Larry Dudek: |
| Responsible Division: NCSX Project |
| Procedure Requirements Designated by RLM LABWIDE: |
| X | Work Planning Form # WP-1188 & 1138 (ENG-032) |  | Lockout/Tagout (ESH-016) |
|  | Confined Space Permit (5008,SEC.8 Chap 5) |  | Lift Procedure (ENG-021) |
|  | Master Equip. List Mod (GEN-005) | X | ES&H Review (NEPA, IH, etc.) NEPA 1283 |
|  | RWP (HP-OP-20) |  | Independent Review |
|  | ATI Walkdown | X | Pre-Job Brief |
| X | Post-job Brief * |  |  |
| D-SITE SPECIFIC: |
| X | D-Site Work Permit (OP-AD-09) |  | Door Permit (OP-G-93) |
|  | Tritium Work Permit (OP-AD-49) |  | USQD (OP-AD-63) |
| X | Pre-Job Brief (OP-AD-79) |  | T-Mod (OP-AD-03) |
|  | ** DCA/DCN (OP-AD-104) # |  |  |

* Required for installations involving internal vacuum installations, critical lifts, and for the initial installation of repetitive work.

** 	OP-AD-104 was voided by procedure ENG-032. However, DCA’s that were open at the time of adoption of ENG-032 are still considered valid for work approval purposes.

REVIEWERS (designated by RLM) Rec’d/ Incorp. Comments

Accountable Technical Individual. …………J. Chrzanowski

Test Director

Independent Reviewer Buddy Kearns

D-Site Shift Supervisor

Independent

NCSX Dimensional Control Coordinator ……………………….

Vacuum

NCSX Field Supervisors… Tom Meighan X

Project Engineer for Stellerator Systems (WBS 1) Manager……Brad Nelson (ORNL) X

Independent NCSX Engineering ………………… P.J. Fogarty (ORNL) X

Quality Assurance/Quality Control. …… Colin Phelps X

Maintenance and Operations Division

Energy Conversion System/Motor Control Division

Engineering ……………………………………..

Environmental Restoration & Waste Management Division

Environmental, Safety & Health……………………………………Jerry Levine X

Industrial Hygiene………………………………………………... Bill Slavin X

Health Physics…………………

RLM ………………………………………………………………..Larry Dudek

| TRAINING (designated by RLM) |
| --- |
| No training required ______________ | Instructor Jim Chrzanowski |
| Personnel (group, job title or individual name) | Read Only | Instruction Pre-job Briefing | Hands On |
| Lead Tech. |  | X |  |
| Technicians performing task |  | X |  |
| Field Supervisors |  | X |  |
| Quality Control Representative |  | X |  |
| Training Rep. |
| RLM Larry Dudek |

RECORD OF CHANGE

| Revision | Date | Description of Change |
| --- | --- | --- |
| 00 |  | Initial release |
| 01 | 5/25/06 | Revamped entire procedure to reflect changes in manufacturing sequence -Added new figures throughout procedure -Added finalization of diagnostic flux loops -Added joint resistance test section of connectors -Modified table and clarified description of assemblies for cooling tube tests -Added more detail of turning fixture installation -Added more detail for final clamp installations -Removal of prosthetic filler -Added removal of studs and bag mold details |

TABLE OF CONTENTS

1	Scope	1

1.1	Introduction	1

1.2	Scope	1

1.3	Identification of winding form being prepared:	1

2	Applicable Documents	1

2.1	NCSX-MIT/QA-142-01:	1

2.2	NCSX-PLAN-MFOP-00:	1

2.3	D-NCSX-MCF-005 Dimensional Control & Metrology for the NCSX MC	1

2.4	D-NCSX-PLAN-MCWDC     Modular Coil Dimensional Control Plan	1

2.5	D-L-NCSX-984 Lifting Modular Coil Assemblies	2

2.6	D-L-NCSX-996 Lifting Finished Modular Coil Assemblies	2

3	Safety Requirements:	2

3.1	Job Hazard Analysis:	2

4	Prerequisites & Conditions:	2

4.1	Pre-Job Briefing:	2

4.2	Daily Operations Startup and Shutdown:	2

4.3	Reference Torque Values:	2

5	Materials and Parts for this station	2

6	Fabrication Process	3

6.1	Daily Startup Activities:	3

6.2	Daily Shutdown Activities:	3

6.3	Install MC or TRC in Turning Fixture:	3

6.4	Clamp Removal	5

6.5	Stud Removal	5

6.6	Prosthetic Filler Removal [Type A and B coils only]	6

6.7	Bag Removal	7

6.8	Coil Inspection:	7

6.9	Insulation of cooling tubes:	8

6.10	Cooling Tube Pressure Tests	8

6.11	Flow Check:	9

6.12	Cooling Tube Electrical Test:	9

6.13	Dimensional Inspection-            DELETE	10

6.14	Coil Clamp Installation	10

6.15	Finalization of Diagnostic Loops	14

6.16	Installation of cooling jumper around poloidal break	15

6.17	Cooling Tube Pressure Tests:	15

6.18	Modular Coil Electrical Joints:	17

6.19	Final Electrical Testing of Coil [Room Temperature]	18

6.20	Name Tag Installation:	20

6.21	Strain Gages and Thermocouples [Optional at this point]	21

6.22	Transporting MCWF from Casting Prep Station 1b to Station 1a:	23

6.23	Disassembly of coil/casting from Support Ring Assembly:	23

7	Completion of Activities at Post VPI Station:	24

7.1	Document Verification:	24

7.2	Field Package:	25

7.3	Approval:	25

7.4	Post-job Briefing:	25

List of Figures

Figure 1- Upper Support Plates	4

Figure 2- Turning Fixture	5

Figure 3 - Cooling Tube Sleeving Insulation	8

Figure 4- Chill Plate Cooling Assembly ID	9

Figure 5- G-11 Pad Location	10

Figure 6- Coil Clamp Assembly	11

Figure 7- Torque Reference Locations	12

Figure 8- Typical Spring Washer Stack Up	12

Figure 9-Typical Winding Clamp Arrangement	12

Figure 10- Chill Plate Assembly Identification	16

Figure 11-Electrical Joint Test Setup	16

Figure 12- Final Terminal Connections Identification	18

Figure 13-Megger Test Results	19

Figure 14- Modular Coil Name Tag [example]	21

Figure 15- Coil Sensor Table	22

Figure 16- Casting Assy. Fixture- Vertical Position	24

Figure 17- Casting Assy. Fixture in Horizontal Position	24

Figure 18- Assy. Fixture without Lift/Support Beam	24

Figure 19- Coil without Support Ring	24

Figure 20-Sensor Locations for Type C Casting	26

Figure 21- Sensor Locations for Type B Casting	27

Figure 22-Sensor Location for Type A Casting	28

List of Tables

Table 1- Tube Inspection Results	10

Table 2- Coil Clamp Torque Data	13

Table 3- Cooling Tube Pressure Test Results	15

Table 4- Joint Resistance	17

Table 5- Coil Resistance	20

# Scope

## Introduction

The NCSX Coil Manufacturing Facility is divided into 5 workstations.  Each workstation has a specific set of tasks that will be performed as part of the overall fabrication process.  This procedure addresses the manufacturing, inspection, test and QC inspection points for a specific workstation required to manufacture the modular coils.

- Station No. 1…	Winding Form Preparation & Post VPI Activities

- Station No. 2…	Winding Station / Molding and VPI Preparation

- Station No. 4…	Winding Station C/ Molding and VPI Preparation

- Station No. 5…	VPI and Autoclave Activities

- Station No. 7…	DELETE

## Scope

This procedure identifies the post VPI activities for each Modular Coil (MC) or Twisted Racetrack Coil (TRC).   It includes:

- Installing the MC into the turning fixture

- Cleanup of the coil following VPI

- Preparation of coil for final coil clamps

- Installation of the coil clamps

- Room temperature electrical testing of coil

- Disassembly of coil/winding form from support ring

- Transport of coil to the basement coil test facility [may not be applicable]

## Identification of winding form being prepared:

Station Number: ________ (Location where work will be performed)

Winding Form Type:  _______________ [Type A, B, C or Twisted Racetrack Coil (TRC)]

MC Winding Form ID No: _________________

DELETE:  Modular Coil Identification Number

# Applicable Documents

## NCSX-MIT/QA-142-01:

All applicable documents associated with this procedure, are identified in the MIT/QA Plan, document number NCSX-MIT/QA-142-01.

## NCSX-PLAN-MFOP-00:

All Modular Coil work processes are governed by the “Manufacturing Facility Operations Plan”, document number NCSX-PLAN-MFOP-00.

## D-NCSX-MCF-005	Dimensional Control & Metrology for the NCSX MC

## D-NCSX-PLAN-MCWDC     Modular Coil Dimensional Control Plan

## D-L-NCSX-984	Lifting Modular Coil Assemblies

## D-L-NCSX-996	Lifting Finished Modular Coil Assemblies

# Safety Requirements:

All work will be performed in a safe manner in accordance with PPPL safety policies ES&H 5008 and “Integrated Safety Management” (ISM) policy.

## Job Hazard Analysis:

JHA’s will be generated for each workstation, identifying existing or potential workplace hazards and to evaluate the risk of worker injury or illness associated with job tasks. (Reference document ESH-004 “Job Hazard Analysis”)  The IH representative will review the JHA’s for accuracy as well as completeness.  It will be reviewed with all activity participants at the Pre-Job briefings.

# Prerequisites & Conditions:

## Pre-Job Briefing:

A pre-job briefing will be held prior to the first time that revision of the procedure is used or if being performed by a new crew.  The briefing will describe the processes and safety issues [JHA] associated with procedure.   Attendance shall be documented via training sign-in sheet.

Pre job Briefing complete: _______________________________ _________________

MC Field Supervisor                           Date

## Daily Operations Startup and Shutdown:

Each working day, it is required to complete and initial the daily operations startup log to ensure that the station is ready to commence work activities for the day.  The signoff log is located in the Daily Station Log.  See section 6.1 and 6.2 for details.

## Reference Torque Values:

Unless a torque value is specified or the fastening material is something other than low carbon steel, the following values shall be used whenever the procedure requires a torquing operation:

3/8-16UNC ……	18 ft-lbs		3/8-24UNF ……	19 ft-lbs 	½-13 UNC ……	38 ft-lbs		½ -20 UNF ……	40 ft-lbs		5/8-11 UNC….	83 ft-lbs		5/8-18 UNF…	95 ft-lbs

¾-10 UNC..……	105 ft-lbs	¾-16 UNF …….	102 ft-lbs	1-8 UNC …       236 ft-lbs	1-14 UNF ……..	212 ft-lbs	1 1/4 UNC ……	432 ft-lbs	1 ½-6 UNC …...732 ft-lbs

# Materials and Parts for this station

The following materials and/or equipment will be used with this procedure.  MSDS’s for chemicals will be located in a notebook in the winding facility.

| General Description | Material | Reference Document/Product No. |
| --- | --- | --- |
| Solvent | Acetone | MSDS# 00561 |
| Short Coil Clamp Assembly | 316L stainless steel | SE1405-257P |
| Name tag | Aluminum |  |
| MC Turning Fixture | Equipment | Drawing no. SE144-008 |
| Rolled Ring Assembly | Fixture | Drawing no. SE144-007 |
| Casting to Ring Assy. Fixture | Fixture | Drawing no. SE144-050 |
| Multi-Meter | Equipment |  |
| Megger Electrical Tester | Equipment |  |
| Mobile Cryo-test Facility Transport Cart | Equipment |  |
| Swagelock fittings | copper |  |
| Teflon tubing for electrical breaks | Teflon |  |
| Strain gage adhesive | M-Bond | AE-10 |
| Modular coil stands | Steel | SE144-031 |

# Fabrication Process

This fabrication procedure is to be used as guide to complete Post VPI activities.   Deviation from this procedure for processes that DOES NOT effect the design of the coil can be made with the concurrence of the MC Field Supervisor.  These deviations shall be documented in the procedure and initialed by the MC Field Supervisor prior to implementing the deviations.  Deviations that may effect the design of the coil requires a Request for Deviation “RFD” approval.  The RFD must be approved prior to proceeding.  Procedure changes need to be incorporated into the document via “Minor Procedure Changes” or “Revisions”.

## Daily Startup Activities:

### Check all daily supplies needed:

### Verify operation of all equipment needed that day.

### Check station for cleanliness

### Check that safety guards are intact

### Check that safety equipment needed for day’s activities are available

### Check that the day’s travelers and procedures are in their document holder.

### Once completed, date and initial daily log at the back of the Station Log Book.

## Daily Shutdown Activities:

### Turn off power to equipment not in use.

### Clean entire workstation area.

### Verify that all Traveler and data sheet information is complete.

### The Lead Technician shall verify that the Station’s Log Book has been completed and signed for the day.

### Once completed, date and initial daily log at the back of the Station Log Book.

## Install MC or TRC in Turning Fixture:

Using the steps outlined in procedure D-NCSX-MCF-003 [VPI] prepare the VPI’d coil for transfer from the autoclave.

Note:  Station 1b may not be available to receive a coil from station 5.  If not, transfer the coil to station 1a and lower/store coil until station 1b is available.

### Station 1b Preparations:

Activities associated with receiving modular coil at winding stations.

  - Prior to installing the MCWF compress the springs under the gear box (drive system) until they are bottomed.

  - Measure the inside width of the winding form ring (where the roller guide wheels engage) and record the smallest value.  		 [Narrowest dimension].

  - Adjust the lower wheels on the winding station so that they are centered in the frame AND are set at a width that is one-half inch greater than the value recorded in the previous step.

  - Lower the MCWF and ring assembly into the turning fixture using the corner brackets for alignment.  Bolt up one end loosely (use spud wrenches to align holes).

- SAFETY NOTE:  Use scaffolding or appropriate ladders while working on upper section of turning fixture.  Scaffolding must be inspected prior to use per Section 9 Chapter 5 in PPPL ES&H Manual.

  - Install the upper guide rollers and align all of the guide rollers to the support ring.  NOTE: Sling the rollers and raise them into position with rope.  Do not climb up ladder with roller assembly in hand.

  - Decompress springs under the gear box (drive unit) until gear is fully engaged with ring gear rack.  The upper set of springs MUST be completely disengaged.  This must be verified prior to proceeding.

Verified by: _________________________ Date: __________________

Lead Technician

- Verify that the upper support/lift beam is in proper position and secured with appropriate hardware that is torqued to the proper value. [See section 4.3]

Verified by: _________________________ Date: __________________

Lead Technician

- Remove the upper support plates between the support-ring and lift beam.  This operation must be verified prior to operating turning fixture. [See Error! Reference source not found.]

Verified by: _________________________ Date: __________________

Lead Technician

Figure 1- Upper Support Plates

  - Adjust the upper alignment rollers (both on the vertical and horizontal beams) so that the ring is aligned vertically and is centered within the turning fixture frame.  A pry bar can be used to position the upper half of the ring so that these adjustments can be made.  The rollers should be set so that there is one-quarter inch clearance to the ring flanges.

  - To ensure proper alignment and operation of the turning fixture, rotate the MCWF a full two revolution in either direction, using the foot-pedal control.  Re-adjust the alignment rollers as required.   Alignment of MCWF to the turning fixture is complete.

Verified by: _________________________ Date: __________________

Lead Technician

Figure 2- Turning Fixture

## Clamp Removal

### Remove the winding clamp side bars, but leave the top tee in position, clamped to the coil bundle.  All hardware and components including the shim washers shall be saved for the next coil.

## Stud Removal

### Mark studs that should be removed from coil per appropriate drawing.  Carefully remove the winding clamp studs using the stud removal tool.  This will break the stud from the winding form leaving the stud base.

### Measure the magnetic permeability of the remaining stud base using a calibrated Severn permeability indicator to verify that the relative magnetic permeability is below the acceptance criteria If the permeability exceeds the acceptance criteria the stud base must be removed by grinding.

Acceptance Criteria:  <1.02

### Safety notes:  Prior to grinding:

#### Ensure that the coil is protected.  Areas that are not protected by the epoxy/glass shell must be covered prior to start of grinding

  - Eye protection is required during grinding

  - Notify the ESU and obtain a flame permit prior to starting grinding operations.

Verified by: _________________________ Date: __________________

Lead Technician

### All studs may not have to be removed.  This decision will be made by NCSX management and the field supervisor.

Location of studs that can remain:

Confirmed by:

Field Supervisor: ______________________________________ Date: _____________

### Removal of the studs has been completed.

Verified by: _________________________ Date: __________________

Lead Technician

Quality Control Representative: __________________________ Date: _____________

## Prosthetic Filler Removal [Type A and B coils only]

Remove the stainless steel prosthetic filler pieces.

### Carefully remove the stainless steel prosthetic filler by grinding away the tack welds.  Extreme care shall be taken to ensure that no harm comes to the coil during the removal of the prosthetic filler.

### DO NOT damage the prosthetic filler during removal since it will be used for multiple coils.

### Measure the magnetic permeability of the tack weld areas using a calibrated Severn permeability indicator to verify that the relative magnetic permeability is below the acceptance criteria If the permeability exceeds the acceptance criteria additional grinding will be necessary.

Acceptance Criteria:  <1.02

Verified by: _________________________ Date: __________________

Lead Technician

Quality Control Representative: __________________________ Date: _____________

## Bag Removal

### Carefully remove the epoxy/glass structure from the coil bundle.

### Caution note: Extreme care shall be taken around the cooling tubes.  Do not use sharp instruments or tools near these tubes without tube protection.

### Safety note:  Use leather gloves during this process, since the epoxy/glass structure has sharp edges.  Safety glasses are required for this operation.

### During the shell/bag removal, do not remove G-11 sprue rings that are attached to the chill plates. See Figure 5- G-11 Pad Location

### Once the epoxy/glass shell structure has been removed, carefully remove the rubber bag mold that surrounds the coil bundles.  This may require some scraping with putty knives.  See caution note in 6.7.2.

### The epoxy/glass structural shell and bag mold have been removed and the coil is ready for final inspection.

Verified by: _________________________ Date: __________________

Lead Technician

## Coil Inspection:

### Carefully inspect boundary of winding packs and winding form for any evidence of epoxy cracks, gaps between winding and winding form, or other relative motion.

### Inspect VPI boundary for leaks, “ballooning” or other defects that could affect coil performance or geometry.

Inspection Findings:

Findings verified by: ____________________________ Date: ____________________

Field Supervisor

## Insulation of cooling tubes:

### Apply heat shrink Teflon tubing over the cooling tubes from the point where the tubes exit the chill plates through the clearance holes in the winding forms. [Figure 3 - Cooling Tube Sleeving Insulation]

Figure 3 - Cooling Tube Sleeving Insulation

### Installation of electrical sleeving is complete.

Cooling Tube insulation is completed and verified by:

Lead Technician: ____________________________ Date: ____________________

Quality Control: _____________________________ Date: ____________________

## Cooling Tube Pressure Tests

Perform a final pressure test to verify the integrity of the cooling tubes.

### Place compression fittings on each end of the coolant tubes.

### Using engineering procedure ENG-014 (Guidelines for Hydrostatic and Pneumatic Testing) test the individual cooling tubes.

### Pressurize the coolant tubes with helium to 200 psi and isolate from the pressure source.

### All safety precautions including the use of PPE’s shall be followed as outlined in the Job Hazard Analysis sheet and recommendations made by the PPPL Industrial Hygienist.

### Gauges shall have a minimum 5-psi graduation.

Verified by: _________________________________ Date: __________________

Quality Control Representative

### Acceptance criteria: The test pressure shall be maintained without any detectable drop in pressure within the resolution of the gauge for at least ten minutes from the time the system was isolated from the pressure source, during which time there shall be no change in the pressure reading on the calibrated pressure gauge.

### Record test data in the table below [Error! Reference source not found.]

## Flow Check:

Flow nitrogen or air through each flow package to verify that there are no blockages.

### Record test data in the table below [Error! Reference source not found.]

## Cooling Tube Electrical Test:

### Verify that cooling tubes are not grounded and electrically isolated to modular coil winding form using a multi-meter.  Document findings in Error! Reference source not found.

Equipment Name & ID Number: ___________________ Calibration Date: ___________

Figure 4- Chill Plate Cooling Assembly ID

Table 1- Tube Inspection Results

| Tube designation | Flow Path Blockage check | Pressure Leak check | Electrical test, tube to ground |
| --- | --- | --- | --- |
| Side A Zone 1 Inner |  |  |  |
| Side A Zone 1 Outer |  |  |  |
| Side A Zone 2 Inner |  |  |  |
| Side A Zone 2 Outer |  |  |  |
| Side A Zone 3 Inner |  |  |  |
| Side A Zone 3 Outer |  |  |  |
| Side B Zone 1 Inner |  |  |  |
| Side B Zone 1 Outer |  |  |  |
| Side B Zone 2 Inner |  |  |  |
| Side B Zone 2 Outer |  |  |  |
| Side B Zone 3 Inner |  |  |  |
| Side B Zone 3 Outer |  |  |  |

Cooling Tube inspections/tests are completed and verified by:

Lead Technician: ____________________________ Date: ____________________

Field Supervisor: ____________________________ Date: ____________________

Quality Control: _____________________________ Date: ____________________

## Dimensional Inspection-            DELETE

## Coil Clamp Installation

### Begin removing the top tee clamp assemblies from the impregnated coil. Do not remove more than (10) clamps from any one location.

### Remove any excess epoxy that may be on the G-11 pads.  See Figure 5- G-11 Pad Location

Figure 5- G-11 Pad Location

### Use drawing SE142C-270 and install a final winding clamp assembly.  See Figure 6- Coil Clamp Assembly

Figure 6- Coil Clamp Assembly

### Verify good fit between clamp surfaces and G11 pad surfaces.   Adjust clamp as required for best fit.

### Secure the top horizontal bar with 3/8-16 UNC socket head cap screw.  Torque bolt to 13 ft-lbs.  Location no. 4 in Figure 7- Torque Reference Locations

### Each clamp will provide 125 lbs of pre-load.  This is accomplished by hand tightening the pusher screw until it is in full contact with the G-11 coil pad.  Then turn the screw an additional 1/4 turn. [Locations # 1, 2, 3 and 5]  See                       Figure 7- Torque Reference Locations for identification numbers of joints.  Record all torque verifications in Table 2- Coil Clamp Torque Data

### Once all of the final coils clamps have been torqued, the temporary bolts at locations 1, 2, 3 and 5 shall be removed and replaced with set screws.  The hardware shall be wire-locked together to ensure that the bolts will not loosen during operation.

Figure 7- Torque Reference Locations

Figure 8- Typical Spring Washer Stack Up

Figure 9-Typical Winding Clamp Arrangement

Table 2- Coil Clamp Torque Data

| Torque verified | Torque #1 | Torque #2 | Torque #3 | Torque #4 | Torque #5 |
| --- | --- | --- | --- | --- | --- |
| Clamp No. |  |  |  |  |  |
| 1 |  |  |  |  |  |
| 2 |  |  |  |  |  |
| 3 |  |  |  |  |  |
| 4 |  |  |  |  |  |
| 5 |  |  |  |  |  |
| 6 |  |  |  |  |  |
| 7 |  |  |  |  |  |
| 8 |  |  |  |  |  |
| 9 |  |  |  |  |  |
| 10 |  |  |  |  |  |
| 11 |  |  |  |  |  |
| 12 |  |  |  |  |  |
| 13 |  |  |  |  |  |
| 14 |  |  |  |  |  |
| 15 |  |  |  |  |  |
| 16 |  |  |  |  |  |
| 17 |  |  |  |  |  |
| 18 |  |  |  |  |  |
| 19 |  |  |  |  |  |
| 20 |  |  |  |  |  |
| 21 |  |  |  |  |  |
| 22 |  |  |  |  |  |
| 23 |  |  |  |  |  |
| 24 |  |  |  |  |  |
| 25 |  |  |  |  |  |
| 26 |  |  |  |  |  |
| 27 |  |  |  |  |  |
| 28 |  |  |  |  |  |
| 29 |  |  |  |  |  |
| 30 |  |  |  |  |  |
| 31 |  |  |  |  |  |
| 32 |  |  |  |  |  |
| 33 |  |  |  |  |  |
| 34 |  |  |  |  |  |
| 35 |  |  |  |  |  |
| 36 |  |  |  |  |  |
| 37 |  |  |  |  |  |
| 38 |  |  |  |  |  |
| 39 |  |  |  |  |  |
| 40 |  |  |  |  |  |
| 41 |  |  |  |  |  |
| 42 |  |  |  |  |  |
| 43 |  |  |  |  |  |
| 44 |  |  |  |  |  |
| 45 |  |  |  |  |  |
| 46 |  |  |  |  |  |
| 47 |  |  |  |  |  |
| 48 |  |  |  |  |  |
| 49 |  |  |  |  |  |
| 50 |  |  |  |  |  |

### All of the clamp hardware has been torqued and secured.

Verified By:

Lead Technician: ____________________________ Date: ____________________

Field Supervisor: ____________________________ Date: ____________________

Quality Control: _____________________________ Date: ____________________

## Finalization of Diagnostic Loops

### The routing of the diagnostic flux loops needs to be completed.  Actual position will be determined by NCSX drawings and the Diagnostic representative.

### Notify the Diagnostic representative that the final routing of the flux loops is ready to begin.

Verified by: _________________________ Date: __________________

Lead Technician

### Position the diagnostic boxes on the outside of the winding form per direction of the Diagnostic representative.  Using the stud gun, weld inconel studs to the winding form to secure the boxes in position.

- Notify the ESU and obtain a flame permit daily prior to starting welding operation.

Verified by Lead Technician

Stud Weld Date: _______________ Obtain Flame Permit: ______________

Stud Weld Operator: ______________________________ Fire Watch: _____________

### Carefully route the twisted flux loops (2 inch pitch) per direction of Diagnostic representative from the G-11 lead blocks through the cooling tube clearance holes in the winding form and into the previously installed diagnostic boxes.  Initially secure the flux loops in place with adhesive tape.  Then tack-weld stainless clips to the winding form.

- Notify the ESU and obtain a flame permit daily prior to starting welding operation.

### Route the Flux loop leads through the lead area and exit the coil in a groove in the upper G-11 lead blocks.

Finalization of Flux Loops complete-Verified:

Lead Technician: ____________________________ Date: ____________________

Diagnostic Representative: ____________________________ Date: ____________________

## Installation of cooling jumper around poloidal break

### Prepare Teflon jumper tubes for installation; to jumper the poloidal break areas.

### Install the Teflon jumper tubes and tighten connections on all outboard circuits

## Cooling Tube Pressure Tests:

Re-leak test the chill plate cooling tubes using helium or nitrogen to verify the integrity of the cooling tubes.

### Place compression fittings on each end of the coolant tubes.

### Using engineering procedure ENG-014 (Guidelines for Hydrostatic and Pneumatic Testing) test the individual cooling tubes.

### Pressurize the coolant tubes with helium to 200 psi and isolate from the pressure source.

### All safety precautions including the use of PPE’s shall be followed as outlined in the Job Hazard Analysis sheet and recommendations made by the PPPL Industrial Hygienist.

### Gauges shall have a minimum 5-psi graduation.

Verified by: _________________________________ Date: __________________

Quality Control Representative

### Acceptance criteria: The test pressure shall be maintained without any detectable drop in pressure within the resolution of the gauge for at least ten minutes from the time the system was isolated from the pressure source, during which time there shall be no change in the pressure reading on the calibrated pressure gauge.

### Record test data in the table below [Table 3- Cooling Tube Pressure Test Results].  See Figure 10- Chill Plate Assembly Identification for identification of chill plate assemblies.

Table 3- Cooling Tube Pressure Test Results

| Tube designation | Pressure Leak check | Tube designation | Pressure Leak check |
| --- | --- | --- | --- |
| Side A Zone 1 Inner |  | Side B Zone 1 Inner |  |
| Side A Zone 1 Outer |  | Side B Zone 1 Outer |  |
| Side A Zone 2 Inner |  | Side B Zone 2 Inner |  |
| Side A Zone 2 Outer |  | Side B Zone 2 Outer |  |
| Side A Zone 3 Inner |  | Side B Zone 3 Inner |  |
| Side A Zone 3 Outer |  | Side B Zone 3 Outer |  |

Cooling Tube pressure tests are completed and verified by:

Lead Technician: ____________________________ Date: ____________________

Quality Control: ____________________________ Date: ____________________

Figure 10- Chill Plate Assembly Identification

Figure 11-Electrical Joint Test Setup

## Modular Coil Electrical Joints:

### Measure the joint resistance between the connector and the terminal blocks [points A and B].  See Figure 11-Electrical Joint Test Setup     [Acceptance criterion is < 1 micro-ohms.]

### Verify the torque value of the joint nuts. Torque to 15 ft-lbs

### Record the joint resistance and torque verification in Table 4- Joint Resistance below.

Table 4- Joint Resistance

| Joint ID | Joint Resistance [(-ohms] | Torque Verify 15 ft-lb | Wire Tie Nuts | Joint ID | Joint Resistance [(-ohms] | Torque Verify 15 ft-lb | Wire Tie Nuts |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A-1 |  |  |  | B-1 |  |  |  |
| A-2 |  |  |  | B-2 |  |  |  |
| A-3 |  |  |  | B-3 |  |  |  |
| A-4 |  |  |  | B-4 |  |  |  |
| A-5 |  |  |  | B-5 |  |  |  |
| A-6 |  |  |  | B-6 |  |  |  |
| A-7 |  |  |  | B-7 |  |  |  |
| A-8 |  |  |  | B-8 |  |  |  |

### Wire-lock each of the nuts to ensure that during operation they do not loosen.  Record verification that joints have been wire tied.

Verified by: _________________________ Date: __________________

Lead Technician

Figure 12- Final Terminal Connections Identification

## Final Electrical Testing of Coil [Room Temperature]

This series of electrical tests will be performed at room temperature to verify the integrity of the coil insulation prior to transporting to the field period assembly area.

### Test Director:

Test Director for this test series is: _______________________

### Safety Requirements & Conditions

#### The following safety requirements and prerequisites shall be used for performing tests on the Modular Coils.

#### All personnel performing these tests shall be familiar with the hazards and work procedure to minimize accidents that may occur.

#### A “Safety Watch” shall be appointed by the Test Director.  The Test Director shall clearly describe to the Safety Watch his/her responsibilities.

#### Name of Safety Watch: ______________________

Responsibilities have been clearly discussed with Safety Watch:

Verified: ________________________________ Date: ________________

Test Director

#### Responsibilities of a Safety Watch include as a minimum:

##### a)	Monitoring the operations in an attempt to prevent careless or unsafe activities.

##### b)	Shutting down the power in case of an accident.

##### c)	Contacting ESU in case of accident

##### d)	Additional responsibilities of a Safety Watch can be found in the ES&H Manual Section 2, Chapter 2.2.6.

#### During the test, the “Test Area” shall be roped-off and suitable “danger high voltage” signs and flashing lights displayed.

Test Area has been safed:

Verified by: _________________________ Date: __________________

Test Director

#### The test operator shall stand on an electrical safety mat during the test operation.

#### Approved rubber electrical safety gloves shall be worn by test members during grounding operations which occur once the test has been completed, and the test equipment turned off.

#### Upon completion of test and before the components are declared safe to touch, (dielectric joint) being tested shall be properly discharged using a “Ground Hook”.  After a minimum period of 10 seconds, while the ground hook is still in place, attach a ground cable to the casting and poloidal mid-plane.  The ground hook may be removed once the ground cable is in place.

#### Electrically ground the winding form, and chill plate cooling tubes. Care must be taken not to damage the tubes with the grounding clips.

### Insulation Resistance Measurement

### Perform a Final Megger test of the completed coil prior to transporting to field period assembly area.

#### Coil Voltage level: 7500 volts

#### Acceptance criteria: Coil Insulation Resistance:  1K Meg ohms

#### Complete the steps below and perform the insulation resistance test [Megger] of pancakes “A” and “B”. Pancakes “A” and “B” are connected together at the terminal block.

#### Test director shall verify that all safety requirements and prerequisites have been performed prior to starting the test.

  - Verify that the turning fixture is well grounded to building steel.

  - Place the megger test set on a firm, stable surface.

  - Securely connect a ground cable between building steel and the test unit.

  - Connect the megger ground lead to the coil casting.

  - Connect a ground cable to the chill plates.

  - Connect the megger power lead to the coil leads.

  - Measure the insulation resistance to ground. The test results shall be in compliance with the requirements noted in Section 6.17.3.

Figure 13-Megger Test Results

| Test Voltage | Insulation Resistance Minimum 1KM | Observations |
| --- | --- | --- |
| 1000 |  |  |
| 2000 |  |  |
| 3000 |  |  |
| 2500 |  |  |
| 5000 |  |  |
| 7500 |  |  |

Equipment ID Number:__________________________	Calibration Date: _____________

Megger Results: Acceptable: _______________ Unacceptable: ____________

Test Director Signoff: _____________________________ Date: ______________

Quality Control Witness: __________________________ Date: ______________

Remarks:

### Coil Resistance Measurement

Measure the resistance of the entire modular coil at the terminal leads. [See Figure 12- Final Terminal Connections Identification]

#### Acceptance criteria: As specified in specific Modular coil design specification [A, B and C]

#### Coil Resistance: ____________________ per specification

#### The test equipment used for this test will be a “Biddle” digital low resistance ohmmeter (DLRO).

#### Equipment ID No ___________________ Calibration Date: __________________

#### Using the bridge probe, make pressure contact on the ends of the system bus being tested.

#### Record the resistance readings in Table 5- Coil Resistance.

#### Place temperature sensor on the surface of the bus leads and record the temperature of the copper after the reading stabilizes.

R20 =      254.5      x Rc

234.5 + Tc

Where: Rc = measured resistance of the conductor (milliohms)

Tc = temperature of coil when resistance measurement is made (degrees C)

Table 5- Coil Resistance

| Measured System Resistance (Rc) m( at Tc | System Resistance corrected to 20 deg. C (R20) | Calculated System Resistance @ 20 deg.C [per MC specification] |
| --- | --- | --- |
| Rc: |  |  |
| Tc: |  |  |

Resistance Results: Acceptable: _______________ Unacceptable: ____________

Test Director Signoff: _____________________________ Date: ______________

## Name Tag Installation:

Mount a permanent name plate to the outside of the winding form adjacent to the leads.  The name tag will include the name of the item and the part and serial number of the item. [E.g. NCSX Modular Coil Type C Assembly, P/N SE140-103, S/N C1.] See Figure 14- Modular Coil Name Tag [example]

Name Tag Information:

Name of Item: Modular Coil   	Coil Type:  __________ S/N: ______________

Part number [Dwg No.]: ________________________

Installation of name plate complete:

Verified by: _________________________ Date: __________________

Field Supervisor

Figure 14- Modular Coil Name Tag [example]

## Strain Gages and Thermocouples [Optional at this point]

The strain gages and thermocouples may not be installed at this time.  If that is the case the post VPI activities at station 1b are complete.  Otherwise install strain gages and thermocouples to the finished coil in the locations identified by the WBS 14 manager. This information will be added as an addendum to this procedure.

### Use the following steps to attach the strain gages.

#### Degrease and clean the surface with Isopropyl alcohol.

#### Dry abrade the gauging surface with 220 to 320 grit silicon-carbide paper to remove any scales or oxides on the base material to improve adhesion.

#### Apply M-Prep Conditioner A and wet-abrade the gage area.  Then repeat procedure by wet abrading and wiping using 400 grit silicon-carbide paper.

#### Apply liberal amount of M-Prep Neutralizer 5A to the gage area.  Remove the Neutralizer by slowly wiping through the gage area using a gauze sponge.

#### Remove the gage from its transparent envelope and place bonding side down on a chemically clean glass plate or empty gage box.  Using Kapton tape as a carrier, position the gage/tape assembly onto the specimen.  Holding the tape at a shallow angle, wipe the assembly onto the specimen surface.

#### Lift the gage end of the assembly [about a 45 º angle] until the gage and terminal are free of the specimen surface.

#### Apply a thin layer of prepared adhesive [M-Bond AE-10] to both the specimen and back of the gage.

#### Lift the end of the tape and bridge over the adhesive at approximately a 30º angle. With a piece of gauze, slowly make a single wiping stroke over the gage/tape assembly.  Use a firm pressure with your fingers when wiping over the gage.

### Using the “Romer” measuring arm, document the position of the sensors that were just installed on to the coil.

### Identify the locations of the sensors on the appropriate coil figure at the back of the procedure [Figure 20-Sensor Locations for Type C Casting Figure 21- Sensor Locations for Type B Casting; Figure 22-Sensor Location for Type A Casting]

Installation of sensors is not required at this time:

Verified by: _________________________ Date: __________________

Field Supervisor

Figure 15- Coil Sensor Table

| No. | Sensor Type* | Description |
| --- | --- | --- |
| 1 |  |  |
| 2 |  |  |
| 3 |  |  |
| 4 |  |  |
| 5 |  |  |
| 6 |  |  |
| 7 |  |  |
| 8 |  |  |
| 9 |  |  |
| 10 |  |  |
| 11 |  |  |
| 12 |  |  |

* Sensor type: Stain gauge or thermocouple

Installation of sensors is complete:

Verified by: _________________________ Date: __________________

Field Supervisor

## Transporting MCWF from Casting Prep Station 1b to Station 1a:

Using lift procedure D-L-NCSX-984 the modular coil winding form shall be transferred from the turning fixture [Figure 2- Turning Fixture] at station 1b to the casting assembly fixture at station 1a.

### Install the upper support plates that secure the support ring to the support/lift beam.  This operation must be verified prior to proceeding.  See Figure 1- Upper Support Plates

Verified by: _________________________ Date: __________________

Lead Technician

- SAFETY NOTE:  Use scaffolding or appropriate ladders while working on upper section of turning fixture.  Scaffolding must be inspected prior to use per Section 9 Chapter 5 in PPPL ES&H Manual.

### Remove the balance weights and plates on the bottom of the ring assembly.

### Using the lift procedure data sheet rig the upper support/lift beam to the overhead crane.

### Once a slight load has been taken, remove the hardware that secures the upper support/lift beam to the turning fixture frame.

### Compress the springs under the gear box (drive system) until they are bottomed.

### Disengage and remove the upper guide rollers. NOTE: Sling the rollers and raise them into position with rope.  Do not climb up ladder with roller assembly in hand.

### Carefully raise the winding form/ring assembly from station 1b and transport to stations no. 1a, directly over the casting assembly fixture.

Verified by: _________________________ Date: __________________

Field Supervisor

## Disassembly of coil/casting from Support Ring Assembly:

### Secure the coil support ring to the casting assembly fixture. Figure 16- Casting Assy. Fixture- Vertical Position

### Using the overhead crane, carefully lower the coil/support ring assembly until the coil is in the horizontal position and resting on the support stands. Figure 17- Casting Assy. Fixture in Horizontal Position

### Disassemble the support/lifting beam and support brackets between the support ring and casting.

### Lift the support ring from the assembly fixture and transport to storage area. Figure 18- Assy. Fixture without Lift/Support Beam  and                                                                    Figure 19- Coil without Support Ring

Figure 16- Casting Assy. Fixture- Vertical Position

Figure 17- Casting Assy. Fixture in Horizontal Position

Figure 18- Assy. Fixture without Lift/Support Beam

Figure 19- Coil without Support Ring

### Mount the coil stands to the completed winding form. [SE144-031]

### Using lift procedure D-L-NCSX-996 [Finished Modular Coil Lift Procedure] transfer the completed modular coil from station 1a to a location determined by the Field Supervisor.

Verified:

Lead Technician: ____________________________ Date: ____________________

Field Supervisor: ____________________________ Date: ____________________

# Completion of Activities at Post VPI Station:

## Document Verification:

Verify that all pertinent data in the procedure and data sheets have been completed.

## Field Package:

Ensure that all data sheets, photographs, QC inspection sheets, etc are included in the “Coil Field Package”.

## Approval:

Prior to releasing a modular coil , it is required that the all-responsible individuals sign the release indicating that all processes at the Post VPI station have been satisfactorily completed.  The release will include signatures from the Station Lead Technician, VPI Director and the QC representative.

All Post VPI activities have been satisfactorily completed.

Lead Technician: ____________________________ Date: ____________________

Field Supervisor: ____________________________ Date: ____________________

QC shall verify completion of documentation:

Quality Control Representative: _________________________ Date: ________

## Post-job Briefing:

Complete a post job briefing with those individuals associated with the post VPI activities to review the technical and safety aspects of the job completed.

Verified by: _________________________ Date: __________________

Field Supervisor

Figure 20-Sensor Locations for Type C Casting

Figure 21- Sensor Locations for Type B Casting

Figure 22-Sensor Location for Type A Casting

y

# Text boxes

Inner Cladding Assembly

ZONE 2

A-3

A-2

ZONE 1

N/A

8

A

Coil Resistance measured across terminal leads

ZONE 3

ZONE 1

Remove Upper Support Plates

Turning Fixture Support Frame

Turning Fixture Support Roller Guide Rollers

Turning Fixture Drive System

B

Location No. 1

Turning Fixture-Upper Support/Lifting Beam

Turning Fixture Support Plates

Turning Fixture Support Ring

Location No. 4

Location No. 5

Location No. 3

Secure support ring to assy. fixture

ZONE 2

7.5 kV

SE141-103

6050 lbs

May 31, 2006

NCSX Modular Coil Type C Assy

G-11 Pad Locations

A-7

B-6

B-5

N/A

A-8

B-4

B-1

B-3

B-2

Inner Cladding Assembly

A-1

A-5

Belleville Washers

Side B

N/A

C1

N/A

B-7

B-8

Heat-shrink sleeving [typ] from chill plates through winding form

Location No. 2

SS Nut

G-11Sprue Ring

Side A

A-6

A-4

Flat Washer

Outer Cladding Assembly

Outer Cladding Assembly

ZONE 3