# Text boxes

Material Receipt

# Station No.6

Coil Testing

# Station No.5

VPI/Autoclave Station

# Station No.4

Molding/VPI Preparation

# Station No.3

Winding Station B

# Station No.2

Winding Station A

Procedure No.        NCSX-PROC-MCF-002

Winding Facility Activities

Basement Activities

- Coil Testing Activities

  - Cold test the modular coil

  - Store tested MC

- VPI/Autoclave Activities

  - Install coil in autoclave and prep for VPI

  - Vacuum impregnate coil

  - Cleanup and install final coil clamps

  - Transport coil to test facility

- Molding & VPI Preparation

  - Install outer Diagnostics & measure

  - Install Outer Chill plates

  - Install bag mold

  - Vacuum leak check bag mold

  - Install coil molding clamps

- Winding Operations

  - Install inner ground wrap insulation

  - Position leads for side “A” winding

  - Wind side “A” of modular coil

  - Measure turns as wound

  - Complete leads for side “A” winding

  - Coil Measurements/electrical tests

  - Reposition coil in turning fixture

  - Position leads for side “B” winding

  - Wind side “B” of coil

  - Measure turns as wound

  - Complete leads for side “B” winding

  - Complete ground wrap sides A & B

# Station No.1

Casting Preparation

- Material Receipt

  - Conductor receipt & inspection

  - Casting receipt & inspection

  - General product inspection guidelines

Procedure No.        NCSX-PROC-MCF-003

Procedure No.        NCSX-PROC-MCF-001

Procedure No.        NCSX-PROC-MCF-004

Procedure No.        NCSX-PROC-MCF-005

Procedure No.               D-NCSX-OP-G-159

- Casting Preparation

  - Mount casting to support ring

  - Measure/inspect casting surfaces

  - Install coil clamp studs

  - Clean & mold release winding surfaces

  - Install inner chill plates & measure

  - Install Diagnostics & measure