| INTERFACE CONTROL DOCUMENT TITLE AND APPROVAL PAGE (Page 1) |
| --- |
| ICD Number: ICD-131-15-0001-00-dA TF Coil Support Requirements | Primary Author: M. Kalish |
| Impacted WBS Elements: WBS-131, WBS-62 | Type of Interface: Functional/mechanical Interface |
| Description of Interface: The Coil Structures must provide support to the TF Coils in the following manner: - Inboard radial preload provided at top and bottom of wedge castings - Out of plane restraint with the ability to allow radial movement applied top and bottom. Four locations total, inboard top, outboard top, inboard bottom, and outboard bottom (ref. Pro Eng Model) - Outboard out of plane supports to provide out of plane adjustment to facilitate alignment. - Vertical restraints applied top and bottom with the ability to adjust the position and apply compression or tension to the TF Coil. Vertical restraints are to allow radial growth - Vertical location adjustable using upper and lower vertical supports - Access to be provided to allow for adjustment of preload studs - The Loads required to be reacted by the structure are defined in memo “Reaction Forces on MCWF from TF-Induced Loads Len Myatt, June 2,2005” |
| Record of Revisions Revision Number Description Date 00-dA Initial issue August 3, 2005 |
| Approvals WBS Manager: WBS Manager: Project Engineer: Project Engineer: Systems Engineering Support Manager: |