National Compact Stellarator Experiment

NCSX

DOCUMENTS & RECORDS PLAN

NCSX-PLAN-DOC

Draft I

January 14, 2003

Prepared by: _______________________________________

R. Simmons, NCSX Systems Engineering Support Manager

Concurrences:

_____________________________  	_____________________________

T Brown, NCSX Design Integration	  P. Heitzenroeder, Deputy Project

Manager				  Manager for Engineering

_____________________________  	_____________________________

B. Nelson, Stellarator Core Systems		L. Dudek, Ancillary Systems

Project Engineer					Project Engineer

_____________________________  	_____________________________

E. Perry, Assembly Operations		J. Malsbury, QA Manager

Project Engineer

Approved by:  ______________________________________

W. Reiersen, Engineering Manager

Controlled Document THIS IS AN UNCONTROLLED DOCUMENT ONCE PRINTED. Check the NCSX Engineering Web prior to use to assure that this document is current.

RECORD OF REVISIONS

| Revision | Date | Originator | Description of Change |
| --- | --- | --- | --- |
| DRAFT I | 1/13/03 | Simmons | Incorporated changes suggested during peer review of other documents. |

Table of Contents

1.0	PURPOSE	1

2.0	DEFINITIONS	1

3.0	RELATED DOCUMENTS	2

4.0	Records Retention Requirements	2

5.0	Documents and Records	3

5.1	General	3

5.2	Identification Schemes	4

5.2.1	Project Definition Agreements, Plans, and Procedures	4

5.2.2	Specifications	5

5.2.3	Drawings and Models	5

5.2.4	Other Documents	6

5.3	Document and Record Types	7

5.3.1	Project Definition Agreements	7

5.3.1.1	Acquisition Execution Plan - unique document	7

5.3.2	Project Plans and Procedures	8

5.3.2.1	Project Execution Plan (PEP) - unique document	8

5.3.2.2	Quality Assurance Plan - unique document	8

5.3.2.3	Systems Engineering Management Plan (SEMP) - unique document	8

5.3.2.4	Configuration Management Plan - unique document	9

5.3.2.5	Project Documents & Records Plan - unique document	9

5.3.2.6	Interface Control Management Plan - unique document	9

5.3.2.7	Data Management Plan - unique document	10

5.3.2.8	Test and Evaluation Plan - unique document	10

5.3.2.9	Mission, Experimental Plan, and Preparations - unique document	10

5.3.2.10	NCSX Procedures	11

5.3.3	Requirements Documents	11

5.3.4.1	General Requirements Document (ASPEC) - unique document	11

5.3.4.2	Development Specifications (BSPEC) - many documents	12

5.3.4.3	Product Specifications (CSPEC)- many documents	13

5.3.4.4	Process Specifications (DSPEC) - many documents	14

5.3.4.5	Material Specifications (ESPEC) - many documents	14

5.3.4	Design Support Documentation	14

5.3.4.1	Design Drawings and Models – many documents	14

5.3.4.2	Interface Control Documents – many documents	15

5.3.4.3	Calculations and Analyses – many documents	15

5.3.4.4	Design Memoranda - many documents	15

5.3.4.5	Design Review Records – many documents	16

5.3.4.6	Engineering Change Proposals – many documents	16

5.3.5	NEPA Documentation	16

5.3.6.1	Environmental Assessment (EA) – unique document	16

5.3.6.2	NEPA Planning Form – many documents	17

5.3.6.3	Safety Assessment Document – unique document	17

5.3.6	Quality Assurance Records	17

5.3.6.1	Quality Assurance Records - many documents	17

5.3.7	Training Records	18

5.3.7.1	Training Records - many documents	18

5.3.8	Procurement Deliverables	18

5.3.8.1	Procurement Deliverables - many documents	18

5.3.8.2	Statements of Work – many documents	18

5.3.9	Other Documents	19

5.3.9.1	Memoranda - many documents	19

5.3.9.2	WBS Dictionary – unique document	19

5.3.9.3	Cost and Schedule Documents – many documents	19

# PURPOSE

This document defines the official documents and records for the design, fabrication, and construction stages of the NCSX Project, including commissioning prior to first plasma. This document defines the purpose, content, format, approval level, records retention requirements, and file/document naming convention for each document and record. This document meets the requirements of PPPL Policy P-050, Quality Documents and Records, and GEN-023, Records Management.

Provisions for the retention, protection, preservation, revision, traceability, accountability, and retrievability of these documents and records are described in the NCSX Data Management Plan (NCSX-PLAN-DMP) and the NCSX Configuration Management Plan (NCSX-PLAN-CMP).

# DEFINITIONS

| Document | Recorded information that describes, specifies, reports, certifies, requires, or provides information, data or results. A document is not a record until it meets the definition of record. |
| --- | --- |
| Calculations | Results obtained from mathematical processes used in design, operation, etc. |
| Guides | A document that provides additional information to NCSX project staff. Examples might be users' guides or documents that describe possible techniques for analysis. |
| Procedure | A document that provides an orderly, detailed method of accomplishing tasks within the applicable Laboratory and NCSX guidelines and with established responsibilities and actions. |
| Record | A completed document or other media that provides objective evidence of an item, service, or process. |
| Standard | A document that defines the minimum quality and performance outcome of a process. |

# RELATED DOCUMENTS

This DOC draws on the documents listed below.  Documents referenced are the latest issues of the:

- NCSX Project Execution Plan (NCSX-PLAN-PEP)

- NCSX Systems Engineering Management Plan (NCSX-PLAN-SEMP)

- NCSX Quality Assurance Plan (NCSX-PLAN-QAP)

- NCSX Configuration Management Plan (NCSX-PLAN-CMP)

- NCSX Data Management Plan (NCSX-PLAN-DMP)

- PPPL Pro/INTRALINK Users Guide (ES-DRFT-002)

- PPPL Policy 050, “Quality Documents and Records”

- PPPL General Procedure 023, “Records Management”

# Records Retention Requirements

The contract between Princeton University and the Department of Energy requires that a records management and retention program be established and implemented at PPPL that meets the requirements of DOE O 200.1.  Procedure GEN-023 provides the overall laboratory plan for complying with this requirement.  The purpose of this section is to identify key NCSX documents and how they fit into the overall scheme. This section focuses on documentation relevant to the design and documentation of NCSX. Documentation associated with other stages, such as operations or decommissioning and dismantlement will be identified in later versions.

The design and requirements documents and records that define and substantiate the design, fabrication, modification, and operation of the NCSX device or define and document the management approaches and procedures that govern how the Project is managed, typically include the following:

Project Definition Agreements

Project Plans and Procedures

Project Requirement Documents

Design Support Documentation

NEPA Documentation

Quality Assurance Records

Training Records

Procurement Records

Other Documents

| Type of Record | NCSX Record Key | DOE Record Type (GEN-023) | Retention Requirement (GEN-023) |
| --- | --- | --- | --- |
| Initial planning documents | DC1 | 14 | Until project completion |
| NEPA documentation and other permits | DC2 | O | 10 years – need DOE approval to dispose of |
| Other technical information and/or data prepared for outside (of DOE) agencies | DC3 | O | 10 years – need DOE approval to dispose of |
| Design requirements documents | DC4 | A16 | Cut off at end of each FY. Destroy after 10 years |
| Project design documentation records | DC5 | 14 | Until dismantlement or disposal |
| Project management records | DC6 | 16 | 1 year after project completed |
| Miscellaneous records supporting, but not required for project record purposes | DC7 | 14 | Until project completion or superceded |

Crosscutting this documentation organization are the DOE guidelines and PPPL Procedure GEN-023, which defines retention requirements by DOE record type.  Table 4-1 below provides the document retention requirements by type of record:

Table 4-1

Document Retention Requirements

# Documents and Records

## General

A list of official documents and records is provided in this section.  This list represents an initial definition of those documents currently envisioned during the conceptual design and initial part of the preliminary design phases.  Other documents will be defined and added as the project progresses.

For each document or record, the following is given:

- Purpose - This gives the purpose of the document. If relevant, this also defines the circumstances under which the document may serve as an official NCSX record.

- Preparation and Approval  - This defines the individuals responsible for preparing and approving the specified document. The individual with approval authority is also responsible for ensuring that ALL appropriate personnel have formally reviewed the document and that comments have been properly treated prior to approving the document.  The NCSX philosophy is to limit the number of approvals within the NCSX Project to as few as possible. Revisions are uniquely identified and undergo the same approval process as the original document.

- Format  - This indicates where the required format for the document is specified. Documents that are unique, i.e. only one is expected to be generated for the project, may have no specified format. The format selected should be that most appropriate to the document.

- Naming Convention - This specifies both the identifier for the document and the name of the file containing the document.

- Storage Location – either the NCSX Engineering Web page < http://www.pppl.gov/me/NCSX_Engineering/> or the Pro/INTRALINK database.  Documents posted on the Engineering Web page will be in a pdf format and drawings and models residing on the Pro/INTRALINK database will be posted as ProEngineer drawings and models if created in the ProEngineer software, in AutoCAD if created in AutoCAD, or in other Project-approved electronic drawing software programs.  Drawings released for fabrication will be stored in a special Released Drawings folder within the Pro/INTRALINK database in pdf format.

- Document Retention Classification – The document retention classification is defined for each document.  Retention requirements are specified by document retention classification in Table 4-1.

The NCSX Project will store all pertinent design and management documents electronically in accordance with processes defined in the NCSX Data management Plan (NCSX-PLAN-DMP) and the NCSX Configuration Management Plan (NCSX-PLAN-CMP) and subordinate procedures.  Project participants will have access to these documents through the Internet.

## Identification Schemes

### Project Definition Agreements, Plans, and Procedures

File names for controlled project definition agreements and plans should be the same as the document name followed by an appropriate descriptor.  This document name shall consist first of the following information, separated by hyphens (no spaces).  For example, NCSX-PLAN-YYY-ZZ where:

- NCSX indicates the NCSX Project

- PLAN indicates that this document is either a project definition agreement or plan and PROC indicates that this is a procedure.

- YYY is a three or four letter shorthand name of the project definition agreement or plan (e.g., SEMP for the Systems Engineering Management Plan, CMP for the Configuration Management Plan, DOC for the Document and Records Plan, etc.).  For a procedure, this shorthand name for the procedure is replaced by a numerical identifier for that procedure (e.g., 001, 002, etc.).

- ZZ indicates the revision level of the document (e.g. 00 for revision 0)

This naming convention is then followed by an underscore (_) and the appropriate state of approval descriptor (e.g., dA indicates Draft A of the revision level or Signed indicates a signed/approved version of the document.

### Specifications

As indicated in the Systems Engineering Management Plan (SEMP), there is a hierarchy of 5 specification levels starting at the top-level General Requirements Document (GRD).  In systems engineering terms, this is the ASPEC.  This top-level specification is then followed by a specification tree consisting of Developmental (or “design to”) specifications (BSPECs) and a series of “build to” specifications consisting of Product (CSPECs), Process (DSPECs) and Material (ESPECs).  The naming convention for specifications shall first consist of the following information, separated by hyphens (no spaces).  For example, NCSX-STYPE-WBS-###-XX where:

- NCSX indicates the NCSX Project

- STYPE indicates the level of specification (e.g., ASPEC for the GRD, BSPEC for the “design to” specification, and CSPEC, DSPEC, or ESPEC for “build to” specifications)

- WBS indicates the three digit WBS number identifier

- ### indicates the three digit numerical number of the specification (e.g., 001, 002, etc.)

- XX indicates the revision level of the document (e.g. 00 for Revision 0)

This naming convention is then followed by an underscore (_) and the appropriate state of approval descriptor (e.g., dA indicates Draft A of the revision level or Signed indicates a signed/approved version of the document.

### Drawings and Models

The Pro/INTRALINK Users Guide provides the details for numbering drawings and models.  Drawings and models are created and maintained electronically using NCSX Project approved drawing software packages.  For Mechanical and Facility drawings and models (in either 2D or 3D), the Project standard is Pro/Engineer.  For Electrical drawings and models (usually only in 2D), the Project standard is AutoCAD.  As approved by the Project on a case-by-case basis, other electronic drawing software packages may be utilized.

Since the NCSX Project is a national project involving both PPPL and ORNL, a flexible identification scheme has been developed for drawings and models that recognize the specific requirements of each laboratory, while still providing a standardized approach.  In all cases, the drawing/model numbers will take a form that follows the NCSX WBS structure.

The NCSX drawings will evolve from a concept stage through release for fabrication.  During the conceptual design phase, an additional concept identifier is added to the standardized drawing number.  For example, during conceptual design, a typical number might take the form of S17E112-001, where:

- S indicates that this is a NCSX drawing – other projects at PPPL will have other identifiers (e.g., FIRE is identified by a F, etc.)

- 17 indicates the concept number.  After leaving conceptual design, this concept number will be dropped.

- E indicates the drawing sheet size

- 112 indicates the 3 digit WBS identifier

- 001 indicates the drawing number

In addition to the basic drawing number, there are three other bits of information that clearly identify the unique drawing.  Until a drawing is released for fabrication, it will not be assigned a revision number.  However, once the drawing is approved and released for fabrication, a revision number will be assigned in the drawing title block; until that occurs, the revision block on the drawing will be blank.  However, the evolution of the drawing will tracked by the version number that appears in an ancillary design status block separate from the drawing main title block.  In addition, this ancillary design status  block will identify the stage of the design of the drawing (e.g., conceptual, preliminary, or final) so that a user might understand the level of design evolution shown on the drawing.

Sketches have a special numbering scheme.  Sketch numbers are assigned for ideas still in the early developmental stages, e.g., before a concept approach has been decided.  Preliminary sketch numbers are also assigned based on the NCSX WBS structure and will take the form of:  S_B_112-XXXXXX where:

- S indicates once again designates the NCSX Project

- B indicates the last initial of the creator of the sketch (first and second initials can also be used)

- 112 indicates the three digit WBS identifier

- XXXXXX indicates the number or an alphanumeric description of the drawing

Prototype and As-Built drawings numbers are merely a slight modification to the standardized numbering scheme.  Prototype drawing numbers will only be assigned when the prototype model is not expected to represent the final production unit.  Prototype drawings and models will have a special designation “P” placed at the end of the standard drawing number.  As-Built are only assigned when the physical model needs to be revised to reflect a physical defect or variance from plan of a single part or component (vs. the entire assembly) that is not repairable and whose non-conformance has been accepted by a NCR.  If a drawing needs to be modified to reflect this non-conformance, a new drawing will be created with the designator “AB” placed at the end of the drawing number to identify those parts revised.

### Other Documents

File names for memos, calculations, and other documents follow a standard format to facilitate filing and sorting.  The format should be as follows:  YYMMDD_Subject_XX_ZZZ.ext where:

- YYMMDD is the date of issue (e.g., 021127 indicating a date of issue of November 27, 2002

- Subject is a brief description of the topic covered in the memo, calculation, etc.=> no blanks permitted, use underscores (_) to separate text.

- XXX is the 3-digit numeric ID for the most appropriate WBS element.  If a 1-digit or 2-digit WBS element is most appropriate, then the single/two digit(s) should be followed by 0 (e.g., 10 for WBS 1, 120 for WBS 12, etc.)

- ZZZ are the author’s initials => should be at least 2 letters, but three letters are preferred.

To the extent feasible, all NCSX records other than drawings and models will be stored electronically on a secure NCSX web page.  As indicated in the NCSX Data Management Plan (DMP), drawings and models will be stored electronically in the Pro/INTRALINK database.

## Document and Record Types

### Project Definition Agreements

#### Acquisition Execution Plan - unique document

| Purpose | Describes the acquisition strategy and business plans to be used in the execution of the NCSX Project |
| --- | --- |
| Review and Approval | Prepared by: NCSX Systems Engineering Support Manager Concurrences by: NCSX Project Management, PPPL and ORNL Lab Management, DOE Federal Project Manager, DOE Manager Princeton Area Office and Contracting Officer, DOE OFES Program Manager, OFES Associate Director for Fusion Energy Sciences, Director Office of Science, and DOE Director of Office of Construction and Engineering Management (OECM) Approved by: DOE Under Secretary for Energy, Science, and Environment |
| Format | -- |
| Naming Convention | NCSX-PLAN-AEP-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC1 |

### Project Plans and Procedures

#### Project Execution Plan (PEP) - unique document

| Purpose | Describes management methodology to be applied during the design and fabrication stages of the NCSX project. |
| --- | --- |
| Review and Approval | Prepared by: NCSX System Engineering Support Manager Concurrences by: NCSX Project Control Manager, NCSX Project Engineering and Management, PPPL and ORNL Lab Management, DOE Federal Project Manager, OFES Program Manager, DOE Director Construction Support Division, DOE Manager Chicago Operations Office Approved by: DOE Associate Director of Fusion Energy Sciences |
| Format | -- |
| Naming Convention | NCSX-PLAN-PEP-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC6 |

#### Quality Assurance Plan - unique document

| Purpose | Provides matrix of PPPL quality requirements to implementing procedures |
| --- | --- |
| Review and Approval | Prepared by: NCSX QA Manager Concurrences by: PPPL ES&H/IS Department Head, NCSX Engineering Manager, NCSX Project Manager, NCSX Deputy Project Manager for Program, and PPPL Engineering Department Head Approved by: PPPL Director |
| Format | -- |
| Naming Convention | NCSX-PLAN-QAP-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC6 |

#### Systems Engineering Management Plan (SEMP) - unique document

| Purpose | Describes engineering management methodology and systems to be applied during the design and fabrication stages of the NCSX project. |
| --- | --- |
| Review and Approval | Prepared by: NCSX Engineering Manager Concurrences by: NCSX Systems Engineering Support Manager, NCSX Project Engineers, NCSX QA Manager, and NCSX Deputy Project Manager for Engineering Approved by: NCSX Project Manager |
| Format | -- |
| Naming Convention | NCSX-PLAN-SEMP-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC6 |

#### Configuration Management Plan - unique document

| Purpose | Provides a description of the processes that will be used to effect configuration management on the NCSX Project |
| --- | --- |
| Review and Approval | Prepared by: NCSX Systems Engineering Support Manager Concurrences by: NCSX Project Control Manager, NCSX Deputy Project Manager for Engineering, NCSX QA Manager, NCSX Physics Manager, NCSX Project Engineers, and NCSX Engineering Manager Approved by: NCSX Project Manager |
| Format | -- |
| Naming Convention | NCSX-PLAN-CMP-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC6 |

#### Project Documents & Records Plan - unique document

| Purpose | Describes the official documents and records of the NCSX project. (This document) |
| --- | --- |
| Review and Approval | Prepared by: NCSX System Engineering Support Manager Concurrences by: NCSX Design Integration Manager, NCSX Deputy Project Manager for Engineering, NCSX Project Engineers, and NCSX QA Manager Approved by: NCSX Engineering Manager |
| Format | -- |
| Naming Convention | NCSX-PLAN-DOC-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC6 |

#### Interface Control Management Plan - unique document

| Purpose | Provides a description of the processes that will be used to effect interface control on the NCSX Project |
| --- | --- |
| Review and Approval | Prepared by: NCSX System Engineering Support Manager Concurrences by: NCSX Deputy Project Manager for Engineering, NCSX Project Engineers, and NCSX QA Manager Approved by: NCSX Engineering Manager |
| Format | -- |
| Naming Convention | NCSX-PLAN-ICMP-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC6 |

#### Data Management Plan - unique document

| Purpose | Provides a description of the processes that will be used to effect document and drawing control on the NCSX Project |
| --- | --- |
| Review and Approval | Prepared by: NCSX System Engineering Support Manager Concurrences by: NCSX Systems Integration Manager, NCSX Deputy Project Manager for Engineering, NCSX Project Engineers, and NCSX QA Manager Approved by: NCSX Engineering Manager |
| Format | -- |
| Naming Convention | NCSX-PLAN-DMP-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC6 |

#### Test and Evaluation Plan - unique document

| Purpose | A Test and Evaluation Plan (TEP) establishes how integrated system testing will be performed and managed. The TEP will include an overview and schedule of the integrated system test program and the purpose, scope, and objective of each system test; test configurations; and test responsibilities. |
| --- | --- |
| Review and Approval | Prepared by: NCSX Construction Manager Concurrences by: NCSX Deputy Project Manager for Engineering, NCSX Project Engineers, NCSX QA Manager, and PPPL Engineering Department Head Approved by: NCSX Engineering Manager |
| Format | -- |
| Naming Convention | NCSX-PLAN-TEP-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC6 |

#### Mission, Experimental Plan, and Preparations - unique document

| Purpose | Provides an overview of the planned phases of NCSX operation |
| --- | --- |
| Review and Approval | Prepared by: NCSX Physics Head Uncontrolled document |
| Format | -- |
| Naming Convention | NCSX-PLAN-EXP-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC6 |

#### NCSX Procedures

| Purpose | Provides clarifying guidance and instructions on preparing specific NCSX documents and/or terms. Intended to supplement existing PPPL engineering procedures. |
| --- | --- |
| Review and Approval | Prepared by: NCSX System Engineering Support Manager Reviewed by: WBS Managers, NCSX Project Engineers, NCSX QA Manager, NCSX ES&H Engineer and other appropriate NCSX impacted individuals Approved by: NCSX Engineering Manager |
| Format | -- |
| Naming Convention | NCSX-PROC-###-XX_YY where ### is the numerical number of the procedure, XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]. Document name provides the scope of the procedure. |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC6 |

### Requirements Documents

#### General Requirements Document (ASPEC) - unique document

| Purpose | The General Requirements Document (GRD) is a system (top) level specification which states the technical and mission requirements for the entire system (WBS Level 1), allocates requirements to functional areas (WBS elements), document design constraints, and defines interfaces between or among functional areas |
| --- | --- |
| Review and Approval | Prepared by: NCSX Project Engineer Concurrences by: NCSX Physics Manager Approved by: Project Manager |
| Format | ENG-006 or equivalent Project standard |
| Naming Convention | NCSX-ASPEC-GRD-XX_YY where XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC4 |

#### Development Specifications (BSPEC) - many documents

| Purpose | Development (“design to”) specifications are documents below the system (top) level that state performance, interface, and other technical requirements in sufficient detail to permit design, engineering for service use, and evaluation. Development specifications are intermediate, between the system specification and product specification(s). |
| --- | --- |
| Review and Approval | Prepared by: Cognizant WBS Manager Concurrences by: Cognizant Project Engineer, NCSX QA Representative Approved by: NCSX Engineering Manager |
| Format | ENG-006 or equivalent Project standard |
| Naming Convention | NCSX- BSPEC-WBS-###-XX_YY where WBS is the three digit WBS identifier, ### is the numerical identifier for that specification within the WBS, XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]). (Document names assigned by cognizant WBS Manager per prescribed convention) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC5 |

#### Product Specifications (CSPEC)- many documents

| Purpose | Product specifications are applicable to production items below the system (top) level. All procurements below the system level should be based on product specifications. Product (“build to”) specifications may be oriented towards procurement of a product through specification of primarily functional (performance) requirements or primarily fabrication (detailed design) requirements. A product functional specification states (a) the complete performance requirements of the product for the intended use, and (b) the necessary interface and interchangeability characteristics. It covers form, fit, and function. Complete performance requirements include all essential functional requirements under service environmental conditions or under conditions simulating the service environment. Quality assurance provisions for hardware include one or more of the following inspections/tests: qualification evaluation, pre-production, periodic production, and quality conformance. A product fabrication specification states (a) a detailed description of the parts and assemblies of the product, usually by prescribing compliance with a set of drawings, and (b) those performance requirements and corresponding tests and inspections necessary to assure proper fabrication, adjustment, and assembly techniques. Tests are normally limited to acceptance tests in a shop environment. |
| --- | --- |
| Review and Approval | Prepared by: Cognizant WBS Manager or Technical Representative Concurrences by: Cognizant WBS Manager (if not the author), Cognizant Project Engineer, NCSX QA Representative Approved by: NCSX Engineering Manager |
| Format | ENG-006 or equivalent Project standard |
| Naming Convention | NCSX- CSPEC-WBS-###-XX_YY where WBS is the three digit WBS identifier, ### is the numerical identifier for that specification within the WBS, XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]). (Document names assigned by cognizant WBS Manager per prescribed convention) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC5 |

#### Process Specifications (DSPEC) - many documents

| Purpose | This type of (“build to”) specification is applicable to a process which is performed on a product or material. Examples of processes are: heat treatment, welding, plating, and marking. Process specifications cover manufacturing techniques which require a specific procedure in order that a satisfactory result may be achieved. Where specific processes are essential to fabrication or procurement of a product or material, a process specification is the means of defining such specific processes. |
| --- | --- |
| Review and Approval | Prepared by: Cognizant WBS Manager Approved by: NCSX Project Engineer |
| Format | ENG-006 or equivalent Project standard |
| Naming Convention | NCSX- DSPEC-WBS-###-XX_YY where WBS is the three digit WBS identifier, ### is the numerical identifier for that specification within the WBS, XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]). (Document names assigned by cognizant WBS Manager per prescribed convention) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC5 |

#### Material Specifications (ESPEC) - many documents

| Purpose | This type of (“build to”) specification defines the required qualities or condition of raw or semi-fabricated material (e.g., electrical cable, copper tubing) used in fabrication |
| --- | --- |
| Review and Approval | Prepared by: Cognizant WBS Manager Approved by: NCSX Project Engineer |
| Format | ENG-006 or equivalent Project standard |
| Naming Convention | NCSX- ESPEC-WBS-###-XX_YY where WBS is the three digit WBS identifier, ### is the numerical identifier for that specification within the WBS, XX is the revision number and YY is the level of approval (e.g. draft [dA] or approved [signed]). (Document names assigned by cognizant WBS Manager per prescribed convention) |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC5 |

### Design Support Documentation

#### Design Drawings and Models – many documents

| Purpose | Drawings and models represent the physical configuration of the Project in either 2D or 3D. |
| --- | --- |
| Review and Approval | Prepared by: Designer or Cognizant Engineer Reviewed by: Cognizant Engineer (if not the creator of the drawing, WBS Manager, and Design Integration Manager Approved by: Cognizant Project Engineer |
| Format | PPPL or ORNL Drawing Standards using ProEngineer, AutoCAD, or other Project-approved drawing software package. |
| Naming Convention | As indicated in paragraph 5.2.1.3 of this Document and Records Plan |
| Storage Location | Pro/INTRALINK Database |
| Document Retention Key | DC5 |

#### Interface Control Documents – many documents

| Purpose | ICDs define the physical interfaces between two separately deliverable items when the mutual boundary area is not controlled by a single developmental (“design to”) specification (BSPEC). |
| --- | --- |
| Review and Approval | Prepared by: WBS Manager on one side of the interface Reviewed by: WBS Manager on the other side of the interface and cognizant Project Engineers Approved by: NCSX Systems Engineering Support Manager (facilitates reaching agreement) |
| Format | NCSX Procedure 003 (NCSX-PROC-003), Interface Control. |
| Naming Convention | As indicated in the above procedure |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC5 |

#### Calculations and Analyses – many documents

| Purpose | Calculations and analyses provide confirmatory evidence of the soundness of the proposed design |
| --- | --- |
| Review and Approval | Prepared by: Cognizant Engineer Checked by: Assigned individual assigned to check the calculation by the responsible WBS Manager |
| Format | Per PPPL Engineering Procedure 033, Design Verification. |
| Naming Convention | As indicated in the above procedure |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC5 |

#### Design Memoranda - many documents

| Purpose | General means of providing design basis information that does not fit into one of the other established documentation/record types. |
| --- | --- |
| Review and Approval | Prepared by: Assigned responsible individual Approved by: None |
| Format | -- |
| Naming Convention | YYMMDD_Subject_XXX_ZZZ where YYMMDD is the date of the memorandum, Subject is a brief description of the topic of the design memorandum, XXX is the 3 digit WBS identifier, and ZZZ are the arthor’s initials. |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | Determined by the content of the memorandum in accordance with Table 4-1 |

#### Design Review Records – many documents

| Purpose | These documents provide the basis for design decisions made at specific monitoring points in the development of the design (e.g., preliminary, final) |
| --- | --- |
| Review and Approval | Prepared by: NCSX WBS Manager Reviewed by: Design Review Committee members Approved by: Engineering Manager |
| Format | Per PPPL Engineering Procedure 033, Design Verification |
| Naming Convention |  |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC5 |

#### Engineering Change Proposals – many documents

| Purpose | These documents describe the authorized changes to the technical, cost and schedule baseline |
| --- | --- |
| Review and Approval | Prepared by: NCSX Cognizant Engineer Concurrences by: WBS Managers, Project Engineers, QA Manager, Physics Manager (if impacted), Engineering Manager, Project Control Manager, ES&H Representative Approved by: NCSX Project Manager or DOE (depending on ECP Level) |
| Format | Per CMP |
| Naming Convention | Per CMP |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC5 |

### NEPA Documentation

#### Environmental Assessment (EA) – unique document

| Purpose | This document provides an overview of the environmental impact of the NCSX Project |
| --- | --- |
| Review and Approval | Prepared by: NCSX ES&H Engineer Approved by: DOE |
| Format | General EA content requirements specified in 10CFR1021 and 40CFR1508.9 |
| Naming Convention |  |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC2 |

#### NEPA Planning Form – many documents

| Purpose | This document provides an assessment of the environmental impact of a proposed project/modification. |
| --- | --- |
| Review and Approval | Prepared by: Cognizant Engineer Reviewed by: NCSX RLM Approved by: PPPL NEPA Compliance Officer |
| Format | ESH-014 or equivalent Project Standards |
| Naming Convention |  |
| Storage Location | Retained by Cognizant Engineer |
| Document Retention Key | DC2 |

#### Safety Assessment Document – unique document

| Purpose | This document provides an overview assessment of the as-built project on the environment and its impact the safety of the public. |
| --- | --- |
| Review and Approval | Prepared by: NCSX ES&H Engineer Approved by: PPPL Safety Review Committee (SRC) |
| Format | PPPL ESHD – 5008, Section 11 |
| Naming Convention |  |
| Storage Location | NCSX Engineering Web Page |
| Document Retention Key | DC2 |

### Quality Assurance Records

#### Quality Assurance Records - many documents

All records are maintained and controlled per Quality Assurance internal document, QP-002, Quality Assurance Records.

| Record Type | Purpose | Applicable Procedure |
| --- | --- | --- |
| Audit/Surveillance | Document results of audits and surveillances on NCSX, the findings, and the corrective action taken to resolve the findings. | QA-002 |
| Risk Acceptance Plan | Documents inspection plan for an activity. | QA-004 |
| Nonconformance Report | Documents nonconformances and their resolution. The definition of nonconformance from QA-005 is: "Any deficiency in characteristic, documentation, design, function, or procedure that renders the quality of an item or activity unacceptable or indeterminate." | QA-005 |
| Storage Location | PPPL QA Files |
| Document Retention Key | DC3 |

### Training Records

#### Training Records - many documents

| Record Type | Purpose | Applicable Procedure |
| --- | --- | --- |
| Course Content | Document content of training programs. | TR-001, Laboratory Training Program |
| Training attendance and completion | Document the individuals who completed each training program. | Same |
| Storage Location | PPPL Training Records |
| Document Retention Key | DC7 |

### Procurement Deliverables

#### Procurement Deliverables - many documents

| Purpose | This includes records provided to NCSX by a supplier as a result of contractual requirements. They provide evidence of the quality of procured items. Examples of such records are: Manufacturing, Inspection, and Test (MIT) Plan Reliability and Maintainability Documents Workmanship Standards Completed Release for Shipment Form Process History, which includes Certificates of Compliance, Material Certifications, Planning & Control Documents, Inspection Reports, Test Reports, Supplier NCRs, and Personnel Qualifications and Certifications Quality Assurance Plan Quality Assurance Program Manuals |
| --- | --- |
| Review and Approval | Prepared by: Supplier Approved by: Supplier or NCSX, as specified in the contract |
| Format | Supplier specified |
| Naming Convention |  |
| Storage Location | PPPL Procurement Files |
| Document Retention Key | DC7 |

#### Statements of Work – many documents

| Purpose | These documents detail work requirements. |
| --- | --- |
| Review and Approval | Prepared by: NCSX Contract Technical Representatives Approved by: NCSX Engineering Manager (or designee) |
| Format | TBD |
| Naming Convention | NCSX-SOW-wbs#-sow#-rev# (Document names assigned by cognizant WBS Manager per prescribed convention) |
| Storage Location | PPPL Procurement Files |
| Document Retention Key | DC5 |

### Other Documents

#### Memoranda - many documents

| Purpose | General means of providing information that does not fit into one of the other established documentation/record types. |
| --- | --- |
| Review and Approval | Prepared by: Assigned responsible individual Approved by: None |
| Format |  |
| Naming Convention | xx-yymmdd-name-zz |
| Storage Location | Retained by author – may also be posted on the Engineering Web Page |
| Document Retention Key | Determined by the content of the memorandum in accordance with Table 4-1 |

#### WBS Dictionary – unique document

| Purpose | A product-oriented family tree composed of hardware, software, data, facilities, and services that result from systems engineering efforts during the development and production of system elements. Displays and defines the product(s) to be developed or produced, and relates the elements of work to be accomplished to each other and to the end product. Provides structure for guiding multi-disciplinary team assignment and cost tracking and control. |
| --- | --- |
| Review and Approval | Prepared by: NCSX Systems Engineering Manager Concurrences by: Impacted WBS Managers, Deputy Project Manager for Engineering, Project Physics Manager, Cognizant Project Engineer, and Engineering Manager. Approved by: NCSX Project Manager |
| Format |  |
| Naming Convention | NCSX-WBS-rev# |
| Storage Location | NCSX Engineering Web Page |
| NCSX Record Key | DC-1 |

#### Cost and Schedule Documents – many documents

| Purpose | These documents provide the chronological development of the cost and schedule baselines |
| --- | --- |
| Review and Approval | Prepared by: NCSX Project Control Manager Concurrences by: WBS Managers, Project Engineers, and Engineering Manager Approved by: NCSX Project Manager or DOE (depending on level of information) |
| Format | Utilize the P3 database |
| Naming Convention |  |
| Storage Location | Details maintained on the P3 database kept by the Project Control Manager, but summary information posted on the NCSX Engineering Web Page |
| NCSX Record Key | DC6 |