###### --NCSX

INTERFACE CONTROL MANAGEMENT PLAN

(NCSX-PLAN-ICMP)

DRAFT A

September 19, 2002

Prepared by:

R. Simmons, Systems Engineering Support Manager

Concurrences:

_____________________________  	_____________________________

J. Malsbury, QA Manager	  B. Nelson, Stellarator Core Systems

Project Engineer

_____________________________  	_____________________________

L. Dudek, Ancillary Systems				E. Perry, Assembly Operations Project Engineer					Project Engineer

_____________________________

P. Heitzenroeder, Deputy Project

Manager for Engineering

Approved by:  ______________________________________

W. Reiersen, Engineering Manager

| Revision | Date | Description of Changes |
| --- | --- | --- |
| DRAFT A | September 19, 2002 | Initial draft |

Table of Contents

1	Introduction	1

1.1	Purpose	1

1.2	Applicable Documents	1

1.3	Overview of the Interface Control and Management Program	1

1.3.1	Responsibility for the ICM Program	1

1.3.2	Interface Definition	2

1.3.3	Interface Documentation	2

1.3.4	Changes to Interfaces	3

2	The Interface Control And Management Process	3

2.1	Evolution of the ICM Process	3

2.2	Scope Sheets and ICDs	4

2.2.1	Numbering Scheme	4

2.2.2	Scope Sheets	4

2.2.3	Interface Control Documents	5

2.3	Relationship to Data Management and the Configuration Management Programs	7

2.3.1	Data Management Program	7

2.3.2	Configuration Management Program	7

2.4	Cancelled/Obsolete ICDs	7

2.5	Interface Incompatibilities	7

2.6	Dispute Resolution	7

Annex I – Scope Sheet

Annex II – Interface Control Document (ICD)

List of Figures

Figure 2.2-1 ICD and Scope Sheet Identification Scheme	4

List of Tables

Table 2.2-1 Scope Sheet and ICD Tracking Log	6

# Introduction

## Purpose

An interface represents a technical agreement between two or more activities or Work Breakdown Structure (WBS) elements that documents the functional, performance, and physical characteristics required to exist at a common boundary between the activities or WBS elements.  Interfaces serve as integration constraints to ensure that systems and subsystems mutually can be assembled and/or function together.  As the design evolves, increasing more detailed interfaces will also evolve and be documented.  The process described in the Interface Control Management Plan (ICMP) describes the policies and procedures for generating and administering these technical agreements.

The process of defining and managing interfaces on NCSX is called Interface Control and Management (ICM).  The ICM program outlined in this ICMP recognizes that the interface definition begins well before the start of conceptual design, but that the control and management process does not begin until the start of preliminary design.  The ICM program ends with project decommissioning.  Two key requirements of ICM are the:

- Technical efforts to arrive at mutually acceptable technical agreements and the preparation of supporting documentation of these agreements; and

- The administrative efforts to manage the generation of agreements and related documentation, including changes as the design evolves.

The ICM Program is closely linked to the Systems Engineering (SE) program and its detailed supporting programs such as Configuration Management and Data Management. A broader discussion of the relationship of the ICM Program to these is contained later in this plan.

## Applicable Documents

This ICMP draws on the documents listed below.  Documents referenced are the latest issues of the:

- Systems Engineering Management Plan (NCSX-PLAN-SEMP)

- Work Breakdown Structure (WBS) Dictionary (NCSX-WBS)

- Quality Assurance Plan (NCSX-PLAN-QAP)

- Data Management Plan (NCSX-PLAN-DMP)

- Documents and Records Plan (NCSX-PLAN-DOC)

- Configuration Management Plan (NCSX-PLAN-CMP)

- Pro/INTRALINK Users Guide

## Overview of the Interface Control and Management Program

### Responsibility for the ICM Program

The Systems Engineering Support Manager is responsible to the NCSX Engineering Manager for administering the NCSX ICM Program.  At a minimum, the following personnel will be involved in identifying, resolving interface problems, and documenting interface agreements:

- Systems Engineering Support Manager

- Cognizant Project Engineers impacted by the proposed interface

- Cognizant WBS Managers impacted by the proposed interface

- Other personnel deemed necessary to fully define and reach agreement on the interface

A major responsibility of the Systems Engineering Support Manager is to facilitate processing of and approval of scope sheets and interface control documents (ICDs), resolving interface requirements definition and responsibility disputes (with the concurrence of the responsible Project Engineer and Engineering Manager), and resolution of interface incompatibilities and changes.

### Interface Definition

#### Primary Interfaces

A primary interface item exists between two separately deliverable items (referred to as Configuration Items/CIs in systems engineering terms) when the mutual boundary area is not controlled by a single WBS manager and/or when, at the discretion of the cognizant Project Engineer, the interface is determined to be critical to the performance of the NCSX program.  Configuration Items (CIs) represent the lowest level of control under configuration management and may be a single physical or functional item or collection of items that will satisfy a final end product or deliverable.  Primary interfaces will be defined, documented, and brought under configuration control by the time of the earliest Preliminary Design Review (PDR) for those CIs.  The methods by which primary interfaces are identified, documented, and managed is controlled by the system described in this ICMP and other project plans and procedures.

#### Secondary Interfaces

A secondary interface is an interface that lies solely within the control of a single WBS Manager, even though it might cross WBS boundaries.  Secondary interfaces will remain under local control by the WBS Manager until such time that the design is completed and the CI ready for delivery or  the CI interface is elevated to a primary interface status.  The methods by which secondary interfaces are identified and managed are left to the discretion of the WBS Manager.  Accordingly, the system described in this ICMP is not mandated for secondary interfaces.

### Interface Documentation

Primary interfaces are defined by ICDs.  The need for new or updated ICDs may be generated by the introduction of new components/software either by engineering changes to existing designs and/or design evolution.  These ICDs may be either in a drawing (pictorial) or book form (written) format.  As a first step in generating ICDs, scope sheets will be developed for each interface.  Section 2 includes a broader discussion of the ICM process and its documentation.  Approved ICDs will be stored in the Pro/INTRALINK database, either as part of drawings and models or as controlled book form ICDs.

### Changes to Interfaces

Once an interface is defined, approved and posted as an ICD, the interface will come under configuration control.  Generally this will occur prior to the time of the PDR for the impacted CIs.  Changes to interfaces will be processed in accordance with the system outlined in the CMP.

# The Interface Control And Management Process

## Evolution of the ICM Process

The analysis of an interface begins with the concept design phase and with the identification of the basic interface boundaries, continues through the design and fabrication phases, the operational phases, and ends with project shutdown and decommissioning.

During the establishment of the NCSX program in the pre-conceptual and conceptual design phases, a system-level interface analysis was conducted that resulted in the definition of the major functional interfaces for each concept being considered.  These basic interfaces were reflected in the overall Pro/Engineer (Pro/E) models that were developed.  At this stage, although no ICDs were generated, at the completion of Conceptual Design Review (CDR) the initial technical, cost, and schedule baselines are established.  The technical documentation that provided the basis for the establishment of the technical baseline represented high-level interfaces between major components and WBS elements, but these interface agreements were not yet formalized.  These baselines serve as the starting point for the preliminary design phase.  It was also at this point in the Systems Engineering process outlined in the System Engineering Management Plan (SEMP), that the majority of Configuration Items (CIs) that will form the configuration management bases were defined.

Once the conceptual design is established and preliminary design commences, the details and completeness of interfaces increase.  Early in the preliminary design phase, scope sheets are prepared to initiate agreements that will eventually define the primary interfaces required between participants.  These scope sheets are intended to act as planning documents that will facilitate definition and agreement as to the specific primary interfaces.  As the Preliminary Design Review (PDR) approaches, ICDs will be prepared that define and facilitate coordination between participants in support of the PDR.  ICDs shall be one of the deliverable items to be finalized by the completion of the PDR.  These ICDs then become part of the technical baseline documentation and are under the configuration control processes outlined in the Configuration Management Plan (CMP).  These ICDs represent key agreements that will enable each agreeing WBS Manager to proceed with his or her  design secure in the knowledge that the interfacing WBS element will not alter the interface without going through the change control process.  As indicated in the SEMP, not all subsystems and CIs undergo PDRs at the same time and so not all subsystems and CIs have their ICDs developed on the same time scale.

As the design progresses into final design and beyond, additional interfaces may be defined and documented on new scope sheets and ICDs will be prepared and approved.  Should modifications to existing ICDs be identified as part of the design evolution process, these changes will be processed through the normal Engineering Change Proposal (ECP) processes described in the CMP.  Completed and modified ICDs will be controlled as part of the technical baseline and will be posted in pdf format in the Pro/INTRALINK database.

## Scope Sheets and ICDs

### Numbering Scheme

Scope sheets and ICDs will utilize a standard numbering scheme that clearly identifies the two impacted WBS elements that interact to form a primary interface.  The following format shall be utilized:

Figure 2.2-1 ICD and Scope Sheet Identification Scheme

### Scope Sheets

Scope sheets are the first step in the process of generating ICDs representing primary interfaces.  The scope sheet is really only a planning document that provides a formal acknowledgement between two parties that an interface exists between them, who is responsible for documenting the primary interface, and when the primary interface will be defined on an ICD.  These will be generated early in the preliminary design phase and will eventually be replaced by formal ICDs prior to the CDR, although the scope sheets will be retained as historical records since they are useful in providing a prose definition of where primary interfaces exist.  The scope sheet is a planning document that facilitates definition and recognition of the ownership of an interface and the ICD is a technical document that provides the technical definition agreement and documentation of the interface physical and functional characteristics.

Annex I to this ICMP contains a sample Scope Sheet format and a broader discussion of the content of the scope sheet.  Scope sheets will be signed by both parties to the primary interface and will be posted on a scope sheet/ICD interface tracking log shown as Figure  .

### Interface Control Documents

#### Interface Types

The format and content of an ICD will vary depending upon the nature of the design requirements documented.  For example, the interface between two electrical connectors may also include mechanical aspects (e.g., connector size, pin/socket configuration, etc.) of the interface.  Thus, an ICD for this interface would necessarily include both electrical and mechanical information on that interface.  Interface design requirements are typically grouped into the following categories:

- Mechanical, including envelopes

- Electrical

- Magnetic

- Fluid

- Environmental

- Sequencing/programming and Timing

- Computer Programming

- Man/Machine

#### Format of ICDs

All ICDs will be prepared in a book form or written format.  If an interface can be completely described in a drawing or model, the book form ICD may only contain a single line reference to the applicable drawing or model on which the interface is shown or to a separate stand-alone interface description drawing (IDD).  These drawings and models will be numbered in accordance with the procedures outlined in the Data Management Plan (DMP) and the Pro/INTRALINK Users Guide.  In many instances, functional design requirements (e.g., electrical, sequencing and timing, etc.) cannot be adequately described on drawings.  When extensive written information or tabular data must be presented, the book form ICD will totally represent the interface.  Book form ICDs may be multi-sheet, letter-size documents.  They may also be used for mechanical/envelope interface requirements provided that the information can be adequately displayed on a standard letter-size page.  Every book form ICD shall contain, as a minimum, a title page (including revision number), the unique ICD number, and a description of the interface, and summary/tabular data that defines the interface.  Annex II to this ICMP describes the book form ICD in greater detail.

#### Use of Callouts to Describe Interfaces

The Pro/INTERLINK Users Guide provides a broader discussion of the preparation of CAD drawings and models using Pro/Engineer software.  Interfaces that can be defined pictorially on a drawing will utilize this format as the preferred method of illustrating primary interfaces.  When the ICD is prepared, the impacted drawing or model, or if needed a separate IDD, will be updated and promoted as appropriate.  The drawing format ICD shall be prepared in sufficient detail to accurately reflect the interface and envelope.  In addition, the overall drawing and model will be annotated to show the ICD number clearly on the drawing and callouts will be use used to qualify or amplify information on the interface.

For drawings and models developed in AutoCAD or other project-approved drawing software package, ICDs will also be clearly reflected on the drawing or model.  If the ICD impacts component or subsystem envelopes, the ICD will also have to be reflected on the overall Pro/Engineering model to be used for space allocation and assembly.

Callouts will be utilized to amplify interface information.  For mechanical and envelope interfaces, the callout will used to display critical dimensions and characteristics to assist the system designers in evaluating potential changes and to assist them in preventing changes that inadvertently alter an interface.  Interface characteristics can be affected by a multitude of details in the design or modification to an electrical circuit, software, or timing or I/O sequencing documents.  This sometimes makes it impractical for the callout to adequately describe the interface at the piece-part level.  In this case, callouts will be placed on a higher level assembly drawing or software program component.

#### Tracking and Implementation System

Table 2.2-1 is a sample of a scope sheet of an illustrative interface and ICD tracking log that will be maintained on the Engineering Web page that is dedicated to interfaces definition and control.  This web page is envisioned to be a simple Excel spreadsheet format to facilitate various sorting options.

| WBS #1 | WBS #2 | Scope Sheet or ICD | Sequential Number | Brief Description |
| --- | --- | --- | --- | --- |
| 110 | 120 | SS | SS-110-120-0001 | Magnetic diagnostics port allocations through the vacuum vessel |

Table 2.2-1 Scope Sheet and ICD Tracking Log

Once an ICD is approved and under configuration control, the implementation of the ICD into the impacted documentation shall be tracked as part of the ECP implementation tracking system outlined in the Configuration Management Plan (CMP).  If an approved ICD is later modified as a result of a subsequent ECP, the ICD will be also listed as an impacted document and its implementation tracked.

## Relationship to Data Management and the Configuration Management Programs

### Data Management Program

An ICD whether in drawing or book form format is just another technical document that needs to be prepared, controlled, and managed.  The Data Management Plan (DMP) provides a discussion of how these ICDs will be managed.

### Configuration Management Program

The Configuration Management Plan (CMP) contains a broader discussion of the overall configuration control process.  Once under configuration control, changes to ICDs, like drawings or models, or specifications are processed via the ECP and will be listed as an impacted document.  As indicated above, the implementation of modifications to ICDs shall be tracked and discussed as part of the detailed ECP implementation status during the monthly status meetings with the WBS Managers.

The design process keeps the interface documentation current by continually addressing primary interfaces between WBS elements.  ICDs approved at the end of the PDR are used as the starting point for the design effort to proceed.  As the design progresses, it may become necessary to modify the existing ICD via an ECP or to impose an interface condition that did not previously exist.

## Cancelled/Obsolete ICDs

In some rare instances, it may be appropriate to cancel an ICD since it no longer defines an existing interface or the interface requirements have changed so significantly due to design changes such that the ICD is no longer applicable.  Requests to cancel an ICD will be processed via the ECP process.  In cases where the interface requirements have changed so significantly, a new scope sheet and ICD will be developed and approved.

## Interface Incompatibilities

Engineering errors, specification anomalies, manufacturing tolerance problems, etc., may result in interface incompatibilities that may not be discovered until after interface agreements are complete.  Incompatibilities may be detected as the design matures, as prototypes are developed, during functional or verification fit checks, assembly and testing, etc.  All incompatibilities must be identified to the impacted parties to the interface, the cognizant Project Engineer, and the Systems Engineering Support Manager as soon as they are discovered.  The potential impact on other interfaces must also be assessed.  A correction approach will be developed by the two interface parties and may include further analysis, hardware/software redesign, or interface revision to correctly define the actual interface.  More than likely, an ECP will result from the resolution of interface incompatibilities.

## Dispute Resolution

In cases where agreement cannot be reached between two parties, the Systems Engineering Support Manager will request the assistance of the cognizant Project Engineer to resolve the dispute.  If the dispute cannot be resolved at that level, the Engineering Manager will be the deciding official.

NCSX Interface Control Management Plan

Annex I

Scope Sheets

Sample Scope Sheet

| INTERFACE SCOPE SHEET |
| --- |
| Scope Sheet Number: | Date Initiated: |
| Title: | Revision #: Rev Date: |
| Impacted WBS Elements: |
| Responsible WBS Mangers: |
| Scope of Interface: |
| Equipment and Responsibility List: |
| Sketch or Drawing of Interface: (or Attach Continuation Sheet) |
| Date ICD will be Prepared: |
| Related Scope Sheets or ICDs: |
| Approvals: WBS Manager: WBS Manager: Project Engineer: Project Engineer: Systems Engineering Support Manager: |

Guidelines for Completing Scope Sheet

- Scope Sheet Number – Number in accordance with Section 2.2.1.  The Systems Engineering Support Manager will assign the sequential number.

- Date Initiated – Self explanatory.

- Title – The title should contain names of the systems or components to which the interface belongs with the originating system named first, e.g., Power Systems Control to Central I&C.  If the scope sheet contains multiple interfaces, the names used will be the names of the interfacing WBS elements.

- Revision and Date – self-explanatory.

- Responsible WBS Managers – identifies the responsible WBS Managers impacted by this interface.

- Scope of Interface – The scope description should be a summary of the Scope Sheet and eventual ICD and its intended purpose.  If deemed important, the scope may also specify the methods to be employed by the ICD to document/verify interface design parameters, such as installation drawings, mated circuits, timing diagrams, etc.  The location of the interface should also be included, e.g., the interface between the shielding and vacuum vessel shall be at the (provide the location by appropriate physical description.

- Equipment and Responsibility List – The equipment responsibility list should consist of listing of interfacing hardware/software/facilities along with their respective identification numbers, common name, and the WBS Manager responsible for their design.  This identifies which party of the interface agreement has responsibility of taking the lead in defining the interface.

- Sketch or Drawing of the Interface – sketch or drawing in sufficient detail to document the interface.  An initial layout drawing showing the location of the interface may be sufficient.

- Date ICD will be Prepared – an agreed upon date when the interface will be finalized and converted to an ICD.  In all instances, this will be prior to the PDR for the impacted Configuration Items.

- Related Scope Sheets or ICDs – All known interfaces impacted by the proposed interface that will be or have been identified on other scope sheets or ICDs should be listed.  Related interfaces documented on scope sheets or ICDs should be reviewed for impact whenever this interface is changed.

Approvals – approval signatures are required for all WBS Managers and Project Engineers that are affected by this interface to formally recognize the agreement.  Signature by the Systems Engineering Support Manager denotes that the scope sheet has been recorded and preparation and approval of the respective ICD will be tracked.

NCSX Interface Control Management Plan

Annex II

Interface Control Documents (ICDs)

Sample ICD

| INTERFACE CONTROL DOCUMENT TITLE AND APPROVAL PAGE |
| --- |
| ICD Number: | Primary Author: |
| Impacted WBS Elements: | Type of Interface: |
| Description of Interface: |
| Record of Revisions Revision Number Description Date |
| Approvals WBS Manager: WBS Manager: Project Engineer: Project Engineer: Systems Engineering Support Manager: |

ICD DETAILS

Section 1.0 – General Information

Scope:

Related ICDs:

Section 2.0 – Notes and Abbreviations

Notes:

Abbreviations:

ICD Details

Section 3.0 – Interface Block Diagrams and System Description

Interface Block Diagrams (attach sheets in necessary):

System Description:

Section 4.0 – Specific Description of the Interface(s)

Installation Information:

Other Information:

Guidelines for Preparing ICDs

All ICDs will be prepared in a book form or written format.  They will be prepared on multi-sheet, 8  by 11 inch letter size paper.  All ICDs will contain the following information:

Page 1 – Title and Approval Page

- Title – to include the following information:

  - ICD Number – per numbering scheme contained in Section 2.2.1 of the ICMP.  For example, this interface might be numbered: NCSX-250-661-0010.

  - Author of ICD – identifies the ICD Participant (WBS Manager) who has lead responsibility for defining the interface

  - WBS Elements Impacted – e.g., WBS 611 and WBS250

  - Type of Interface – e.g., mechanical/envelope interface

  - Description of Interface – e.g., Neutral Beam Cooling Water System to Neutral Beam Heating System

- Revision Record Table – to include record of revision numbers and date of the revision.  The initial approved issue will be Revision 0.

- Approval Record

  - Signatures of Both WBS Managers

  - Signatures of Both Responsible Project Engineers

  - Signature of the Systems Engineering Support Manager

Page 2 -  ICD Details and (if necessary) Follow-on Pages

    - Section 1.0 – General ICD Information

        - Scope – this should be a summary of the ICD contents and its intended purpose.  The ICD should accurately reflect the latest approved technical baseline that will be reviewed as part of the PDR.  If deemed necessary to adequately describe the interface, the methods employed by the ICD to document/verify interface design parameters; the drawing/model number.

        - Equipment and Responsibility List – the equipment responsibility list should consist of a list of interfacing hardware/software/facilities, along with their respective identification number, common name, and the ICD participant (WBS Manager) responsible for their design.

        - Related ICDs – all ICDs should include a complete list of those ICDs that may be impacted by and/or impacts the new/revised ICD.  These related ICDs shall be identified by their unique identifier and name.  Related ICDs should be reviewed for impact whenever an interface design is implemented or proposed.

    - Section 2.0 – Notes and Abbreviations

        - Notes – any explanatory notes that might clarify the intent of the ICD or explain or quantify information which applies to the ICD, whether in general or to specific areas of the interface.  If the ICD can be described by a drawing or model with amplifying callouts, the general character of the callout should be listed here.  Tolerances should also be specified.

        - Abbreviations – all unfamiliar abbreviations, acronyms, symbols, etc. used in an ICD should be defined in this section.

      - Section 3.0 – Interface Block Diagrams and System Description

        - Interface Block Diagrams – the interface block diagram should be a relatively simple pictorial representation of the interface.  The interface block diagram can be more complex if required to adequately define the interface.  In cases where the interface is depicted on an existing drawing or model, you need only record the drawing number and title here (per the numbering scheme outlined in the DMP and Pro/INTRALINK Users Guide).

        - System Description – Only need to enter a brief word description of the systems to adequately describe the interface, e.g., “The Neutral Beam Cooling Water System(WBS 661) shall provide water to cool the Neutral Beam Injection System (WBS 250) components.  Coolant lines shall be provide for supply and return of the coolant.”

      - Section 4.0 – Specific Description of the Interface(s)

        - Installation Information – provide a physical description (augmented by sketches if appropriate) of the installation of the interface, e.g., the mechanical interface between WBS 661 and WBS 250 in this example.

        - Other information – provide other interface information as appropriate.  For example, if the interface involves a cooling system, the supply information (flow rate, temperature, and pressure) should be specified as well as the return information (pressure).  For electrical interfaces, both the mechanical and electrical details should be specified to adequately define the interface.

# Comments

Page: 1
 Interface control is part of the overall configuration management program. Do we need a separate document for interfaces or can this be added to the Configuration Management Plan?

Page: 1
 You wouldn’t let me reference the “latest issues” in a the QA Plan!!! Actually, I think it is the appropriate thing to do.

Page: 2
 This is a plan and, as such, shouldn’t contain procedural information.

Page: 3
 I’m sure you are tired hearing this, but this part is not consistent with PPPL culture.

Page: 3
 However, the ICD should be developed and placed under configuration control at the same time that the first system or subsystem (of the two involved in the interface) has a PDR.

Page: 5
 Figure?

Page: 5
 Does this conflict with ¶ 2.2.1, which defines how these will be numbered?

Page: 5
 I am not familiar with this term. Will others be?

Page: 6
 I envision this table to be an Excel spreadsheet that you can view by clicking on a link. A subpage to the Engineering web page would probably not be needed for one link.

Page: 6
 I think this is the first time in this document that indicates the use of ECPs to make changes to approved ICDs. Would prefer that this is clearly indicated early in this document. However, the most important place where this should clearly be highlighted is in the associated NCSX procedure on the ECP process.

Page: 7
 Would these replace the existing ones? If so, then an ECP is needed to update them. If not, then an ECP is still needed to cancel the old ones. This should be clearly indicated here.

Page: 7
 Minor word change, but we use the term “plan” for many formal NCSX documents. In order to indicate that a formal project wide plan is not required here, I believe “approach” would be a better term.

Page: 6
Section 2.2.1 requires that the lower WBS number be first.

# Text boxes

Controlled Document

THIS IS AN UNCONTROLLED DOCUMENT ONCE PRINTED.  Check the NCSX Engineering Web prior to use to assure that this document is current.