National Compact Stellarator Experiment

NCSX

RELIABILITY, AVAILABILITY, AND MAINTAINABILITY PLAN

NCSX-PLAN-RAM-00-dA

August 8, 2003

Prepared by: _______________________________________

R. Simmons, NCSX Systems Engineering Support Manager

Concurrences:

_____________________________  	_____________________________

B. Nelson, Stellarator Core Systems		L. Dudek, Ancillary Systems

Project Engineer					Project Engineer

_____________________________  	_____________________________

E. Perry, Assembly Operations		J. Malsbury, QA Manager

Project Engineer

Approved by:  ______________________________________

W. Reiersen, Engineering Manager

Controlled Document THIS IS AN UNCONTROLLED DOCUMENT ONCE PRINTED. Check the NCSX Engineering Web prior to use to assure that this document is current.

RECORD OF REVISIONS

| Revision | Date | Originator | Description of Change |
| --- | --- | --- | --- |
| 0-dA | 8/8/03 | Simmons | Initial draft. |

Table of Contents

1	background	1

1.1	Overview	1

1.2	RAM Definitions	1

1.2.1	Reliability	1

1.2.2	Maintainability	1

1.2.3	Availability	2

2	PURPOSE	2

3	RESPONSIBILITIES	2

3.1	Systems Engineering	2

3.2	WBS Managers	2

4	Qualitative Characteristics of the ncsx ram program	3

4.1	Reliability	3

4.1.1	Requirements	3

4.1.2	Design Process	3

4.2	Maintainability	3

# background

## Overview

Experience has demonstrated that the design and commissioning of complex systems and devices with major technological advances will invariability have significant reliability deficiencies that could not be foreseen in the early design stages.  The National Compact Stellarator Experiment is certainly one of the more complex and technologically advanced fusion concepts under development today.  The primary objective of the NCSX Reliability, Availability, and Maintainability (RAM) program is to instill the systematic design disciplines to minimize or perhaps eliminate such an expectation for the NCSX Project.

From a reliability engineering perspective, the NCSX design incorporates all the classic hardware and system reliability risks associated with magnetic stresses and forces, electrical stresses, thermal stresses, vibration, moisture, and friction.  The primary NCSX design concern for reliability and maintainability is the close tolerances and design margins of major stellarator core components.  The RAM design designs for these components are critical considerations for NCSX success.  Further, it can be expected that, should significant NCSX reliability problems emerge, dedicated management attention and significant resources will be required to correct the problem.  Hence the desire to be proactive in the design to mitigate and/or eliminate potential RAM design problems is of paramount importance as the design progresses.

## RAM Definitions

### Reliability

Reliability is a measure of the certainty that a NCSX component system will perform its intended mission for a specified interval under specific conditions.   Simply stated, it is what fraction of the time a component or system will work.  Mathematically, it can be expressed in term of the Mean Time Between Failures (MTBT) or failures over time and the Mean Time to Repair (MTTR).  Qualitatively, it must be demonstrated that component or system designs are robust and utilize components or systems with a proven track record of operational success.

### Maintainability

Maintainability is a measure that if prescribed procedures and resources is used, a NCSX component or system will operate in the desired condition, or can be restored to that condition, within a specified time interval.  It is the inherent characteristic of a design that determines the amount of maintenance required to retain or restore the component or system to its desired condition; e.g., how quickly can the component or system be fixed.  Qualitatively, it must be demonstrated that maintenance procedures and necessary spares will be available when needed.

### Availability

Availability is based on the question, “is the NCSX component or system available in a working condition when it is needed.”   It reflects the readiness of the component or system.  Qualitatively, it must be demonstrated that the component or system will be available when needed.

You may want to change RAM to RAMI, where the I is Inspectability, the ability or ease of inspecting to determine where the component or system is in it’s service lifetime; e.g. measuring a pump vibration amplitude and spectrum to see it beginning to fail and replacing it as a part of preventative maintenance rather than waiting for it to fail on a Saturday at Midnight.

# PURPOSE

Rather than develop detailed RAM predictive models, the NCSX Project will apply a graded approach that sets out the principles and processes for ensuring the design is developed with due consideration to RAM requirements and that the achievement of these RAM requirements is demonstrated during design reviews.  This document lays out the guidelines and processes by which the RAM program is implemented based on consider of risk. This approach is much more qualitative in nature than the classical RAM mathematical analyses.

The NCSX General Requirements Document (NCSX-ASPEC-GRD) implements the overall project for mission reliability, operational availability, shot reliability, and maintainability. These general RAM requirements are then allocated down to the system and subsystem level via the Development Specifications (BSPECS) and further down to the component level via the Product Specifications (CSPEC).  The hierarchy of specifications and relationships is described in further detail in the Systems Engineering Management Plan (NCSX-PLAN-SEMP).  This RAM Plan compliments other NCSX Plans such as the Quality Assurance Plan (NCSX-PLAN-QAP) and the Configuration Management Plan (NCSX-PLAN-CMP) and applicable PPPL Engineering Procedures (e.g., ENG-008, “FEMCA”, etc.). A good approach, apportion system reliability budgets and make each system owner meet his/her budget.

# RESPONSIBILITIES

## Systems Engineering

The NCSX Engineering Manager is responsible for the development and implementation of the NCSX RAM program.  The Systems Engineering Support Manager assists him in carrying out this responsibility.

## WBS Managers

WBS Managers are responsible for optimizing designs for reliability and maintainability through systematic evaluation of design options, and for performing Failure Modes, Effects and Criticality Analyses (FEMCAs) for RAM design improvement and verification.  They are expected to demonstrate that their designs are robust from a RAM perspective at design reviews.

# Qualitative Characteristics of the ncsx ram program

## Reliability

### Requirements

The process to a more reliable component or system begins with the establishment and communication of requirements for capability, operational thresholds, and goals in clear and easily understood terms.  Several key features are important to remember:

- The requirements must be clear;

- The design requirements should be as simple as possible - simple design requirements lead to components and systems that are less expensive to build, operate, and maintain; and

- The requirements should be testable (easily verified).

### Design Process

Successful designs utilize robust and proven components and systems that have a successful demonstrated track record.  For those components and systems that are approaching state-of art, the reliability of the design can be improved by:

- Establishing design criteria based on historical experience with proven designs;

- Performing trade studies to arrive at design concepts with the highest potential design margins;

- Performing sufficient research and development activities to demonstrate that the proposed design is robust, can be easily built, and will satisfy desire performance parameters;

- Making detailed decisions that may adjust requirements, resources, and constraints into the most reliable design.

Good! Have Design Criteria Documents for each system and Interface Control Documents for system to system interface control.

## Maintainability

Maintainability and reliability are the two major system characteristics that combine to form the commonly use effectiveness index – availability.  Maintenance is an important process in achieving high maintainability – both preventative maintenance and corrective maintenance.  Maintainability is a design consideration and maintenance is a consequence of that design.  Maintainability can be improved by paying proper attention to the following areas:

- Accessibility – Can the component and/or system be easily reached for repair or adjustments?  If not, how is the accessibility challenge mitigated?

- Visibility – Can the component and/or system being worked on visible or do special remote viewing measures be taken?

- Testability – Can proper testing enable faults to be predicted and/or detected and isolated to the necessary level of detail to permit cost-effective preventative and corrective maintenance to occur? Are ??

Yes, this is a critical part of Inspectability.  For components you can replace them proactively at an agreed upon % of their MTBF or predict failure and intercept it.

- Reliability Centered Maintenance (RCM) – Is there a discipline means of identifying preventive maintenance tasks?  Originally used in the aircraft industry, RCM utilizes information from the FMECA to identify items that are the most critical to system availability.  The resulting analysis can then be used identify and schedule preventative maintenance tasks on a scheduled, periodic basis to prevent failures while the equipment is in operation – this goes well beyond the routine maintenance activities such as lubrication and adjustments that are needed to keep systems in operation.

- Complexity – How many parts are used in the component and/or system?   Are the parts standard or special purpose?  Generally, simpler systems tend to be more reliable and maintainable than do complex ones.

- Standardization and Interchangeability – Can the failed or malfunctioning unit be swapped around or readily replaced by an identical unit with no need for recalibration? Standardization of systems, parts, tools, and procedures reduce the training necessary and the risk to readiness.  Modular designs also lend themselves to higher reliability and maintainability.