| Princeton Plasma Physics Laboratory Procedure |
| --- |
| Procedure Title: D-Site Work Permits |
| Number: D/DSITE-OP-AD-09 | Revision: 7 | Effective Date: (Ref. OP-AD-97) Expiration Date: (2 yr. unless otherwise stipulated) |
| Procedure Approvals |
| Author S. W. Langish | Date |
| ATI Al vonHalle | Date |
| RLM M. Williams | Date |
| Responsible Division: D-Site Caretaking |
| Procedure Requirements designated by RLM |
|  | Work Planning Form #______ (ENG-032) |  | Lockout/Tagout (ESH-016) |
|  | Confined Space Permit (5008, Sec. 8, Chap 5) |  | Lift Procedure (ENG-021) |
|  | Master Equip. List Mod (GEN-005) |  | ES&H Review (NEPA, IH, etc.) |
|  | RWP (HP-OP-20) |  | Independent Review |
|  | ATI Walkdown |  | Pre-job Brief |
|  | * Post-job Brief |  |  |
| D-Site Specific |
|  | D-Site Work Permit (OP-AD-09) |  | Door Permit (OP-G-93) |
|  | Tritium Work Permit (OP-AD-49) |  | T-MOD (OP-AD-03) |
|  | Pre-job brief (OP-AD-79) |  |  |
|  | ** DCA/DCN (OP-AD-104) #_____________ |  |  |

# •	Required for installations involving internal vacuum vessel installations, critical lifts, and for
the initial installation of repetitive work

**	OP-AD-104 was voided by procedure ENG-032.  However, DCAs that were open at the time of
adoption of ENG-032 are still considered valid for work approval purposes.

REVIEWERS (designated by RLM)

Accountable Technical Individual A. vonHalle

Test Director

Independent Reviewer

D-Site Shift Supervisor W. Blanchard, R. Camp, R. H. Carnevale, C. Gentile

NSTX

TFTR Caretaking

Vacuum

Tritium

Quality Assurance/Quality Control.

Maintenance and Operations Division

Energy Conversion System/Motor Control System

D&D HP/Rad Waste Coordinator

Environmental Restoration & Waste Management Division

D&D Mechanical/Vacuum

Environmental, Safety, & Health J. W. Anderson

Industrial Hygiene

Health Physics

D&D Construction Manager

| TRAINING (designated by RLM) |
| --- |
| No training required _____________ _ | Instructor ____ __ |
| Personnel (group, job title or individual name) | Read Only | Instruction Pre-job Briefing | Hands On |
| Users | ( |  |  |
| Training Rep. |
| RLM M. Williams |

# 1.0	PURPOSE

### The purpose of this procedure is to establish a system of Work Permits (WP) to control tasks within the D-Site Facility.  The Work Permit system is a means to control and coordinate work activities; maintain a safe working environment; implement rules for maintaining workplace cleanliness; and recording of tasks.  In addition, provisions for documenting the evolution of routine or minor activities are also included.

# 2.0	SCOPE

## 2.1	Applicability

### Work Permits are applicable at all times and shall be used to authorize work activities in the NSTX Test Cell (NTC), TFTR Test Cell (TFTR TC), Test Cell Basement (TCB), Tritium Area (TA), Mechanical Equipment Room (MER), Radioactive Waste Storage Facility (RWSF), and the D-site roof areas.  Work Permits are also applicable for work that may affect the Liquid Effluent Collection System (LECS), D-Site Stack, NTC, TFTR TC, TCB, MER, or Tritium Area.

## Requirements

### Except for access to the D-Site roofs, Work Permits are not required for the following activities provided personnel do not enter radiation or contamination fields:

- Inspections;

- Supervisory personnel exercising purely supervisory functions;

- Personnel performing routine startup, shutdown, surveillance, monitoring, or minor adjustment activities (when these activities do not require tools);

- Personnel performing safety inspections;

- Guided tour groups.

### 2.	While most activities require an approved Work Permit (Attachment II), Attachment I provides a method for documenting the evolution control requirements for minor or routine activities as an alternative to a run-copy procedure or IP.  Attachment I cannot be used where one or more of the following activities are involved:

- Interfacing to a working experimental vacuum system;

- Lockout/tagout of AC power above 120V/208;

- Tritium contaminated line breaks;

- Work in a radiation field (above 2.4 mrem/hr);

- Tritium contaminated water release or draining;

- Work that would make OER equipment inoperable (as described in 
OP-AD-77, HVAC, tritium stack and area monitors, and tritium systems);

- Use of materials with industrial hygiene hazards

- System removals from the TFTR TC, TCB, or TA.

## 2.2	Requirements (continued)

    - Specifically included for using Attachment I are work activities involving:

- Movement of material and equipment within a radiologically controlled area under an approved, current RWP.

- Relocation and field fittings of equipment

- Equipment troubleshooting and repair using approved safing and access procedures.

    - Activities approved under Attachment I should be at the highest level of assembly possible (to minimize the number of permits), and multiple tasks within the same work discipline may be grouped on a single permit with the concurrence of the D-Site Shift Supervisor.  If there are questions as to the appropriate permit to use, contact the D-Site Shift Supervisor (%163).

# 3.0	REFERENCES

- ESHD-5008	PPPL ES&H Manual

- ESH-16	Control of Hazardous Energy Sources via Lockout/Tagout of Energy Isolation Devices

- HP-OP-04,	Surface Contamination Surveys

- HP-OP-06,	Monitoring for Occupational Exposure to Airborne Tritium

- HP-OP-12,	Radiological Work Permit Procedure

- OP-AD-24	Control of Workplace Cleanliness Around the TFTR Machine

- OP-AD-39	TFTR Conduct of Operations

- OP-AD-44,	TFTR Rollover Procedure

- OP-AD-56	Control of Equipment and System Status

- OP-AD-68	Access to the Tritium Systems Area at D-Site

- OP-AD-77	Operating Equipment Requirements

- OP-AD-79,	Requirements for Performing Maintenance on Tritium Contaminated Equipment

- OP-AD-113,	Access to the Test Cell and Test Cell Basement - Post TFTR Operations

- OP-AD-115,	Moving Radioactive/Contaminated Material To/From D-Site

# 4.0	PROCEDURE

| 4.1 Job Supervisor | Identifies the need to do work in the NSTX Test Cell (NTC), TFTR Test Cell (TFTR TC), Test Cell Basement (TCB), Tritium Area, Mechanical Equipment Room (MER), Radioactive Waste Storage Facility (RSWF), or the D-site roof areas, or identifies activities that might affect these areas. Ensures that all workers are qualified for tasks that they will perform. |
| --- | --- |
|  | Completes the appropriate Work Permit as described in steps 3 through 5 and presents (or submits by fax at x2468 or electronically via email) the Work Permit to the D-Site Shift Supervisor. |
|  | Completes the following sections of Attachment II: General – identifies the Job Supervisor; identifies date and time of intended entry, and expected closeout date; any additional workers and their tools; and a description of the work. Indicates whether the activity is on the rollover schedule, and if QC or HP support are required (if QC or HP is needed for the job, notifies QC or HP prior to the start of the job). Location – identifies the location(s) of the work activites. Documentation – identifies the documents controlling the work activity (Work Planning Form, IP other Procedure, or Attachment I); indicates if Lockout/Tagout, RWP, Flame Permit, Door Permit, Tritium Release Permit, Lift Procedure, and/or Confined Space Permits are required. The Job Supervisor shall assure that all workers on the job are fully cognizant of all work area cleanliness and safety concerns. For MINOR Activities – Completes sections 1 through 7 of Attachment I. The NEPA status information may be obtained from the ES&H Division. T-MOD’s are available from the D-Site Shift Supervisor (%163). |

| 4.1 Job Supervisor (continued) |
| --- |
|  | The Job Supervisor signs and dates the WP. It is the responsibility of the RI to complete the WP in sufficient time prior to the anticipated start of work and to ensure that the D-Site Shift Supervisor or NSTX Construction Manager has reviewed and approved it. |
|  | At the conclusion of the activity or at the request of D-Site Caretaking, the Job Supervisor (or designee) closes out the WP by signing on the reverse side of the WP. In so doing, the Job Supervisor confirms that no un-surveyed material has been removed from the TC, TCB, or TA, that all tools have been removed and that all areas where work has been done are clean. |
| 4.2 QC | Assists in work activities as needed and signs the closeout portion of the WP as required. |
| 4.3 HP | Supplies D-Site Caretaking with Global Surveys and specific surveys, and radiation levels and stay times to be entered on the WP. |
|  | Writes special Radiation Work Permits (RWP’s) as needed, surveys material to be removed from the TFTR TC, TCB, TA, or the NSTX TC. Assists in the work activities as needed. Writes RWP’s for roof access as required by HP. |
|  | Performs surveys of the D-Site roof areas for radiation and contamination levels at HP’s discretion. |
|  | Assures that there are no HP concerns for D-Site roof access. |
|  | Signs the closeout portion of the WP as required. |

| 4.3 D-Site Shift Supervisor | Reviews the Job Supervisor portion of the WP for completeness and acceptability. In consultation with the Job Supervisor, modifies the WP as appropriate. |
| --- | --- |
|  | Completes the D-Site Shift Supervisor section of the work permit. The D-Site Shift can, at his/her discretion, extend work permit control to other areas or concerns, not specifically addressed on the permit, as conditions warrant. Additional concerns are addressed in the “Comment” field at the bottom of the permit. |
|  | The D-Site Shift Supervisor signs his approval of the WP. For work relevant to NSTX, the D-Site Shift Supervisor may request the NSTX Construction Manager to review and co-sign the work permit. Enters any comment relevant to the WP, including if the WP is for a non-standard area. |
|  | Assigns a WP# to the Work Permit and maintains the log. |
|  | Contacts the Job Supervisor to close out WP’s as necessary, and distributes WP’s for closeout signatures as needed. |
|  | Reviews completed and closed out WP’s and sends them to the Operations Center. |

# ACRONYMS

FCPC 	Field Coil Power Conversion

HP	Health Physics

HVAC	Heating, Ventilation, and Air Conditioning

MER	Mechanical Equipment Room

MG	Motor Generator

NBPC	Neutral Beam Power Conversion

NEPA	National Environmental Policy Act

NSTX	National Spherical Tokamak Experiment

OER	Operation Equipment Requirements

QC	Quality Control

RWP	Radiation Work Permit

TA	Tritium Area

TC	Test Cell

TCB	Test Cell Basement

TFTR	Tokamak Fusion Test Reactor

WP	Work Permit

# ATTACHMENT I

##### D-SITE WORK PERMIT (OP-AD-09)	Work Permit # ________

OP-AD-09 Attachment I can be employed to perform minor tasks associated with the following (mark as applicable);

(1)	Approved Work Planning Form (#)

(2)	Approved NEPA (#)

(3)	T-Mod (#)

(4)	Description of MINOR task to be performed:

(5)	Area/System control procedures

(6)			Date

System Engineer Approval

(7) 			Date

Designated Branch Head Approval

| D-SITE WORK PERMIT NO.: |
| --- |
| Job Supervisor MUST complete 1 through 22 |
| GENERAL |
| 1) Name of Job Supervisor: | Date: |
| 2) Names of additional workers? |
| 3) Tools? |
| 4) Description of work? |
| 5) Is task on the rollover schedule? | NO | YES |
| 6) HP required? | NO | YES |
| 7) QC required? | NO | YES |
| LOCATION/AREA |
| 8) TFTR | TC | TCB Location_______________ |
| Inside 102’ perimeter? | NO | YES Bays___________________ |
| D-SITE ROOF LECS STACK | RWP? HP Approval____________ |
| GALLERY Tritium Area | RWP? HP Approval____________ |
| MER RWSF | RWP? HP Approval____________ |
| *NSTX TC |  |  |
| *Does this NSTX job involve any material with a Radiation sticker? YES NO |
| *If yes, then all material must be surveyed by HP prior to leaving NTC. _______________ Job Supervisor |
| OTHER AREA ______________________________ |
| DOCUMENTATION |
| 9) Attachment I? |  |
| 10) Run Copy Procedure? | Proc# |
| 11) Work Planning Form? | WP # |
| 12) Installation Procedure? | IP # |
| 13) ESU Impairment Tag/FLAME Permit required? |  |
| 14) DOOR Permit required? |  |
| 15) CONFINED SPACE permit required? | CSP # |
| 16) RADIATION WORK permit required? | RWP # |
| 17) LIFT procedure required? | Lift Pro # |
| 18) T2 GASEOUS/WATER permit required? | OP-AD-79 |
| 19) Material being removed from TFTR TC or TCB? | If yes, then material must be surveyed. |
| 20) T2 line break or vent required? | OP-AD-79 |
| 21) Pre-job brief required? | OP-AD-79 |
| 22) SIGNATURE of Job Supervisor Individual/Date |  |
| To be completed by the D-Site Shift Supervisor |
| (a) Operating Equipment Requirements issues? |  |
| (b) Work in Radiation Area? | Rad. Level/Stay Time?______________ |
|  | Chirpers(SRD’s) Req’d if > 2.5 mr/hr |
| (c) D-Site Shift Supervisor |  |
| (d) Comments/Restrictions: |  |

WORK PERMIT CLOSEOUT

Task(s) complete (or secured) tools removed and area clean: Job Supervisor (or designee) Date

QC concerns satisfactory: QC (if required) Date

HP concerns satisfactory: HP (if required) Date

Closed Out by: D-Site Shift Supervisor Date

MAJOR TASK: e.g. interfacing to a working experimental vacuum system; Lockout/tagout of AC power above 120V; Activated or Tritium contaminated equipment or line breaks; Tritium contaminated water release or draining; Work on OER equipment (HVAC, tritium stack and area monitors, and tritium systems); Materials with industrial hygiene hazards; System removals from the TFTR Test Cell or Test Cell Basement. Material Surveys: Anything that was in a Radiologically Controlled Area (e.g. TFTR TC, TCB, TA, RWSF, etc.) must be surveyed.