Checking Guidelines for all models / drawings that will be released for fabrication

- All Intralink released objects must have a description. The description should all be in caps

- All objects should have a number – no names. The number should be of the form: se123-123.  A vendor part number or legitimate library part number may also be used.  Concept numbers such as smc123-123 (mc represents your initials) must be converted to se123-123 before the model is moved to the fabrication release level.

- Models should be moved out of our sketch areas and moved to the correct WBS Intarlink folder if the model represents the final released part.

- All parts should have a density specified. Common densities are shown in Table 1.

- All parts and assemblies should have the analysis, model analysis, model mass properties calculated based on the master rep.

- Make sure the “Insert Here” is located after the last feature or component in the model.

- Layers / Features should be placed on one layer only. Layers should be blanked and the status saved.

- Models should be check to assure that there are no warnings; frozen features, circular references, etc.

- Assembly models – Parts/components/subassemblies should not be placed on layers. Simplified reps should be used to control the display.

- Geometric datum(s) should be placed on a layer called 9_GEO.

If possible the following steps should also be taken:

- Any components that are suppressed should be removed from the model. If the component or feature needs to be suppressed we should understand why and try to work in the direction of removing the suppressed features/models.

- We should take a look at the layers and try to get some organization back to the layering scheme. Ex If we have several layers that deal with surfaces we should try and put them together. We have a layer called 6_all_surfaces. If a new layer has to do with surfaces try 6_new_surface. This way all the surface layers will be in the same location. The same for datum’s, point, axis etc…. To the extent possible we should try to minimize the no. of layers.

Table 1 - Common Material Densities

|  | MATERIAL | DENSITY |
| --- | --- | --- |
| Type | Full Description | lbs/in^3 |
|  |  | High |
| Metals | Aluminum alloys, 1000 series | 0.098 |
|  | Aluminum alloys, 2000 series | 0.102 |
|  | Aluminum alloys, 3000 series | 0.099 |
|  | Aluminumalloys, 5000 series | 0.098 |
|  | Aluminum alloys, 6000 series | 0.098 |
|  | Aluminum alloys, 7000 series | 0.102 |
|  | Aluminum, Casting alloys | 0.102 |
|  | Beryllium | 0.068 |
|  | Beryllium Copper | 0.298 |
|  | Brass, Cartridge | 0.308 |
|  | Brass, Free Cutting | 0.307 |
|  | Brass, Naval | 0.304 |
|  | Cast Iron, Grey, CL35 | 0.252 |
|  | Chromium | 0.260 |
|  | Copper OFHC | 0.323 |
|  | Gold, (99.95) | 0.698 |
|  | Iron, Pure | 0.284 |
|  | Inconel 625 | 0.305 |
|  | Inconel 718 | 0.296 |
|  | Lead & its alloys | 0.410 |
|  | Nickel-base superalloys | 0.322 |
|  | Bronzes, wrought | 0.321 |
|  | Platinum, (99.9) | 0.775 |
|  | Silver, Fine | 0.379 |
|  | Stainless Steels, cast | 0.294 |
|  | Stainless Steels, standard austenitic | 0.290 |
|  | Stainless Steel 304 | 0.290 |
|  | Stainless Steel 316 | 0.290 |
|  | Steel, Carbon Alloy | 0.283 |
|  | Tin | 0.289 |
|  | Titanium | 0.183 |
|  | Tungsten | 0.710 |
|  | Zinc | 0.258 |
|  | Zinc, Cast | 0.240 |
|  | Zirconium | 0.240 |
| non-metalics | Alumina-silica fibers | 0.099 |
|  | Boron carbide | 0.011 |
|  | E-glass fibers | 0.097 |
|  | Epoxies, reinf | 0.079 |
|  | Epoxies, unreinf | 0.051 |
|  | Glass fiber-epoxy composites | 0.075 |
|  | Plasatic foams, rigid, no. surf skin | 0.024 |
|  | Phenolics, comp | 0.072 |
|  | Polycrystalline glass | 0.094 |
|  | Polyimides, reinf | 0.069 |
|  | PVC | 0.056 |
|  | S-glass fibers | 0.090 |
|  | Silicon | 0.084 |
| Data taken from Material Engineering - Comparison of Materials, December 1987 |