Applicability

This procedure is applicable to the entire NCSX Project.

Introduction

The NCSX ProE/INTRALINK Users Guide provides the processes by which a ProE drawing is promoted from a “conceptual design” status through a “release for fabrication” status. Rather than repeat that process for each step in the promotion process, this procedure will focus on the final step where a draw or set of drawing have advanced to the stage where they are now ready to be released for fabrication and/or installation.

In accordance with the ProE/INTRALINK Users Guide, drawings ready for release “Release for Fabrication” status are to converted to pdf before they are signed electronically and the “Release for Fabrication/Installation” stamp applied.  The NCSX Electronic Signature Procedure PROC-005 outlines that process in detail, but this procedure will apply specifically to the final review and sign-offs of a “Release for Fabrication” drawing.

Part A of this procedure addresses the final review and concurrence processes and documentation performed within INTRALINK to ensure that the necessary and appropriate technical and management reviews of the drawing or drawings is completed.  Part B of this procedure then addresses the final process of obtaining Design Supervisor’s approval and the placement of the “Release for Fabrication” stamp on the impacted drawings.

Referenced Documents

| NCSX_GUID-PRO | NCSX Pro/INTRALINK Users Guide |
| --- | --- |
| NCSX-PROC-005 | Electronic Signatures |
| NCSX-PROC-004 | NCSX Work Planning |
| PPPL Engineering Procedure 010 | Control of Drawings, Software, and Firmware |

Procedure

- Final Review and Approvals of the Drawing Ready for Fabrication

| Responsibility | Action |
| --- | --- |
| Designer | Notifies the Design Integration Manager that a drawing or drawing package is ready for promotion to the fabrication stage. |
| Design Integration Manager | Coordinates with the Cognizant Engineer to develop a list of names of those individuals who need to review and approve the drawing or drawing package. Normally, this list will occur the following personnel: Independent Checker Authorized Weld Engineer (for mechanical drawings) Design Integration Manager (if integration activities are involved) Cognizant Engineer Note: If the Cognizant Engineer desires others to review the drawing package, it is his or her responsibility to have the drawings reviewed by those individuals and comments provided to him or her before the Cognizant Engineer signs the drawing within INTRALINK. |
|  | Ensures that INTRALINK sends out the necessary automated e-mails notifying the above named individuals (Checker, Weld Engineer, Design Integration Manager, and Cognizant Engineer). The approval sequence should go in order such that the Checker reviews and signs prior to the Weld Engineer who then signs before the Design Integration Manager. |
| Reviewers | Reviews and comments (as appropriate) on the drawings. If there are comments, the reviewer rejects the drawing within INTRALINK and provides reasons for his or her rejection of the drawing. The drawing is then returned to the Designer within INTRALINK and the process starts all over at Step A.1. until such time that all reviewers have approved the drawing within INTRALINK. Once the drawing is fully approved by the reviewers, including the Cognizant Engineer, proceed to Step A.7. |
| Cognizant Engineer | Once he or she has signed the drawing within INTRALINK, ensures that the drawing and all associated parts and assemblies are automatically moved into the “Fabrication Release” level within INTRALINK and that INTRALINK has automatically notified the Designer that the package is approved within INTRALINK. Notifies the Design Integration Manager that the drawing package is approved within INTRALINK. |
| Design Integration Manager | Ensures that the necessary review and approval documentation is retained with INTRALINK. Proceeds to Section B for the final approval and sign-off. |

- Final Sign-Off of Release for Fabrication Drawings

| Responsibility | Action |
| --- | --- |
| Designer | When notified by INTRALINK via automatic e-mail that the drawing/drawing package has been approved within INTRALINK, converts ProE drawing to PDF format and enters electronic signature block for the Design Supervisor or his designee (Branch Head or Division Manager) per NCSX Procedure 005. Places drawing in PDF format into the appropriate FTP folder. Notifies Design Supervisor that the drawing is posted and ready for his electronic signature. |
| Design Supervisor (or Designee – see B.1.) | Verifies that the appropriate drawing standards were followed, that applicable ECNs were incorporated, etc., and that the drawing package was approved within INTRALINK. If not, notifies the Designer and rejects the drawing. If INTRALINK documentation is complete and appropriate, proceeds to Step B.5. Signs the drawing as per NCSX Procedure 005 and places the “Release for Fabrication/Installation” stamp on the drawing. Places the approved and signed drawing/drawing package into the Released Drawing folder within INTRALINK and notifies the Design Integration Manager that the drawing/drawing package is approved. |

Attachment 1 – The NCSX Drawing Release and Signature Process