Record of Revisions

| Revision | Date | Description of Changes |
| --- | --- | --- |
| 0-dF | 4/25/2005 | Initial Issue |

Applicability

This procedure is applicable to the entire NCSX Project.

Introduction

The NCSX ProE/INTRALINK Users Guide provides the processes by which a electronic 3D Computer Aided Design and Drafting(CADD) model, assembly, part, or drawing is promoted from a “conceptual design” status through a “release for fabrication” status. While this procedure will focus on Pro/E mechanical drawings as a reference, the processing and approval of other CADD-generated drawings such as AUTOCAD for electronic drawings is very similar within the INTRALINK process. Rather than repeat the process for each step in the promotion process, this procedure will focus on the final step where a draw or set of drawing have advanced to the stage where they are now ready to be released for fabrication and/or installation.  It will then address the process by which these are revised.

Electronic models are the basic building block of the ProE CAD system.  From these 3D models all the associated parts and assemblies with the exception of standard or “library” parts such as fasteners, washers, etc) and 2D drawings are derived.  The 3D models, parts, assemblies, and 2D drawings are all mutually promoted to the same release level as each other.  This will also include data curves if they are needed or skeleton parts (used for making port cuts).  However, STEP or IGES files are not stored in the promotion process since they are directly obtained from the approved data files that are in the promotion process.  Only final 2D drawings are “physically” signed in a pdf format using the procedure described in the NCSX Electronic Signature Procedure PROC-005.  All others will be electronically reviewed and approved using the inherent ProE/INTRALINK database processes and procedures.  The ProE/INTRALINK database also provides configuration control processes for 3D models, parts, assemblies, and 2D drawings.

Referenced Documents

| Document Number | Document Title |
| --- | --- |
| NCSX-PLAN-CMP | Configuration Management Plan |
| NCSX-GUID-PRO/INTR | Pro/INTRALINK Users Guide |
| NCSX-PROC-002 | Configuration Control |
| NCSX-PROC-005 | Electronic Signatures |
| NCSX-PROC-009 | Requests for Deviations |
| PPPL Engineering Procedure 010 | Control of Drawings, Software, and Firmware |
| PPPL-DRFT-001 | PPPL Drafting Standard |

Procedure

Final Review and Approvals of Models, Assemblies, Part, and Drawings Ready for Fabrication

Revision of “Release for Fabrication” Drawings

Once a drawing is promoted and approved in a “Release for Fabrication” status, the drawing comes under configuration control.  In accordance with the NCSX Configuration Control process outlined in the NCSX Configuration Management Plan (NCSX-PLAN-CMP) and its accompanying NCSX Procedure (NCSX-PROC-002), once any document is under configuration control, an Engineering Change Proposal (ECP) is required to initiate and authorize a change, unless the NCSX Systems Engineering Manager, after consultation with the NCSX Engineering Manager specifically authorizes a change without an ECP (generally only limited to editorial and minor changes).   Per the applicable PPPL Engineering Procedure (ENG-010), an Engineering Change Notice (ECN) is also required to document and authorize changes to drawings already in a “Release for Fabrication” status and/or add new drawings needed to fully implement and document the authorized change.  The procedure that follows provides the step-by-step process.

- Annotation of Drawings with RFD or NCR Identification

Attachments

1 – The NCSX Drawing Release and Signature Process

2 – Request to Promote Form and Process

3 – NCSX ECN Forms

These attachments are intended for information and illustration of the processes described in this procedure.

Forms are located at:

http://ncsx.pppl.gov/SystemsEngineering/Config_Mgmt/ECNs/ECN_StatusIndex.htm

# Text boxes

Designer notifies the Design Integration Manager that a drawing package (model, parts, assemblies, and drawings) is ready for promotion to the “Release for Fabrication” stage.

Design Integration Manager coordinates with the Cognizant Engineer to develop a list of names of those individuals who need to review and approve the drawing package.  Normally, this list will include at a minimum following personnel:

- Independent Checker

- Authorized Weld Engineer (for mechanical drawings if required)

- Design Integration Manager

- Cognizant Engineer /WBS Manager

NOTE:  The Cognizant Engineer may request additional reviewers be added as appropriate.

Once list of reviewers identified, the Design Integration Manager establishes a release scheme within INTRALNK to identify the appropriate reviewers for the approval process.

NOTE:  Once the release scheme is defined, INTRALINK will automatically transmit e-mail notification to the reviewer list that the affected drawing package(s) are ready for review and approval.

1

1

Reviewers  receive INTRALINK e-mail notification and review and comment (as appropriate) on the model and assures that all requited parts, assemblies and drawings are in the package that are up for approval.

Comments?

Yes

No

Reviewer rejects drawing within INTRALINK and provides reason for the rejection.

Designer receives comment(s) from the reviewers and revises drawings and restarts review process from the beginning.  This process is repeated until all reviewers have approved the drawing package within INTRALINK.

Reviewers approve drawing package within INTRALINK. Once fully approved, including by the Cogninzant Engineer, INTRALINK automatically notifies the Designer.

Designer converts drawing(s) to pdf, and establishes the PPPL Drafting Supervisor signature block and defines the proper security per the applicable NCSX Procedure (NCSX-PROC-005).

Note: INTRALINK automatically notifies the identified reviewers that the drawing has been approved and is ready for final sign-off by the Design Supervisor or his authorized designee.

END

When all the reviewers have approved the drawing package without comment.

2

2

Design Integration Manager receives INTRALINK notice of drawing package approvals, confirms that they are in the proper ProE/INTRALINK files, and then posts pdf drawings in the appropriate folder and then notifies the Drafting Supervisor that the pdf drawing(s) are ready for signature.

Drafting Supervisor (or designee) verifies that the appropriate drawing standards were followed and that the drawing package was approved within INTRALINK.

- If not correct, notifies the Design Integration Manager and Designer and rejects the drawing. Designer will then have to correct drawing package and restart the review and approval cycle again.

- If INTRALINK documentation is complete and appropriate:

  - Places the “Release for Fabrication/Installation” stamp on the drawing(s) and signs the drawing(s) in the signature block area of the stamp as per NCSX-PROC-005;

  - Places the approved pdf drawings into the Released Drawing folder in INTRALINK; and

  - Notifies the Design Integration Supervisor that the drawing(s) is approved.

END

1

Systems Engineering Support Manager notifies initiator of the ECP, other NCSX Project personnel, and PPPL Drafting Supervisor that an ECP that impacts an approved drawing(s) has been approved or not approved.

If ECP not required on ECP is approved, Initiator prepares ECN per ECN-010 using the NCSX ECN Form (slightly modified form) and forwards to the Systems Engineering Support Manager

Systems Engineering Support Manager reviews ECN and:

  - If not complete, returns to Originator for rework until such time that the ECN is complete; or

  - If complete, requests ECN number from the Drafting Supervisor, annotates ECN with that number, converts ECN to pdf format, and obtains signature approvals per PROC-005.  When ECN fully signed:

  - Forwards completed ECN to the Drafting Supervisor for his records along with a copy of the implementing ECP:

  - Notifies the Designer and Design Integration Manager that the ECN has been approved; and

  - Posts the approved ECP (as approprate) and ECN on the NCSX Engineering Web.

Designer updates drawing package to reflect the ECP and ECN, including revision number and processes per the review and approval procedures found in Section A of this Procedure. Iterates this drawing package until fully approved and posted in the  appropriate INTRALINK folders.

END

Initiator notifies Systems Engineering Support Manager of a proposed change.

Systems Engineering Manager, after consultation with the NCSX Engineering Manager, determines if an ECP is needed.

NOTE: Minor editorial or other minor changes may not require an ECP

ECP Required?

Yes

No

Initiator prepares ECP and Systems Engineering Support Manager processes ECP per PROC-002.

1

END

Models and Drawings updated per Section C of this procedure.

The next time the Pro/E model or drawing is revised, the Design Integration Manager ensures that the associated pdf drawing and the approved RFDs and NCRs are incorporated.

Design Integration Manager copies impacted pdf drawings and annotates them with an identifier indicating that a RFD or NCR has been approved for this particular drawing.

- PDF drawing will be labeled same as the source Pro/E drawing with the exception that a Alphabetic designator (e.g., SEXXXX-00-A)will be utilized to clearly identify that the pdf drawing  has been modified.

- Annotation should provide sufficient information to assist the reader in understanding the general scope of the RFD or NCR.

- Processes pdf drawing for signature per Section A of this procedure.

END

Process revision to models and drawings per Section B of this procedure.

Update Drawings

Annotate Drawings

Update or Annotate Drawings?

RFD (PROC-009) or NCR (QA-005) processed and approved.