From: Hutch Neilson

Sent: Tuesday, November 20, 2007 9:57 PM

To: Michael R. Kalish

Cc: Michael C. Zarnstorff; Phil Heitzenroeder; Subrahmanya Ramakrishnan; Arthur W. Brooks; Thomas G. Brown

Subject: Trim Coil requirements

Mike,

Following up on the recent peer review, here is the requested

guidance regarding trim coil requirements:

1.  Response time / voltage:  zero to 20 kA-turn in 20 ms (Strawman)  Please advise on the voltage and force implications before going too far with this.

2.  Dimensional accuracy:  Fabrication tolerance: ±1/4 in.; Positioning tolerance: ±1/2 in.   Record as-built dimensions.

3.  Midplane coils:  examine the feasibility of adding two coils straddling the midplane at the C-C joints.  One coil on each side of

the joint.

Hutch