A.1 Initial Operation

A.1.1 Coil Set Definition

A.1.1.1 Current Centroid Locations

Coil centroids are defined by the TBD coil set.

A.1.1.2 Turns per Coil

|  | M1 |  | M2 |  | M3 |  | PF1A | PF4 | PF6 | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Turns |  | 22 |  | 22 |  | 20 | 48 | 80 | 14 | 1 |

A.1.2 Coil Inductance Matrix (Henries)

|  | M1 | M2 | M3 | PF1A | PF4 | PF6 | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- |
| M1 | 1.50E-02 | 3.42E-03 | 1.53E-03 | -2.18E-05 | 1.34E-04 | -3.10E-04 | -1.79E-05 |
| M2 | 3.42E-03 | 1.12E-02 | 2.84E-03 | 5.19E-06 | -1.40E-05 | -6.89E-05 | -1.19E-05 |
| M3 | 1.53E-03 | 2.84E-03 | 9.76E-03 | 4.14E-05 | -1.84E-04 | -6.88E-05 | -9.55E-06 |
| PF1A | -4.05E-05 | 1.62E-05 | 7.58E-05 | 8.22E-04 | 8.14E-05 | 5.35E-05 | 3.97E-06 |
| PF4 | 1.34E-04 | -1.40E-05 | -1.84E-04 | 8.14E-05 | 1.52E-02 | 5.90E-04 | 1.73E-05 |
| PF6 | -3.10E-04 | -6.89E-05 | -6.88E-05 | 5.35E-05 | 5.90E-04 | 6.24E-03 | 3.46E-05 |
| Plasma | -1.79E-05 | -1.19E-05 | -9.55E-06 | 3.97E-06 | 1.73E-05 | 3.46E-05 | 2.68E-06 |

A.1.3 Reference Scenario Data

A.1.3.1 Reference Equilibria (amp-turns per coil)

| Equlibrium ID | M1 | M2 | M3 | PF1A | PF4 | PF6 | Plasma |  | Comment |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 8 | 2.00E+05 | 2.00E+05 | 1.82E+05 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0 |  | First Plasma S1 |
| 9 | 2.00E+05 | 2.00E+05 | 1.82E+05 | 0.00E+00 | 0.00E+00 | 0.00E+00 | -26000 |  | First Plasna S2 |

A.1.3.2 Current Waveforms

Conductor currents are given in amperes. Maxima are shown in blue, minima in red.

| 0.5T First Plasma Scenario | t(s) |  | M1 | M2 | M3 | PF1A | PF4 | PF6 | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | -4.000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | 0.000 | 9115 | 9115 | 9115 | 0 | 0 | 0 | 0 |
|  |  | 0.050 | 9115 | 9115 | 9115 | 0 | 0 | 0 | 0 |
|  |  | 0.120 | 9115 | 9115 | 9115 | 18109 | 2947 | 227 | -26068 |
|  |  | 0.123 | 9115 | 9115 | 9115 | 18466 | 3005 | 231 | -26068 |
|  |  | 0.130 | 9115 | 9115 | 9115 | 19299 | 3141 | 241 | -26068 |
| Maximum |  |  | 9115 | 9115 | 9115 | 19299 | 3141 | 241 | 0 |
| Minimum |  |  | 0 | 0 | 0 | 0 | 0 | 0 | -26068 |
| I2t (A2-s) |  |  | 2.71E+08 | 2.74E+08 | 2.67E+08 | 6.04E+07 | 6.02E+06 | 5.40E+04 |  |
| tESW (s) |  |  | 3.26 | 3.30 | 3.21 | 0.16 | 0.61 | 0.93 |  |

| Field Line Mapping Scenario | t(s) |  | M1 | M2 | M3 | PF1A | PF4 | PF6 | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | -0.300 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | 0.000 | 1823 | 1823 | 1823 | 0 | 0 | 0 | 0 |
|  |  | 0.100 | 1823 | 1823 | 1823 | 0 | 0 | 0 | 0 |
|  |  | 0.200 | 1823 | 1823 | 1823 | 0 | 0 | 0 | 0 |
|  |  | 2.600 | 1823 | 1823 | 1823 | 0 | 0 | 0 | 0 |
|  |  | 10.100 | 1823 | 1823 | 1823 | 0 | 0 | 0 | 0 |
| Maximum |  |  | 1823 | 1823 | 1823 | 0 | 0 | 0 | 0 |
| Minimum |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| I2t (A2-s) |  |  | 3.61E+07 | 3.59E+07 | 3.65E+07 | 0.00E+00 | 0.00E+00 | 0.00E+00 |  |
| tESW (s) |  |  | 10.86 | 10.81 | 10.98 | 0.00 | 0.00 | 0.00 |  |

| Summary |  | M1 | M2 | M3 | PF1A | PF4 | PF6 | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Maximum |  | 9115 | 9115 | 9115 | 19299 | 3141 | 241 | 0 |
| Minimum |  | 0 | 0 | 0 | 0 | 0 | 0 | -26068 |
| Max I2t (A2-s) |  | 2.71E+08 | 2.74E+08 | 2.67E+08 | 6.04E+07 | 6.02E+06 | 5.40E+04 |  |
| tESW (s) at max current |  | 3.26 | 3.30 | 3.21 | 0.16 | 0.61 | 0.93 |  |

A.1.3.3 Temperature History

Coil temperatures are in Kelvin. Maxima are shown in blue.

| 0.5T First Plasma Scenario | t(s) |  | M1 | M2 | M3 | PF1A | PF4 | PF6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | -4.000 | 85 | 85 | 85 | 85 | 85 | 85 |
|  |  | 0.000 | 89 | 89 | 89 | 85 | 85 | 85 |
|  |  | 0.050 | 89 | 89 | 89 | 85 | 85 | 85 |
|  |  | 0.120 | 89 | 89 | 89 | 85 | 85 | 85 |
|  |  | 0.123 | 89 | 90 | 89 | 85 | 85 | 85 |
|  |  | 0.130 | 89 | 90 | 89 | 85 | 85 | 85 |
|  |  | 3.311 | 90 | 91 | 90 | 86 | 85 | 85 |
| Dissipated Energy (J) |  | 0.000 | 2.81E+06 | 2.79E+06 | 2.27E+06 | 4.66E+04 | 2.22E+04 | 1.82E+02 |
|  |  |  |  |  |  |  |  | 7.95E+06 |

| Field Line Mapping Scenario | t(s) |  | M1 | M2 | M3 | PF1A | PF4 | PF6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | -0.300 | 85 | 85 | 85 | 0 | 0 | 0 |
|  |  | 0.000 | 85 | 85 | 85 | 0 | 0 | 0 |
|  |  | 0.100 | 85 | 85 | 85 | 0 | 0 | 0 |
|  |  | 0.200 | 85 | 85 | 85 | 0 | 0 | 0 |
|  |  | 2.600 | 85 | 85 | 85 | 0 | 0 | 0 |
|  |  | 10.100 | 86 | 86 | 86 | 0 | 0 | 0 |
|  |  | 11.422 | 86 | 86 | 86 | 0 | 0 | 0 |
| Dissipated Energy (J) |  | 0.000 | 3.50E+05 | 3.41E+05 | 2.91E+05 | 0.00E+00 | 0.00E+00 | 0.00E+00 |
|  |  |  |  |  |  |  |  | 9.82E+05 |

| Summary |  | M1 | M2 | M3 | PF1A | PF4 | PF6 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Max Final Temperature |  | 90 | 91 | 90 | 86 | 85 | 85 |
| Max Dissipated Energy (J) |  | 2.81E+06 | 2.79E+06 | 2.27E+06 | 4.66E+04 | 2.22E+04 | 1.82E+02 |
|  |  |  |  |  |  | 7.95E+06 |

A.1.3.4 Electrical Power Requirements

Initial Power Supply and Cabling Requirements and Modeling Assumptions For the First Plasma and Field Line Mapping Scenarios, DC power will be supplied by existing C-site supplies. Power supply requirements for these reference scenarios have been calculated based on the following assumptions:

[1] All coils of the same type (e.g. all M1 coils) are connected in series. 	All coils in the same circuit are connected in series.  Circuit configurations are defined in the table below.

[2] No allowance was made for current limiting reactors in any of the circuits. It was assumed that the bus inductance was negligible.

[3] The following bus resistances (in milli-ohms) were assumed: M1 (4.04), M2/3 (3.17), PF1A (2.37), PF4 (10.4), PF6 (5.57).

[4] DC ratings were calculated based on a 15 minute pulse repetition rate.

| Initial capability required | 0.5T First Plasma 0.1T Field Line Mapping | M1 | M2/3 | PF1A | PF4 | PF6 |
| --- | --- | --- | --- | --- | --- | --- |
| 9 MW | Max I2t (A2-s) | 2.7E+08 | 2.7E+08 | 6.0E+07 | 6.0E+06 | 5.4E+04 |
| 101 MVA | tESW (s) | 3.26 | 3.30 | 0.16 | 0.61 | 0.93 |
| 10 MJ | Required DC rating (A) | 549 | 552 | 259 | 82 | 8 |
|  |  |  |  |  | UCLA and |  |
|  |  |  | 2 R-5 in |  | R-5 in |  |
|  | Power Supply | R-10 | parallel | R-20 | series | R-5 |
|  | Voltage Rating (V) | 200 | 300 | 500 | 800 | 300 |
|  | Current Rating (kA) | 10 | 10 | 20 | 5 | 5 |

A.1.4 Pulsed Heat Loads

Pulsed heat loads calculated on the basis of the worst case scenario for each coil.

A.1.4.1 Maximum Temperature and Energy Deposition

| Pulsed heat Loads | M1 | M2 | M3 | PF1A | PF4 | PF6 |
| --- | --- | --- | --- | --- | --- | --- |
| Initial Temperature (K) | 85 | 85 | 85 | 85 | 85 | 85 |
| Max Temperature (K) | 90 | 91 | 90 | 86 | 85 | 85 |
| Energy Deposited (J) | 2.81E+06 | 2.79E+06 | 2.27E+06 | 4.66E+04 | 2.22E+04 | 1.82E+02 |
|  |  |  |  |  |  | 7.95E+06 |

A.1.4.2 LN2 Consumption During Pulsed Operation

| Max LN2 Consumption |  | Tsat (K) Psat (MPa) hfg (kJ/kg) Mass per pulse (kg) | Density (kg/m3) (m3/kg) | Volume (m3) (liters) | (gallons) |
| --- | --- | --- | --- | --- | --- |
| Per shot Time between shots (minutes) Hours per day Full pwr shots per day Operating days per week | 15 8 32 5 | 78 0.1093654 198.3014 40.071935 | 805.73502 0.0012411 | 0.049733391 49.733391 | 13 per shot 420 per day 2102 per wk |

A.1.4.2 LN2 Delivery Requirements

|  | Gallons per Truck 6500 | Trucks |
| --- | --- | --- |
| Pulsed heat loads only |  |  |
| Max pulsed heat loads |  | 0.32 per week |
| Field line mapping |  | 0.06 per week |
| First Plasma |  | 0.04 per week |
| Parasitic loads only |  |  |
| Normal |  | 2.12 per week |
| 150C Bakeout |  | 2.86 per week |
| Cooldown only |  | 1.63 |

A.2 Full Operating Capability

A.2.1 Coil Set Definition

A.2.1.1 Current Centroid Locations

Coil centroids are defined by the c08r00 coil set.

A.2.1.2 Turns per Coil

|  | M1 |  | M2 |  | M3 | PF1 |  | PF2 | PF3 |  | PF4 | PF5 |  | PF6 |  | TF |  | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Turns |  | 22 |  | 22 | 20 |  | 72 | 72 |  | 72 | 80 |  | 24 |  | 14 |  | 12 | 1 |

A.2.2 Coil Inductance Matrix (Henries)

|  | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M1 | 1.50E-02 | 3.42E-03 | 1.53E-03 | -6.07E-05 | 1.01E-05 | 4.16E-05 | 1.34E-04 | -2.52E-04 | -3.10E-04 | 9.54E-03 | -1.79E-05 |
| M2 | 3.42E-03 | 1.12E-02 | 2.84E-03 | 2.44E-05 | -1.14E-05 | -5.58E-06 | -1.40E-05 | -4.97E-05 | -6.89E-05 | 7.35E-03 | -1.19E-05 |
| M3 | 1.53E-03 | 2.84E-03 | 9.76E-03 | 1.14E-04 | -9.45E-06 | -3.87E-05 | -1.84E-04 | -2.26E-04 | -6.88E-05 | 5.19E-03 | -9.55E-06 |
| PF1 | -6.07E-05 | 2.44E-05 | 1.14E-04 | 2.99E-03 | 4.82E-04 | 7.20E-05 | 1.47E-04 | 1.67E-04 | 1.18E-04 | 0.00E+00 | 8.92E-06 |
| PF2 | 1.01E-05 | -1.14E-05 | -9.45E-06 | 4.82E-04 | 2.58E-03 | 4.33E-04 | 3.22E-04 | 1.75E-04 | 1.14E-04 | 0.00E+00 | 6.78E-06 |
| PF3 | 4.16E-05 | -5.58E-06 | -3.87E-05 | 7.20E-05 | 4.33E-04 | 2.57E-03 | 1.14E-03 | 1.81E-04 | 1.04E-04 | 0.00E+00 | 4.40E-06 |
| PF4 | 1.34E-04 | -1.40E-05 | -1.84E-04 | 1.47E-04 | 3.22E-04 | 1.14E-03 | 1.52E-02 | 1.14E-03 | 5.90E-04 | 0.00E+00 | 1.82E-05 |
| PF5 | -2.52E-04 | -4.97E-05 | -2.26E-04 | 1.67E-04 | 1.75E-04 | 1.81E-04 | 1.14E-03 | 1.28E-02 | 3.49E-03 | 0.00E+00 | 4.81E-05 |
| PF6 | -3.10E-04 | -6.89E-05 | -6.88E-05 | 1.18E-04 | 1.14E-04 | 1.04E-04 | 5.90E-04 | 3.49E-03 | 6.24E-03 | 0.00E+00 | 3.97E-05 |
| TF | 9.54E-03 | 7.35E-03 | 5.19E-03 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 4.90E-02 | 1.51E-06 |
| Plasma | -1.79E-05 | -1.19E-05 | -9.55E-06 | 8.92E-06 | 6.78E-06 | 4.40E-06 | 1.82E-05 | 4.81E-05 | 3.97E-05 | 1.51E-06 | 2.68E-06 |

A.2.3 Reference Scenario Data

A.2.3.1 Reference Equilibria (amp-turns per coil)

| Equlibrium ID | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF | Plasma |  | Comment |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 7.63E+05 | 7.10E+05 | 6.38E+05 | 0.00E+00 | 0.00E+00 | 3.05E+05 | 2.40E+05 | 2.03E+05 | -1.05E+05 | -4.26E+04 | 0 |  | iota>0.5 |
| 2 | 6.95E+05 | 7.06E+05 | 6.21E+05 | 0.00E+00 | 0.00E+00 | 1.60E+05 | -1.92E+05 | 2.42E+04 | 1.07E+04 | -1.33E+04 | 0 |  | iota<0.5 |
| 3 | 6.95E+05 | 7.06E+05 | 6.21E+05 | 0.00E+00 | 0.00E+00 | 1.60E+05 | -1.92E+05 | 2.05E+04 | 7.53E+04 | -1.33E+04 | -120000 |  | 120kA, zero beta |
| 4 | 6.59E+05 | 6.54E+05 | 5.43E+05 | 0.00E+00 | 0.00E+00 | 1.05E+05 | -3.54E+05 | 5.58E+04 | 9.00E+04 | 4.53E+04 | -179000 |  | 179kA, full beta |
| 5 | 6.82E+05 | 6.40E+05 | 5.78E+05 | 0.00E+00 | 0.00E+00 | -1.30E+06 | -1.50E+06 | 1.07E+05 | 6.12E+04 | 2.62E+04 | -320000 |  | 320kA, zero beta |
| 6 | 6.69E+05 | 6.44E+05 | 5.57E+05 | 0.00E+00 | 0.00E+00 | -1.14E+05 | -2.09E+05 | -3.27E+05 | 2.60E+05 | 3.77E+04 | -160000 |  | 160kA, zero beta |
| 7 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 0.00E+00 | 1.94E+05 | 0 |  | 0.5T TF |

A.2.3.2 Current Waveforms

Conductor currents are given in amperes. Maxima are shown in blue, minima in red.

| 1.7T Ohmic Scenario | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.700 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 0.000 | 34673 | 32277 | 31908 | -23438 | -23438 | -14478 | -4495 | 7293 | -8195 | -3548 | 0 |
|  | 0.100 | 34673 | 32277 | 31908 | -23438 | -23438 | -14478 | -4495 | 7293 | -8195 | -3548 | 0 |
|  | 0.140 | 31611 | 32115 | 31058 | -14475 | -14475 | -9334 | -7030 | 135 | 4932 | -1106 | -120052 |
|  | 0.240 | 31611 | 32115 | 31058 | -10963 | -10963 | -6531 | -5907 | 309 | 5041 | -1106 | -120052 |
|  | 0.440 | 31611 | 32115 | 31058 | -3941 | -3941 | -924 | -3661 | 657 | 5257 | -1106 | -120052 |
| Maximum |  | 34673 | 32277 | 31908 | 0 | 0 | 0 | 0 | 7293 | 5257 | 0 | 0 |
| Minimum |  | 0 | 0 | 0 | -23438 | -23438 | -14478 | -7030 | 0 | -8195 | -3548 | -120052 |
| I2t (A2-s) |  | 1.19E+09 | 1.11E+09 | 1.05E+09 | 3.30E+08 | 3.31E+08 | 1.36E+08 | 2.24E+07 | 2.79E+07 | 4.56E+07 | 1.07E+08 |  |
| tESW (s) |  | 0.99 | 1.07 | 1.03 | 0.60 | 0.60 | 0.65 | 0.45 | 0.52 | 0.68 | 8.52 |  |

| 1.7T High Beta Scenario | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.700 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 0.000 | 34673 | 32277 | 31908 | -14660 | -14660 | -7469 | -1688 | 7728 | -7924 | -3548 | 0 |
|  | 0.100 | 34673 | 32277 | 31908 | -14660 | -14660 | -7469 | -1688 | 7728 | -7924 | -3548 | 0 |
|  | 0.140 | 31611 | 32115 | 31058 | -5697 | -5697 | -2325 | -4223 | 570 | 5203 | -1106 | -120052 |
|  | 0.240 | 29814 | 29625 | 27016 | -6146 | -6146 | -3461 | -6371 | 2009 | 6213 | 3760 | -178272 |
|  | 0.440 | 29814 | 29625 | 27016 | -5444 | -5444 | -2901 | -6147 | 2044 | 6235 | 3760 | -178272 |
| Maximum |  | 34673 | 32277 | 31908 | 0 | 0 | 0 | 0 | 7728 | 6235 | 3760 | 0 |
| Minimum |  | 0 | 0 | 0 | -14660 | -14660 | -7469 | -6371 | 0 | -7924 | -3548 | -178272 |
| I2t (A2-s) |  | 1.15E+09 | 1.04E+09 | 9.44E+08 | 1.25E+08 | 1.26E+08 | 3.59E+07 | 2.70E+07 | 3.25E+07 | 4.87E+07 | 1.75E+08 |  |
| tESW (s) |  | 0.95 | 1.00 | 0.93 | 0.58 | 0.58 | 0.64 | 0.67 | 0.54 | 0.78 | 12.38 |  |

| 2T High Beta Scenario | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.850 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 0.000 | 37190 | 37783 | 36538 | -14615 | -14615 | -9054 | -7498 | 460 | 453 | -1301 | 0 |
|  | 0.050 | 37190 | 37783 | 36538 | -14615 | -14615 | -9054 | -7498 | 460 | 453 | -1301 | 0 |
|  | 0.097 | 37190 | 37783 | 36538 | -6931 | -6931 | -2919 | -5041 | 660 | 6114 | -1301 | -141238 |
|  | 0.192 | 35075 | 34852 | 31783 | -7540 | -7540 | -4319 | -7595 | 2348 | 7300 | 4424 | -209732 |
|  | 0.197 | 35075 | 34852 | 31783 | -7522 | -7522 | -4305 | -7589 | 2349 | 7300 | 4424 | -209732 |
| Maximum |  | 37190 | 37783 | 36538 | 0 | 0 | 0 | 0 | 2349 | 7300 | 4424 | 0 |
| Minimum |  | 0 | 0 | 0 | -14615 | -14615 | -9054 | -7595 | 0 | 0 | -1301 | -209732 |
| I2t (A2-s) |  | 1.28E+09 | 1.27E+09 | 1.15E+09 | 1.41E+08 | 1.40E+08 | 5.74E+07 | 5.20E+07 | 2.24E+06 | 1.20E+07 | 2.36E+08 |  |
| tESW (s) |  | 0.93 | 0.89 | 0.86 | 0.66 | 0.65 | 0.70 | 0.90 | 0.41 | 0.23 | 12.06 |  |

| 1.2T Long Pulse Scenario | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.500 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 0.000 | 24475 | 22784 | 22523 | -14066 | -14066 | -8241 | -2380 | 5271 | -5708 | -2504 | 0 |
|  | 0.100 | 24475 | 22784 | 22523 | -14066 | -14066 | -8241 | -2380 | 5271 | -5708 | -2504 | 0 |
|  | 0.128 | 22314 | 22670 | 21923 | -7747 | -7747 | -4616 | -4172 | 218 | 3558 | -780 | -84743 |
|  | 0.228 | 21045 | 20911 | 19070 | -7961 | -7961 | -5336 | -5656 | 1239 | 4274 | 2654 | -125839 |
|  | 1.728 | 21045 | 20911 | 19070 | -2694 | -2694 | -1131 | -3972 | 1500 | 4436 | 2654 | -125839 |
| Maximum |  | 24475 | 22784 | 22523 | 0 | 0 | 0 | 0 | 5271 | 4436 | 2654 | 0 |
| Minimum |  | 0 | 0 | 0 | -14066 | -14066 | -8241 | -5656 | 0 | -5708 | -2504 | -125839 |
| I2t (A2-s) |  | 1.12E+09 | 1.07E+09 | 9.04E+08 | 1.05E+08 | 1.05E+08 | 3.61E+07 | 4.33E+07 | 1.36E+07 | 4.45E+07 | 9.20E+07 |  |
| tESW (s) |  | 1.86 | 2.06 | 1.78 | 0.53 | 0.53 | 0.53 | 1.35 | 0.49 | 1.37 | 13.05 |  |

| 320kA Ohmic Scenario | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.600 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | 0.000 | 31611 | 32115 | 31058 | -22763 | -22763 | -15953 | -9680 | -122 | 66 | -1106 | 0 |
|  | 0.100 | 31611 | 32115 | 31058 | -22763 | -22763 | -15953 | -9680 | -122 | 66 | -1106 | 0 |
|  | 0.206 | 31091 | 29143 | 28966 | 11386 | 11386 | -9008 | -15155 | 5050 | 4730 | 2191 | -320775 |
|  | 0.306 | 31091 | 29143 | 28966 | 14897 | 14897 | -6205 | -14032 | 5224 | 4838 | 2191 | -320775 |
|  | 0.506 | 31091 | 29143 | 28966 | 21919 | 21919 | -598 | -11786 | 5572 | 5054 | 2191 | -320775 |
| Maximum |  | 31611 | 32115 | 31058 | 21919 | 21919 | 0 | 0 | 5572 | 5054 | 2191 | 0 |
| Minimum |  | 0 | 0 | 0 | -22763 | -22763 | -15953 | -15155 | -122 | 0 | -1106 | -320775 |
| I2t (A2-s) |  | 1.10E+09 | 1.02E+09 | 9.66E+08 | 4.18E+08 | 4.04E+08 | 1.49E+08 | 1.50E+08 | 1.71E+07 | 1.15E+07 | 1.40E+08 |  |
| tESW (s) |  | 1.10 | 0.99 | 1.00 | 0.81 | 0.78 | 0.59 | 0.65 | 0.55 | 0.45 | 29.19 |  |

| 0.5T TF | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.800 |  |  |  |  |  |  |  |  |  | 0 |  |
|  | 0.000 |  |  |  |  |  |  |  |  |  | 16204 |  |
|  | 0.100 |  |  |  |  |  |  |  |  |  | 16204 |  |
|  | 0.200 |  |  |  |  |  |  |  |  |  | 16204 |  |
|  | 0.300 |  |  |  |  |  |  |  |  |  | 16204 |  |
|  | 0.500 |  |  |  |  |  |  |  |  |  | 16204 |  |
| Maximum |  |  |  |  |  |  |  |  |  |  | 16215 |  |
| Minimum |  |  |  |  |  |  |  |  |  |  | 0 |  |
| Current direction |  |  |  |  |  |  |  |  |  |  | 1.00E+00 |  |
| I2t (A2-s) |  |  |  |  |  |  |  |  |  |  | 4.05E+08 |  |
| tESW (s) |  |  |  |  |  |  |  |  |  |  | 1.54 |  |

| Summary |  | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF | Plasma |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Maximum |  | 37190 | 37783 | 36538 | 21919 | 21919 | 5217 | 1584 | 7728 | 7300 | 16215 | 0 |
| Minimum |  | 0 | 0 | 0 | -23438 | -23438 | -15953 | -15155 | -122 | -8195 | -3548 | -320775 |
| Max I2t (A2-s) |  | 1.28E+09 | 1.27E+09 | 1.15E+09 | 4.18E+08 | 4.04E+08 | 1.49E+08 | 1.50E+08 | 3.25E+07 | 4.87E+07 | 4.05E+08 |  |
| tESW (s) at max current |  | 0.93 | 0.89 | 0.86 | 0.76 | 0.74 | 0.59 | 0.65 | 0.54 | 0.73 | 1.54 |  |

A.2.3.3 Temperature History

Coil temperatures are in Kelvin. Maxima for all reference scenarios are shown in blue.

| 1.7T Ohmic Scenario | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.700 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 |
|  | 0.000 | 93 | 92 | 92 | 88 | 88 | 86 | 85 | 85 | 85 | 85 |
|  | 0.100 | 96 | 94 | 94 | 88 | 88 | 86 | 85 | 85 | 85 | 85 |
|  | 0.140 | 97 | 95 | 95 | 88 | 88 | 86 | 85 | 85 | 85 | 85 |
|  | 0.240 | 99 | 98 | 97 | 89 | 89 | 86 | 85 | 85 | 85 | 85 |
|  | 0.440 | 104 | 103 | 102 | 89 | 89 | 87 | 85 | 85 | 85 | 85 |
|  | 3.621 | 113 | 111 | 109 | 89 | 89 | 87 | 85 | 85 | 86 | 86 |
| Dissipated Energy (J) |  | 1.62E+07 | 1.44E+07 | 1.13E+07 | 4.87E+05 | 4.88E+05 | 1.94E+05 | 8.28E+04 | 1.32E+05 | 1.55E+05 | 1.22E+06 |
|  |  |  |  |  |  |  |  |  |  |  | 4.47E+07 |

| 1.7T High Beta Scenario | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.700 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 |
|  | 0.000 | 93 | 92 | 92 | 86 | 86 | 85 | 85 | 85 | 85 | 85 |
|  | 0.100 | 96 | 94 | 94 | 86 | 86 | 85 | 85 | 85 | 85 | 85 |
|  | 0.140 | 97 | 95 | 95 | 86 | 86 | 85 | 85 | 85 | 85 | 85 |
|  | 0.240 | 99 | 97 | 97 | 86 | 86 | 85 | 85 | 85 | 85 | 85 |
|  | 0.440 | 103 | 102 | 101 | 86 | 86 | 85 | 85 | 85 | 85 | 85 |
|  | 3.621 | 112 | 109 | 106 | 86 | 86 | 85 | 85 | 85 | 86 | 86 |
| Dissipated Energy (J) |  | 1.54E+07 | 1.33E+07 | 9.81E+06 | 1.78E+05 | 1.79E+05 | 5.03E+04 | 1.00E+05 | 1.54E+05 | 1.65E+05 | 2.01E+06 |
|  |  |  |  |  |  |  |  |  |  |  | 4.13E+07 |

| 2T High Beta Scenario | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.850 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 |
|  | 0.000 | 98 | 99 | 98 | 86 | 86 | 86 | 85 | 85 | 85 | 85 |
|  | 0.050 | 99 | 101 | 99 | 86 | 86 | 86 | 85 | 85 | 85 | 85 |
|  | 0.097 | 101 | 102 | 101 | 86 | 86 | 86 | 85 | 85 | 85 | 85 |
|  | 0.192 | 104 | 105 | 104 | 86 | 86 | 86 | 85 | 85 | 85 | 85 |
|  | 0.197 | 104 | 105 | 104 | 86 | 86 | 86 | 85 | 85 | 85 | 85 |
|  | 3.378 | 115 | 115 | 112 | 87 | 87 | 86 | 86 | 85 | 85 | 87 |
| Dissipated Energy (J) |  | 1.79E+07 | 1.73E+07 | 1.26E+07 | 2.01E+05 | 1.99E+05 | 8.06E+04 | 1.93E+05 | 1.05E+04 | 4.04E+04 | 2.74E+06 |
|  |  |  |  |  |  |  |  |  |  |  | 5.13E+07 |

| 1.2T Long Pulse Scenario | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.500 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 |
|  | 0.000 | 87 | 87 | 87 | 86 | 86 | 85 | 85 | 85 | 85 | 85 |
|  | 0.100 | 89 | 88 | 88 | 86 | 86 | 85 | 85 | 85 | 85 | 85 |
|  | 0.128 | 89 | 88 | 88 | 86 | 86 | 85 | 85 | 85 | 85 | 85 |
|  | 0.228 | 90 | 89 | 89 | 86 | 86 | 85 | 85 | 85 | 85 | 85 |
|  | 1.728 | 107 | 106 | 102 | 86 | 86 | 85 | 85 | 85 | 85 | 85 |
|  | 4.909 | 111 | 110 | 105 | 86 | 86 | 85 | 85 | 85 | 85 | 86 |
| Dissipated Energy (J) |  | 1.48E+07 | 1.37E+07 | 9.29E+06 | 1.49E+05 | 1.49E+05 | 5.05E+04 | 1.61E+05 | 6.41E+04 | 1.51E+05 | 1.05E+06 |
|  |  |  |  |  |  |  |  |  |  |  | 8.88E+05 |

| 320kA Ohmic Scenario | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.600 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 |
|  | 0.000 | 90 | 91 | 90 | 87 | 87 | 86 | 85 | 85 | 85 | 85 |
|  | 0.100 | 93 | 93 | 92 | 88 | 88 | 86 | 85 | 85 | 85 | 85 |
|  | 0.206 | 95 | 95 | 95 | 88 | 88 | 87 | 86 | 85 | 85 | 85 |
|  | 0.306 | 97 | 97 | 96 | 88 | 88 | 87 | 86 | 85 | 85 | 85 |
|  | 0.506 | 102 | 101 | 100 | 89 | 89 | 87 | 86 | 85 | 85 | 85 |
|  | 3.687 | 110 | 108 | 107 | 90 | 90 | 87 | 87 | 85 | 85 | 86 |
| Dissipated Energy (J) |  | 1.46E+07 | 1.29E+07 | 1.01E+07 | 6.25E+05 | 6.03E+05 | 2.13E+05 | 5.69E+05 | 8.09E+04 | 3.86E+04 | 1.61E+06 |
|  |  |  |  |  |  |  |  |  |  |  | 0.00E+00 |

| 0.5T TF | t(s) | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | -0.800 |  |  |  |  |  |  |  |  |  | 85 |
|  | 0.000 |  |  |  |  |  |  |  |  |  | 86 |
|  | 0.100 |  |  |  |  |  |  |  |  |  | 86 |
|  | 0.200 |  |  |  |  |  |  |  |  |  | 86 |
|  | 0.300 |  |  |  |  |  |  |  |  |  | 86 |
|  | 0.500 |  |  |  |  |  |  |  |  |  | 87 |
|  | 4.287 |  |  |  |  |  |  |  |  |  | 88 |
| Dissipated Energy (J) |  |  |  |  |  |  |  |  |  |  | 4.79E+06 |
|  |  |  |  |  |  |  |  |  |  |  | 4.79E+06 |

| Summary |  | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Max Final Temperature |  | 115 | 115 | 112 | 90 | 90 | 87 | 87 | 85 | 86 | 88 |
| Max Dissipated Energy (J) |  | 1.79E+07 | 1.73E+07 | 1.26E+07 | 6.25E+05 | 6.03E+05 | 2.13E+05 | 5.69E+05 | 1.54E+05 | 1.65E+05 | 4.79E+06 |
|  |  |  |  |  |  |  |  |  |  | 5.13E+07 |

A.2.3.4 Electrical Power Requirements

Upgrade Power Supply and Cabling Requirements and Modeling Assumptions Other than for the First Plasma and Field Line Mapping Scenarios, it is assumed that DC power will be brought over from D-site. Power supply requirements for these reference scenarios have been calculated based on the following assumptions:

[1] All coils of the same type (e.g. all M1 coils) are connected in series. 	All coils in the same circuit are connected in series.  Circuit configurations are defined in the table below.

[2] All coils of the same type have a single CLR connected in series with the coils. 	Each CLR has an inductance of 267 micro-H and a resistance of 100 milli-ohms.

[3] DC power will be carried from D-site to the test cell via cables approximately 750 feet in length (each way). Required DC current ratings and cables per pole in each circuit are defined in the table below. An inductance of 132 micro-Henries per cable pair (supply and return) was assumed.

[4] TFTR power supply sections (PSS) will be used. 	Each PSS has an open circuit voltage of 1012.85V and a maximum current of 28kA. When operated in parallel, the maximum rated current is reduced by 10%.

[5] Required DC ratings are based on a pulse repetation time of 15 minutes.

| Ultimate capability required | 1.7T Ohmic 1.7T Hi Beta 2T Hi Beta 1.2T Long Pulse 320kA | M1 | M2 | M3 | PF4 | PF6 | TF | PF1/2 | PF3 | PF5U | PF5L |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 128 MW 380 MVA 94 MJ | Max I2t (A2-s) tESW (s) Required DC rating (A) | 1.28E+09 0.93 1193 | 1.27E+09 0.89 1190 | 1.15E+09 0.86 1128 | 1.50E+08 0.65 409 | 4.87E+07 0.73 233 | 4.05E+08 1.54 670 | 4.04E+08 0.74 670 | 1.49E+08 0.59 407 | 3.25E+07 0.54 190 | 3.25E+07 0.54 190 |  |
|  | Cables per pole Series PSS per | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 26 Cables |
|  | branch Branches Branch configuration | 2 2 Parallel | 2 2 Parallel | 2 2 Parallel | 2 1 | 2 2 Anti-parallel | 4 2 Anti-parallel | 4 2 Anti-parallel | 2 1 | 2 1 | 2 1 | 40 PSS |

A.2.4 Pulsed Heat Loads

Pulsed heat loads calculated on the basis of the worst case scenario for each coil.

A.2.4.1 Maximum Temperature and Energy Deposition

| Pulsed heat Loads | M1 | M2 | M3 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6 | TF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Initial Temperature (K) | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 | 85 |
| Max Temperature (K) | 115 | 115 | 112 | 90 | 90 | 87 | 87 | 85 | 86 | 88 |
| Energy Deposited (J) | 1.79E+07 | 1.73E+07 | 1.26E+07 | 6.25E+05 | 6.03E+05 | 2.13E+05 | 5.69E+05 | 1.54E+05 | 1.65E+05 | 4.79E+06 |
|  |  |  |  |  |  |  |  |  |  | 5.13E+07 |

A.2.4.2 LN2 Consumption During Pulsed Operation

| Max LN2 Consumption |  | Tsat (K) | Psat (MPa) | hfg (kJ/kg) | Mass per pulse (kg) | Density (kg/m3) | (m3/kg) | Volume (m3) | (liters) | (gallons) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Per shot |  | 78 | 0.109365352 | 198.301405 | 258.4629516 | 805.735019 | 0.001241103 | 0.320779097 | 320.7790968 | 85 per shot |
| Time between shots (minutes) | 15 |  |  |  |  |  |  |  |  |  |
| Hours per day | 8 |  |  |  |  |  |  |  |  |  |
| Full pwr shots per day | 32 |  |  |  |  |  |  |  |  | 2712 per day |
| Operating days per week | 5 |  |  |  |  |  |  |  |  | 13559 per wk |

A.2.4.2 LN2 Delivery Requirements

|  | Gallons per Truck 6500 | Trucks |  |
| --- | --- | --- | --- |
| Pulsed heat loads only |  |  |  |
| Max pulsed heat loads |  |  | 2.09 per week |
| Field line mapping |  |  | 0.05 per week |
| First Plasma |  |  | 0.02 per week |
| Parasitic loads only |  |  |  |
| Normal |  |  | 2.12 per week |
| 150C Bakeout |  |  | 2.86 per week |
| 350C Bakeout |  |  | 3.52 per week |
| Cooldown only |  |  | 1.63 |