NCSX PRODUCT SPECIFICATION

MODULAR COIL TYPE-C ASSEMBLY

NCSX-CSPEC-142-05-00

DRAFT 6/29/05

Prepared by: _____________________________________________________________

D. Williamson, WBS14

Concurred by: ____________________________________________________________

J. Chrzanowski, Coil Windings and Assembly

Concurred by: ____________________________________________________________

B. Nelson, NCSX Stellarator Core

Concurred by: ____________________________________________________________

J. Malsbury, NCSX QA Manager

Approved by: ____________________________________________________________

W. Reiersen, Engineering Manager

-------------------------Controlled Document -----------------------

This is a controlled document. Check the NCSX Engineering web for latest revision.

REVISION HISTORY

| Revision No. | Affected Pages | Date |
| --- | --- | --- |
| 0 (Initial Issue) | All | 6/29/05 |

TABLE OF CONTENTS

1	INTRODUCTION AND SCOPE	1

1.1	Introduction	1

1.2	Scope	1

2	APPLICABLE DOCUMENTS	1

2.2	Standards and Specifications	1

2.2	Drawings	1

3	REQUIREMENTS	9

3.1	Definition	9

3.2	Characteristics	11

3.2.1	Winding Form Assembly	11

3.2.1.1	Material	11

3.2.1.2	Size and Weight	11

3.2.1.3	Magnetic Permeability	11

3.2.1.4	Electrical Requirements	11

3.2.1.5	Winding Surface Tolerance	11

3.2.1.6	Surface finish	11

3.2.1.7	Winding Clamp Modifications	11

3.2.2	Inner Copper Cladding	12

3.2.2.1	Material	12

3.2.2.2	Quantity, Size, and Weight	12

3.2.2.3	Sliding Fit	12

3.2.2.4	Electrical Requirements	13

3.2.3	Ground Insulation	13

3.2.3.1	Material	13

3.2.3.2	Quantity, Size, and Weight	13

3.2.4	Conductor and Turn Insulation	13

3.2.4.1	Material	13

3.2.4.2	Size and Weight	13

3.2.4.3	Conductor Length	13

3.2.4.4	Electrical Properties	13

3.2.4.5	Current Center	13

3.2.5	Supplemental Turn Insulation at Leads	13

3.2.5.1	Material	13

3.2.5.2	Size and Weight	13

3.2.6	Lead Blocks	14

3.2.6.1	Material	14

3.2.6.2	Quantity, Size and Weight	14

3.2.6.3	Surface Finish	14

3.2.7	Terminal Blocks and Insulators	14

3.2.7.1	Material	14

3.2.7.2	Quantity, Size, and Weight	14

3.2.7.3	Surface Finish	14

3.2.7.4	Bolted Connections	14

3.2.8	Chill Plates	14

3.2.8.1	Material	14

3.2.8.2	Quantity, Size, and Weight	14

3.2.8.3	Electrical Properties	14

3.2.9	Coolant Tubes	15

3.2.9.1	Material	15

3.2.9.2	Quantity, Size, and Weight	15

3.2.10	VPI Bag Mold	15

3.2.10.1	Material	15

3.2.10.2	Quantity, Size and Weight	15

3.2.11	Clamp Assembly	15

3.2.11.1	Material	15

3.2.11.2	Quantity, Size and Weight	15

3.2.12	Instrumentation -revise	15

3.2.12.1	Strain gages	15

3.2.12.1.1	Material	15

3.2.12.1.2	Quantity, Size, and Weight	15

3.2.12.1.3	Location	15

3.2.12.2	Thermocouples	16

3.2.12.2.1	Material	16

3.2.12.2.2	Quantity, Size, and Weight	16

3.2.12.2.3	Location	16

3.2.12.3	Flux loops	16

3.2.12.3.1	Material	16

3.2.12.3.2	Quantity, Size, and Weight	16

3.2.12.3.3	Location	16

3.2.12.3.4	Termination	16

4	QUALITY ASSURANCE	16

4.1	Inspection and Test Requirements	16

4	DOCUMENTATION	19

5.1	System of Documentation	19

TABLE OF FIGURES

Figure 3-1 – Typical Modular Coil Cross-Section	10

Figure 3-2 – Winding Surface Dimensions and Tolerances (se141-116.drw)	12

# INTRODUCTION AND SCOPE

## Introduction

The National Compact Stellarator Experiment (NCSX) is a quasi-axisymmetric facility that combines the high beta and good confinement features of an advanced tokamak with the low current, disruption-free characteristics of a stellarator.  The experiment is based on a three field-period plasma configuration with an average major radius of 1.4 m, a minor radius of 0.3 m, and a toroidal magnetic field on axis of up to 2 T.  The modular coils are one set in a complex assembly of four coil systems that surround the highly shaped plasma.  There are six each of three coil types in the assembly for a total of 18 modular coils.  The coils are constructed by winding copper cable onto a cast stainless steel winding form that has been machined to high accuracy, so that the current center of the winding pack is within ±1.5 mm of its theoretical position.  The modular coils operate at a temperature of 80 K and are subjected to rapid heating and stress during a pulse.

## Scope

This specification defines the modular coil Type-C assembly and requirements for its construction and operation.

# APPLICABLE DOCUMENTS

## Standards and Specifications

ASTM A703/M-01		Specification for Steel Castings

ASTM B152/M-00		Standard Specification for Copper Sheet

ASTM B280-03		Standard Specification for Seamless Copper Tube

NCSX-BSPEC-14-00		System Requirements for the Modular Coil System

NCSX-CSPEC-142-03	Modular Coil Conductor Specification

NCSX-MCWFOP-00		Winding Facility Operations Plan

NCSX-MITQA-142-01	Modular Coil MIT/QA Plan

NCSX-PLAN-QAP		NCSX Quality Assurance Plan

## Drawings

The Type-C modular coil assembly shall be fabricated per the following Pro/ENGINEER models and drawings, which are stored in the Pro/INTRALINK database:

| DRAWING | REV | REL DATE | DESCRIPTION |
| --- | --- | --- | --- |
| Top level assembly and layouts |
| se140-103.drw | 0 | WIP | MODULAR COIL ASSEMBLY TYPE-C |
| se142c-019.drw | 0 | WIP | TYPE-C WINDING PACK DIMENSIONS |
| se142c-016.drw | 0 | WIP | TYPE-C ELECTRICAL SCHEMATIC |
| se142c-015.drw | 0 | WIP | TYPE-C COOLING SCHEMATIC |
| Winding form assembly, SE141-103 |
| ds141-036.drw | 0 | 09/23/04 | STUD, 1.375-6UNC-2A X 9 LG |
| ds141-038.drw | 0 | 09/23/04 | INSULATING WASHER |
| ds141-060.drw | 0 | 09/23/04 | NUT, 12PT HEX 1.375-6UNC-2B |
| ds141-079.drw | 0 | 09/23/04 | FLAT WASHER |
| se141-078.drw | 1 | 09/23/04 | POL BREAK SHIM ASSEMBLY TYPE-C |
| se141-103.drw | 1 | 09/23/04 | MOD COIL WINDING FORM ASSEMBLY TYPE-C |
| se141-116.drw | 5 | 04/29/05 | PRODUCTION WINDING FORM TYPE-C |
| se141-123.drw | 0 | WIP | MCWF TYPE-C STUD WELDMENT |
| Side-A winding pack assembly, SE142C-018 |
| se142c-018.drw | 0 | WIP | TYPE-C SIDE-A WINDING PACK ASSEMBLY |
| se142c-134.drw | 0 | 06/09/05 | TYPE-C SIDE-A LOWER LEAD BLOCK COMBINED |
| se142c-136.drw | 0 | WIP | TYPE-C SIDE-A UPPER LEAD BLOCK COMBINED |
| se142c-382-101_105.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-106_110.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-111_115.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-116_120.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-121_125.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-126_130.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-131_135.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-136_140.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-141_145.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-146_150.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-151_155.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-156_160.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-161_165.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-166_170.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-171_175.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-176_180.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-181_185.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-186_190.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-191_195.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-196_200.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-201_205.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-206_210.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-211_215.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-216_220.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-221_225.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-226_230.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-231_235.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-236_240.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-241_245.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-246_250.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-251_255.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-256_260.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-261_265.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-266_270.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-271_275.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-276_280.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-281_285.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-286_290.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-382-291_295.drw | 0 | 04/20/05 | TYPE-C SIDE-A UPPER CLADDING FLAT PATTERN |
| se142c-384-101_105.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-106_110.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-111_115.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-116_120.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-121_125.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-126_130.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-131_135.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-136_140.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-141_145.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-146_150.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-151_155.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-156_160.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-161_165.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-166_170.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-171_175.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-176_180.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-181_185.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-186_190.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-191_195.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-196_200.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-201_205.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-206_210.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-211_215.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-216_220.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-221_225.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-226_230.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-231_235.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-236_240.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-241_245.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-246_250.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-251_255.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-256_260.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-261_265.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-266_270.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-271_275.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-276_280.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-281_285.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-286_290.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-384-291_295.drw | 0 | 04/20/05 | TYPE-C SIDE-A LOWER CLADDING FLAT PATTERN |
| se142c-386-101_105.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-106_110.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-111_115.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-121_125.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-126_130.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-131_135.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-136_140.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-141_145.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-146-150.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-151-155.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-156_160.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-161_165.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-166_170.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-171_175.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-176_180.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-181_185.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-186_190.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-191_195.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-201_205.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-206_210.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-211_215.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-216_220.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-221_225.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-226_230.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-231_235.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-236_240.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-241_245.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-246_250.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-251_255.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-256_260.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-261_265.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-266_270.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-271_275.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-276_280.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-281_285.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-286_290.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-386-291_292.drw | 0 | WIP | TYPE-C SIDE-A UPPER CHILL PLATE FLAT PATTERN |
| se142c-388-101_105.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-106_110.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-111_115.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-121_125.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-126_130.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-131_135.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-136_140.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-141_145.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-146-150.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-151-155.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-156_160.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-161_165.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-166_170.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-171_175.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-176_180.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-181_185.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-186_190.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-191_195.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-201_205.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-206_210.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-211_215.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-216_220.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-221_225.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-226_230.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-231_235.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-236_240.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-241_245.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-246_250.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-251_255.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-256_260.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-261_265.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-266_270.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-271_275.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-276_280.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-281_285.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-286_290.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| se142c-388-291_292.drw | 0 | WIP | TYPE-C SIDE-A LOWER CHILL PLATE FLAT PATTERN |
| Side-B winding pack assembly, SE142C-017 |
| se142c-017.drw | 0 | WIP | TYPE-C SIDE-B WINDING PACK ASSEMBLY |
| se142c-135.drw | 0 | 06/09/05 | TYPE-C SIDE-B LOWER LEAD BLOCK COMBINED |
| se142c-137.drw | 0 | WIP | TYPE-C SIDE-B UPPER LEAD BLOCK COMBINED |
| se142c-482-101_105.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-106_110.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-111_115.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-116_120.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-121_125.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-126_130.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-131_135.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-136_140.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-141_145.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-146_150.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-151_155.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-156_160.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-161_165.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-166_170.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-171_175.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-176_180.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-181_185.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-186_190.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-191_195.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-196_200.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-201_205.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-206_210.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-211_215.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-216_220.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-221_225.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-226_230.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-231_235.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-236_240.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-241_245.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-246_250.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-251_255.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-256_260.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-261_265.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-266_270.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-271_275.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-276_280.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-281_285.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-286_290.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-482-291_295.drw | 0 | 04/20/05 | TYPE-C SIDE-B UPPER CLADDING FLAT PATTERN |
| se142c-484-101_105.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-106_110.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-111_115.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-116_120.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-121_125.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-126_130.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-131_135.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-136_140.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-141_145.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-146_150.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-151_155.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-156_160.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-161_165.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-166_170.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-171_175.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-176_180.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-181_185.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-186_190.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-191_195.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-196_200.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-201_205.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-206_210.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-211_215.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-216_220.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-221_225.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-226_230.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-231_235.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-236_240.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-241_245.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-246_250.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-251_255.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-256_260.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-261_265.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-266_270.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-271_275.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-276_280.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-281_285.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-286_290.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-484-291_295.drw | 0 | 04/20/05 | TYPE-C SIDE-B LOWER CLADDING FLAT PATTERN |
| se142c-486-101_105.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-106_110.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-111_115.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-121_125.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-126_130.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-131_135.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-136_140.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-141_145.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-146-150.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-151-155.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-156_160.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-161_165.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-166_170.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-171_175.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-176_180.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-181_185.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-186_190.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-191_195.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-201_205.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-206_210.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-211_215.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-216_220.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-221_225.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-226_230.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-231_235.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-236_240.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-241_245.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-246_250.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-251_255.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-256_260.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-261_265.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-266_270.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-271_275.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-276_280.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-281_285.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-286_290.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-486-291_292.drw | 0 | WIP | TYPE-C SIDE-B UPPER CHILL PLATE FLAT PATTERN |
| se142c-488-101_105.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-106_110.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-111_115.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-121_125.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-126_130.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-131_135.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-136_140.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-141_145.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-146-150.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-151-155.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-156_160.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-161_165.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-166_170.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-171_175.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-176_180.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-181_185.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-186_190.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-191_195.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-201_205.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-206_210.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-211_215.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-216_220.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-221_225.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-226_230.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-231_235.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-236_240.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-241_245.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-246_250.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-251_255.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-256_260.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-261_265.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-266_270.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-271_275.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-276_280.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-281_285.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-286_290.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| se142c-488-291_292.drw | 0 | WIP | TYPE-C SIDE-B LOWER CHILL PLATE FLAT PATTERN |
| Leads terminal assembly, SE142C-050 |
| se142c-047.drw | 0 | WIP | TYPE-C JUMPERS BASE BLOCK |
| se142c-049.drw | 0 | WIP | TYPE-C JUMPERS INSULATOR |
| se142c-050.drw | 0 | WIP | TYPE-C LEADS TERMINAL ASSEMBLY |
| se142c-051.drw | 0 | WIP | TYPE-C TERMINAL JUMPER #1 |
| se142c-052.drw | 0 | WIP | TYPE-C TERMINAL JUMPER #2 |
| se142c-053.drw | 0 | WIP | TYPE-C TERMINAL JUMPER #3 |
| se142c-054.drw | 0 | WIP | TYPE-C TERMINAL JUMPER #4 |
| se142c-055.drw | 0 | WIP | TYPE-C SHORT TERMINAL LUG |
| se142c-056.drw | 0 | WIP | TYPE-C LONG TERMINAL LUG |
| se142c-057.drw | 0 | WIP | TYPE-C TERMINAL LUG CONNECTOR |
| se142c-058.drw | 0 | WIP | TYPE-C TERMINAL LUG CONNECTOR |
| se142c-059.drw | 0 | WIP | TYPE-C CABLE CONNECTOR |
| se142c-062.drw | 0 | WIP | WASHER .53 ID 1.25 OD X .06 THK |
| se142c-063.drw | 0 | WIP | FLAT WASHER |
| se142c-064.drw | 0 | WIP | 1/2-13unc SCREW |
| se142c-065.drw | 0 | WIP | .53 ID .875 OD .06 THK FLAT WASHER |
| se142c-068.drw | 0 | WIP | INSULATING WASHER |
| se142c-069.drw | 0 | WIP | INSULATING SLEEVE |
| Lead blocks enclosure, SE142C-233 |
| se142c-226.drw | 0 | WIP | LEAD BLOCKS WEDGE, SIDE-B |
| se142c-227.drw | 0 | WIP | LEAD BLOCKS WEDGE, SIDE-A |
| se142c-183.drw | 0 | WIP | LEAD BLOCKS CHILL PLATE, SIDE-A |
| se142c-241.drw | 0 | WIP | LEAD BLOCKS CHILL PLATE, SIDE-B |
| se142c-201.drw | 0 | WIP | LEAD BLOCKS SUPP COOLING TUBE, SIDE-A |
| se142c-202.drw | 0 | WIP | LEAD BLOCKS SUPP COOLING TUBE, SIDE-A |
| se142c-220.drw | 0 | WIP | LEAD BLOCKS SIDE PLATE, SIDE-A |
| se142c-221.drw | 0 | WIP | LEAD BLOCKS SIDE PLATE, SIDE-B |
| se142c-184.drw | 0 | WIP | LEAD BLOCKS TOP PLATE |
| Clamp assembly, SE1405-275P |
| se1405-258p.drw | 1 | 04/04/05 | WASHER, BELLEVILLE |
| se1405-261p.drw | 1 | 04/04/05 | SCREW, SET, 15/16-20 UNEF-2A X 3/8 |
| se1405-263p.drw | 1 | 04/04/05 | WASHER, SPERICAL, CONVEX |
| se1405-267.drw | 0 | 04/04/05 | TRC CLAMP PAD |
| se1405-272.drw | 0 | 04/04/05 | CLAMP SWIVEL STUD |
| se1405-273.drw | 0 | 04/04/05 | CLAMP SWIVEL PAD |
| se1405-274.drw | 0 | 04/04/05 | TRC FLAT WASHER 3/4 OD |
| se1405-275p.drw | 0 | 04/04/05 | CLAMP ASSEMBLY, SHORT |
| se1405-276.drw | 1 | 04/04/05 | BAR, CLAMP, HORIZONTAL |
| se1405-277.drw | 0 | 04/04/05 | PISTON, SPHERICAL, CONCAVE |
| se1405-278.drw | 0 | 04/04/05 | CLAMP BUSHING |

# REQUIREMENTS

## Definition

The modular coil Type-C assembly includes the winding form, conductor and insulation, leads and termination, cooling system, instrumentation, vacuum-pressure epoxy impregnation (VPI) features, and the coil clamps. Figure 1 shows the main subcomponents of the coil assembly:

Winding form – a cast, stainless steel structure with a machined “tee” profile

Cladding – inner layer of copper that cools the winding pack by conduction

Ground insulation – multiple layers of glass cloth surrounding the winding pack

Conductor – stranded copper wire with a compacted, rectangular cross-section

Turn insulation – pre-wrapped layers of glass around each conductor

Lead blocks – insulated supports for conductor entry/exit from winding pack

Terminal blocks – electrical connection to coax power feed

Chill Plates – outer layer of copper and tubes for LN2 cooling

Bag mold – silicone and fiberglass shell that surrounds winding pack

Clamps – support that provides clamping force, preload on winding pack

Instrumentation – strain gages, thermocouples, and voltage taps

Magnetic diagnostics – two wires co-wound on the plasma side of winding pack

Figure 3-1 – Typical Modular Coil Cross-Section

## Characteristics

Each of the modular coil Type-C assembly subcomponents has performance or physical characteristics that are necessary for proper function of the coil and should be verified prior to or during assembly.

### Winding Form Assembly

#### Material

The winding form material is a cast, stainless steel alloy, similar to CF8M.  Poloidal break insulators are composed of NEMA Grade G-11CR laminate.

#### Size and Weight

The bounding dimensions of the winding form assembly is 45 x 77 x 95-in and the weight is approximately 6100-lbs.

#### Magnetic Permeability

The relative magnetic permeability of the winding form shall not exceed 1.02.

#### Electrical Requirements

The resistance of the mid-plane insulation and of the bolt insulation shall be >500 kohms when tested at 100 VDC .

#### Winding Surface Tolerance

The dimensions of the “tee” section of the winding form are illustrated in Figure 3-2. The winding surface has a profile tolerance of +/- .010-in to the theoretical CAD surface.

#### Surface finish

All winding surfaces shall have a surface finish <125-u in.

#### Winding Clamp Modifications

Threaded studs shall be attached to the winding form by welding, as specified in drawing se141-123.drw.

Figure 3-2 – Winding Surface Dimensions and Tolerances (se141-116.drw)

### Inner Copper Cladding

#### Material

The cladding material is 0.040-in thick copper sheet, UNS No. C10200, with high thermal conductivity and a temper suitable for forming. Annealed condition is acceptable.

#### Quantity, Size, and Weight

There are 384 pieces of cladding, with average dimensions of 1.5 x 4-in. and a total weight of ~30-lbs.

#### Sliding Fit

The cladding shall conform to the winding surface but not be permanently bonded or attached to it.  The cladding may be temporarily secured to the winding form during the winding process.

#### Electrical Requirements

The cladding shall be electrically isolated from the winding form by a half-lapped layer of 0.0035-in thick Kapton tape.

### Ground Insulation

#### Material

The ground insulation is composed of S2 glass and adhesive Kapton.

#### Quantity, Size, and Weight

The total thickness of 0.0445-in is composed of three layers: 1) a butt-lapped layer of 0.007-in S2 glass, 2) a half-lapped layer consisting of  2-in wide x 0.007-in S2 glass and 1.5-in wide x 0.0065-in adhesive Kapton tape, and 3) a butt-lapped layer of the same composite

### Conductor and Turn Insulation

#### Material

The conductor material is 34-AWG CDA-101 copper wire, and the turn insulation is S-2 glass cloth with S920 Silane finish.

#### Size and Weight

The nominal size of the conductor with insulation is .374 x .415-in, and the weight is approximately 410-lbs per 1000-ft.

#### Conductor Length

The total length of conductor for the Type-C coil assembly is ~8 x 220-ft.

#### Electrical Properties

The resistance of the conductor shall be less than 0.089-Ω per 1000-ft when measured at room temperature.

#### Current Center

The wound coil shall have a current center that is within 1.5-mm of the theoretical position.

### Supplemental Turn Insulation at Leads

#### Material

S2 glass and interleaved Kapton with adhesive backing.

#### Size and Weight

The total thickness of 0.041-in is composed of two half-lapped layers consisting of 1-in wide x 0.007-in S2 glass and 0.75-in wide x 0.0065-in adhesive Kapton tape.

### Lead Blocks

#### Material

The lead blocks are constructed of an insulating material such as NEMA grade G-11CR epoxy laminate.

#### Quantity, Size and Weight

There are two lead blocks per side, the largest of which is 1.8 x 6.8 x 11-in in size.  The total weight of the lead blocks is ~10-lbs.

#### Surface Finish

The lead blocks shall be free of burrs and sharp edges that can damage the conductor. All surfaces unless machined shall be sanded to remove any high gloss surface, to promote bonding of the epoxy to the lead blocks.

### Terminal Blocks and Insulators

#### Material

The terminal material is copper, UNS No. C10200, with interleaved insulation composed of NEMA Grade G-11CR epoxy laminate.

#### Quantity, Size, and Weight

There are four jumpers per coil, with average dimensions of 1.5 x 4.5 x 5.5-in and a weight of ~0.5-lb each.

#### Surface Finish

The terminal blocks and insulators shall be free of burrs and sharp edges that can damage the conductor.

#### Bolted Connections

Each conductor is attached to the terminal blocks through a bolted electrical connection.

### Chill Plates

#### Material

The cladding material is 0.040-in thick copper sheet, UNS No. C10200, with high thermal conductivity and a temper suitable for forming. Annealed condition is acceptable.

#### Quantity, Size, and Weight

There are 384+ chill plate parts, with average dimensions of 1.5 x 4 x 4-in. and a total weight of ~30-lbs.

#### Electrical Properties

The chill plates shall be electrically isolated from both the winding form and the cladding assembly.

### Coolant Tubes

#### Material

The tubing material is UNS C10200, with dimensions 0.25-in dia x 0.030-in wall per ASTM B280-03.

#### Quantity, Size, and Weight

There are 8 tube segments per coil, with a maximum length of 15-ft.

### VPI Bag Mold

#### Material

The bag mold is composed of self-fusing gray silicone tape, 2-part RTV-11 (white), Nomex felt (Stock No. NX08-6), and Hysol resin/hardener (Part 3561/2039).

#### Quantity, Size and Weight

[2] layers of silicone tape/ painted with RTV-11/ overwrapped with [2] layers of Nomex felt filled with Hysol epoxy formulation.

### Clamp Assembly

#### Material

All clamp components are to be constructed of a non-magnetic stainless steel, such as alloy UNS S31600.

#### Quantity, Size and Weight

There are 48 permanent clamps in the coil assembly.

### Instrumentation -revise

#### Strain gages

#### Material

Fiber optic strain gage

#### Quantity, Size, and Weight

Minimum of 8 strain gages

#### Location

Three each at each end of the coil, located at the tip of the tee web and the inside/outside surface of the tee base.  Two additional strain gages to be located near and opposite the coil leads.

#### Thermocouples

#### Material

Type E Chromel/Constantan, 0.010-in diameter.

#### Quantity, Size, and Weight

Minimum of six thermocouples.

#### Location

Within a coil plane, opposite the leads region, thermocouples shall be located in the middle of each winding pack and spaced vertically between the layers.

#### Flux loops

#### Material

The flux loops are composed of 0.030-in diameter mineral insulated wire with shrink tubing for insulation.

#### Quantity, Size, and Weight

Four loops are required, each with a length of approximately 15-ft.

#### Location

Wires shall be located at the inner and outer corner, plasma side of each winding pack.

#### Termination

Wires shall be routed along the lead block to the base of the winding form.

# QUALITY ASSURANCE

## Inspection and Test Requirements

Inspections and tests shall be performed in accordance with approved procedures referencing criteria for acceptance for rejection.  The following table describes the actions to be taken in order to verify the requirements listed in Section 3:

| Requirement | Description | Verification | Remarks |
| --- | --- | --- | --- |
| 3.2.1 Winding Form Assembly |
| 3.2.1.1 | Materials | Vendor supplied certification |  |
| 3.2.1.2 | Size and weight | Inspection | Note weight of winding form and finished coil. |
| 3.2.1.3 | Magnetic permeability | Test | Spot check of vendor tests. |
| 3.2.1.4 | Electrical requirements | Test | Check resistance of poloidal break. |
| 3.2.1.5 | Winding surface tolerance | Inspection | Perform initial dimensional inspection of winding form. |
| 3.2.1.6 | Surface finish | Inspection |  |
| 3.2.1.7 | Winding form modifications | Inspection | Verify proper alignment re winding law. |
| 3.2.2 Inner Copper Cladding |
| 3.2.2.1 | Material | Supplier certification |  |
| 3.2.2.2 | Quantity, size, and weight | Inspection | Verify flat patterns per asm drawing. |
| 3.2.2.3 | Sliding fit | Inspection | Remove burrs and sharp edges. |
| 3.2.2.4 | Electrical requirements | Test | Check resistance between cladding and winding form. |
| 3.2.3 Ground Insulation |
| 3.2.3.1 | Material | Supplier certification |  |
| 3.2.3.2 | Size and weight |  |  |
| 3.2.4 Conductor and Insulation |
| 3.2.4.1 | Material | Supplier certification |  |
| 3.2.4.2 | Size and weight | Inspection | Verify conductor dims while winding. |
| 3.2.4.3 | Conductor length | Inspection |  |
| 3.2.4.4 | Electrical properties | Test | Perform continuity check. |
| 3.2.4.5 | Current center | Inspection | Perform regular dimensional inspections. |
| 3.2.5 Supplemental Turn Insulation |
| 3.2.5.1 | Material | Supplier certification |  |
| 3.2.5.2 | Size and weight |  |  |
| 3.2.6 Lead Blocks |
| 3.2.6.1 | Material | Supplier certification |  |
| 3.2.6.2 | Quantity, size, and weight |  |  |
| 3.2.6.3 | Surface finish | Inspection | Remove burrs and sharp edges. |
| 3.2.7 Terminal Blocks |
| 3.2.7.1 | Material | Supplier certification |  |
| 3.2.7.2 | Quantity, size, and weight |  |  |
| 3.2.7.3 | Surface finish | Inspection | Remove burrs and sharp edges. |
| 3.2.7.4 | Bolted connection | Test | Check resistance at connections. |
| 3.2.8 Chill Plates |
| 3.2.8.1 | Material | Supplier certification |  |
| 3.2.8.2 | Quantity, size, and weight | Inspection |  |
| 3.2.8.3 | Electrical properties | Test | Check resistance between chill plates, cladding, and winding form. |
| 3.2.9 Coolant Tubes |  |  |  |
| 3.2.9.1 | Material | Supplier certification |  |
| 3.2.9.2 | Quantity, size, and weight |  |  |
| 3.2.10 VPI Bag Mold |
| 3.2.10.1 | Material | Supplier certification |  |
| 3.2.10.2 | Quantity, size, and weight |  |  |
| 3.2.11 Clamp Assembly |
| 3.2.11.1 | Material | Supplier certification |  |
| 3.2.11.2 | Quantity, size, and weight |  |  |
| 3.2.12 Instrumentation |
| 3.2.12.1 Strain gages |
| 3.2.12.1.1 | Material | Supplier certification |  |
| 3.2.12.1.2 | Quantity, size, and weight |  |  |
| 3.2.12.1.3 | Location |  |  |
| 3.2.12.2 Thermocouples |
| 3.2.12.2.1 | Material | Supplier certification |  |
| 3.2.12.2.2 | Quantity, size, and weight |  |  |
| 3.2.12.2.3 | Location |  |  |
| 3.2.12.3 Flux Loops |
| 3.2.12.3.1 | Material | Supplier certification |  |
| 3.2.12.3.2 | Quantity, size, and weight |  |  |
| 3.2.12.3.3 | Location | Inspection | Note position of wire in cross-section. |
| 3.2.12.3.4 | Termination | Test | Check electrical continuity of termination. |

# DOCUMENTATION

## System of Documentation

During coil assembly, the team shall maintain a system of documentation whereby objective evidence of materials used in construction and the functional compliance of the coil can be verified.  Such documentation shall include process travelers and any certification, inspection, examination, test, and discrepancy reports that are required.