NCSX Specification

System Requirements Document (SRD)

for the

Cryostat (WBS 171)

NCSX-BSPEC-171-0A

Draft A

5 April 2005

Prepared by: __________________________________________________________________________

G. Gettelfinger, WBS Manager for Cryostat (WBS 171)

Concur: ______________________________________________________________________________

B. Nelson, Project Engineer for Stellarator Core Systems (WBS 1)

Concur: ______________________________________________________________________________

M. Zarnstorff, Head, Project Physics

Concur: ______________________________________________________________________________

R. Simmons, Systems Engineering Support Manager

Concur: ______________________________________________________________________________

W. Reiersen, Engineering Manager

Concur: ______________________________________________________________________________

J. Levine, ES&H

Concur: ______________________________________________________________________________

J. Malsbury, Quality Assurance

Approved by: _________________________________________________________________________

G. H. Neilson, NCSX Project Manager

Record of Revisions

| Revision | Date | ECP | Description of Change |
| --- | --- | --- | --- |
| Draft A | 4/5/05 |  | Released for comment |

TABLE OF CONTENTS

1	Scope	1

1.1	Document Overview	1

1.2	Incomplete and Tentative Requirements	1

2	Applicable Documents	2

2.1	NCSX Documents	2

3	Subsystem Requirements	3

3.1	Subsystem Definition	3

3.1.1	Subsystem Diagrams	3

3.1.1.1	Functional Relationships	3

3.1.1.2	Functional Flow Block Diagram	4

3.1.2	Interface Definition	4

3.1.2.1	Vacuum Vessel (WBS 12)	4

3.1.2.2	Coil Support Structures (WBS 15)	4

3.1.2.3	Coil Services (WBS 16)	5

3.1.2.4	Base Support Structure (WBS 172)	5

3.1.2.5	Stellarator Core Management and Integration (WBS 19)	5

3.1.2.6	Magnetic Diagnostics (WBS 31)	5

3.1.2.7	Electrical Power Systems (WBS 4)	5

3.1.2.8	GN2 Cryostat Cooling (WBS 623)	5

3.1.3	Major Component List	5

3.2	Characteristics	5

3.2.1	Performance	5

3.2.1.1	Perform Initial and Pre-run Verification	5

3.2.1.1.1	Initial Facility Startup	5

3.2.1.1.1.1	Initial Verification of Operability	6

3.2.1.1.1.2	Design Verification	6

3.2.1.1.2	Pre-Run Facility Startup	6

3.2.1.2	Prepare for and Support Experimental Operations	6

3.2.1.2.1	Subsystem Verification and Monitoring	6

3.2.1.2.2	Bakeout	6

3.2.1.2.3	Disruption Handling	6

3.2.2	Cryostat Physical Characteristics	6

3.2.2.1	Service Envelope	6

3.2.2.2	Aggregate Thermal Leakage	6

3.2.2.3	Gas Inlet/Discharge Points	7

3.2.2.4	Panels – Fundamental Forms	7

3.2.2.5	Panels – Purge Feature	7

3.2.2.6	Additional Gravity Loads	7

3.2.3	System Quality Factors	7

3.2.3.1	Reliability, Availability, and Maintainability	7

3.2.3.2	Design Life	8

3.2.3.3	Seismic Criteria	8

3.2.4	Transportability	8

3.3	Design and Construction	8

3.3.1	Materials, Processes, and Parts	8

3.3.1.1	Magnetic Permeability	8

3.3.1.2	Cryostat Material	8

3.3.1.2.1	Cryostat Structural Material	8

3.3.1.2.2	Panel Insulation	8

3.3.1.2.3	Joint Insulation	9

3.3.1.2.4	Inboard/outboard Boots	9

3.3.1.3	Structural and Cryogenic Criteria	9

3.3.1.4	Corrosion Prevention and Control	9

3.3.1.5	Metrology	9

3.3.2	Electrical Grounding	9

3.3.3	Nameplates and Product Marking	9

3.3.3.1	Labels	9

3.3.4	Workmanship	9

3.3.5	Interchangeability	10

3.3.6	Environmental, Safety, and Health (ES&H) Requirements	10

3.3.6.1	Personnel Safety	10

3.3.6.2	Flammability	10

3.4	Documentation	10

3.4.1	Specifications	10

3.5	Logistics	10

3.5.1	Maintenance	10

4	Quality Assurance Provisions	11

4.1	General	11

4.2	Verification Methods	11

4.3	Quality Conformance	11

Appendix A – Quality Conformance Matrix	12

Table of Figures

Figure 3-1 Cryostat Functional Relationships	3

Figure 3-2 NCSX Functional Flow Block Diagram	4

Table of Tables

Table 3-1 Cryostat Specifications	10

# Scope

The National Compact Stellarator Experiment (NCSX) is an experimental research facility that is to be constructed at the Department of Energy’s Princeton Plasma Physics Laboratory (PPPL). Its mission is to acquire the physics knowledge needed to evaluate compact stellarators as a fusion concept, and to advance the understanding of 3D plasma physics for fusion and basic science.

A primary component of the facility is the stellarator core, an assembly of four coil systems that surround a highly shaped plasma and CRYOSTAT chamber. The stellarator core must be cooled to 80 degrees Kelvin for the planned schedule of experiments.  Such cooling requires a Cryostat to serve as an insulation and isolation system.

This specification addresses the design requirements for the NCSX Cryostat (WBS 171).

## Document Overview

This document, the System Requirements Document (SRD) for the Cryostat (WBS 171) is the complete development specification for these subsystems.  Performance requirements allocated to these subsystems in the system specification, the General Requirements Document (NCSX-ASPEC-GRD-02), have been incorporated in this document.  In this document, the term “the system” refers to the overall device and facility. The terms “subsystem” and “cryostat” refers to the WBS 171 subsystem element.

The specification approach being used on NCSX provides for a clear distinction between performance requirements and design constraints.  Performance requirements state what functions a system has to perform and how well that function has to be performed.  Design constraints, on the other hand, are a set of limiting or boundary requirements that must be adhered to while allocating requirements or designing the system.  They are drawn from externally imposed sources (e.g., statutory regulations, DOE Orders, and PPPL ES&H Directives) as well as from internally imposed sources as a result of prior decisions, which limit subsequent design alternatives.

## Incomplete and Tentative Requirements

Within this document, the term “TBD” (to be determined) indicates that additional effort (analysis, trade studies, etc) is required to define the particular requirement.  The term “TBR” (to be revised) indicates that the value given is subject to change.

# Applicable Documents

The following documents form a part of this specification to the extent specified herein.  In the event of a conflict, the contents of this specification shall be considered a superseding requirement.

## NCSX Documents

Project Execution Plan (NCSX-PLAN-PEP-01)

General Requirements Document (NCSX-ASPEC-GRD-02)

Stellarator Core Systems (WBS 1) WBS Dictionary (NCSX-WBS1-02)

Structural and Cryogenic Design Criteria

Seismic Design Criteria

Grounding Specification for Personnel and Equipment Safety

Reliability, Availability, and Maintainability (RAM) Plan

# Subsystem Requirements

## Subsystem Definition

The cryostat (WBS 171) subsystem provides an insulating, semi-hermetic barrier that will allow the surrounding of the stellarator core with a cold, dry nitrogen atmosphere down to a temperature of 77K.  The semi-hermetic nature of the cryostat excludes the components of atmosphere from approaching the stellarator core in the design temperature range (77K to 311K).

### Subsystem Diagrams

#### Functional Relationships

A block diagram of the cryostat and its environment is shown in Figure 3-1.

Figure 3-1 Cryostat Functional Relationships

#### Functional Flow Block Diagram

A functional flow block diagram (FFBD) is provided in Figure 3-2.

Figure 3-2 NCSX Functional Flow Block Diagram

### Interface Definition

#### Vacuum Vessel (WBS 12)

The vacuum vessel port extensions, the vertical ports, and all associated cover flanges penetrate the cryostat.  Such penetrations shall be designed to provide gas-tight (7 kPa differential) insulating seals sufficient to preclude the condensing of atmospheric moisture at the penetration.  Electrical wiring and hydraulic tubing for vessel/port/extension heating and cooling as well as vessel I&C may pass through these penetrations as well.

#### Coil Support Structures (WBS 15)

The cryostat’s gravity/seismic support system shall react a portion of its load through dedicated supports into the coil support structures.

#### Coil Services (WBS 16)

Services for the magnetic field coils such as DC power leads, hydraulic (LN2) coolant lines, and I&C conductors shall pass through cryostat penetrations.  Such penetrations shall be sealed in the manner of 3.1.2.1, above.

#### Base Support Structure (WBS 172)

a.	The cryostat’s gravity/seismic support system shall react a portion of its load through dedicated supports into the base support structure.

b.	The base support structure, carrying the whole of the stellarator core, shall have twelve vertical towers penetrating the underside of the cryostat.  Such penetrations shall be sealed in the manner of 3.1.2.1, above.

#### Stellarator Core Management and Integration (WBS 19)

a.	The management and integration effort shall be constantly informed regarding evolutions in the cryostat design.

b.	The cryostat shall be of demountable design allowing access to the stellarator core for maintenance and modification in pursuit of experimental objectives.  WBS 19 managers may specify a TBD maximum tolerable access period to safely open the cryostat boundary after a warm-up of the core.

#### Magnetic Diagnostics (WBS 31)

The magnetic diagnostics effort shall require penetrations for conductor feedthroughs. Such penetrations shall be sealed in the manner of 3.1.2.1, above.

#### Electrical Power Systems (WBS 4)

a.	The single point grounding scheme shall require one or more penetrations through the cryostat to the stellarator core.

b.	AC power for circulating fans or other convection-encouraging devices may be required within the cryostat. Such penetrations shall be sealed in the manner of 3.1.2.1, above.

#### GN2 Cryostat Cooling (WBS 623)

The GN2 cryostat cooling system shall require both supply and return penetrations allowing the circulation of variable-temperature nitrogen gas around the stellarator core.  Also provided in support of the cryostat shall be I&C for the cryostat and overpressure protection.

### Major Component List

There are no major components for which additional development specifications are planned.

## Characteristics

### Performance

#### Perform Initial and Pre-run Verification

##### Initial Facility Startup

Background

Initial facility startup includes all activities required to verify safe operation of NCSX systems after their initial assembly and installation, or after a major facility reconfiguration, and before plasma operations.  Initial facility startup activities would be performed prior to First Plasma and will include subsystem pre-operational test procedures (PTPs) and an Integrated System Test Program (ISTP) to verify that the system operates safely and as expected prior to plasma operation. For example, the ISTP will include verification of proper coil polarities and power supply connections. The ISTP will also include verification that, at First Plasma, the system demonstrates a level of system performance sufficient for the start of research operations, as specified in the Project Execution Plan (NCSX-PLAN-PEP-01). A subset of the ISTP will be conducted before the start of a run.

###### Initial Verification of Operability

The cryostat subsystem shall provide the capability to perform subsystem PTPs and support a comprehensive ISTP, to verify, prior to plasma operation that the system is properly configured, able to isolate the stellarator core from the ambient environment, and can be operated safely. [Ref. GRD Section 3.2.1.1]

###### Design Verification

The subsystem shall be instrumented such that key cryostat performance parameters (consumption rate, etc.) can be measured and compared to calculated values to assure that the subsystem is performing consistent with the design intent prior to First Plasma.

##### Pre-Run Facility Startup

The subsystem shall support the capability to perform a controlled startup of the facility, and verify that the cryostat subsystem is properly configured, functioning correctly, and can be operated safely.  [Ref. GRD Section 3.2.1.2]

#### Prepare for and Support Experimental Operations

##### Subsystem Verification and Monitoring

The subsystem shall provide the capability to verify that the subsystem is properly configured, functioning correctly, and can be operated safely prior to the start of an operating day and prior to the start of each pulse (plasma discharge).  [Ref. GRD 3.2.1.3 and GRD 3.2.1.4]

##### Bakeout

The cryostat shall provide a sufficiently low internal flow resistance and overpressure capability to allow the increased heat removal requirements of vessel bakeout (and requisite cryostat gas flow increase) while allowing the LN2 system to maintain the cryo-resistive coils at 90K or less [Ref. GRD Section 3.2.1.2.3.3].

##### Disruption Handling

The cryostat shall be designed to withstand vacuum boundary displacements up to TBD mm due to major disruptions characterized by instantaneous disappearance of the plasma at with a maximum plasma current of 320 kA.  [Ref. GRD Section 3.1.5.5]

### Cryostat-Specific Characteristics

#### Service Envelope

The cryostat design shall meet all characteristics statements and requirements with the exterior temperature arbitrarily ranging from 283K to 311K and the interior gas temperature ranging from 77K to 311K with out degradation.

#### Aggregate Thermal Leakage

The cryostat design, including penetration and joint sealing, shall limit the influx of ambient heat to about 13.9 kW.

#### Gas Inlet/Discharge Points

Current design efforts allow for a GN2 cooling/warming system (WBS 623) to flow gas through the cryostat and around the stellarator core. These design efforts favor an two axial duct take-offs; one at the bottom/center location of the cryostat and one at the top/center location. While design evolution may argue for an alternate approach, the incumbent scheme is essentially a requirement.

#### Panels – Fundamental Forms

The stellarator core displays something approximating radial symmetry about an axis while a closer inspection reveals a toroidal periodicity.  To the largest extent possible, configurable, basic cryostat panels shall be described with provisions for custom configuration as the experimental program unfolds.  Such basic forms with potential for change hold promise for quantity purchasing savings.

#### Panels – Purge Feature

All cryostat panels shall contain a feature allowing the admission of ambient temperature nitrogen gas to obviate the chance of frost or ice forming within the panel and, thus, reducing the insulation capability of the panel

#### Additional Gravity Loads

The cryostat shall be able to support TBD kg/m2 of exterior surface for additional utility/diagnostic masses.

### System Quality Factors

#### Reliability, Availability, and Maintainability

Background

The overall objective is to provide a device with high operational availability, meaning that the number of plasma discharges achieved in a run period is a large percentage (greater than 75%) of the number planned after the initial shakedown and commissioning phases of the facility.  Bottoms-up reliability predictions are difficult to perform and have large uncertainties for first-of-a-kind experimental devices such as NCSX.  Therefore, quantitative RAM requirements on NCSX will be few.  Rather, NCSX will rather rely on sound engineering practice to assure high availability in NCSX, which has been the tried-and-true approach on similar scale fusion devices.  Sound engineering practices include:

- Applying design principles that promote reliability (e.g., employing an adequate factor of safety on mechanical and electrical stresses, avoiding unnecessary complexity, using proven design approaches and well characterized materials, etc.)

- Optimizing designs for reliability and maintainability through systematic evaluation of design options,

- Performing failure modes, effects and criticality analysis (FMECAs) for RAM design improvement and verification, and

- Employing peer reviews as a mechanism to enhance the design process.

The NCSX RAM Plan defines the processes that will be used by the Project to achieve a device with high availability.

Requirements

- The cryostat shall incorporate reliability and maintainability features in the design that are consistent with achieving a high (greater than 95%) operational availability.

- Provisions for recovery shall be made for every credible failure mode.

- The cryostat shall be capable of being disassembled and reassembled to permit replacement of any part or machine reconfiguration that would require disassembly.

- Provisions for lifting, e.g. lifting eyes, other sling attachment provisions, or equivalent provisions, shall be made in the design of the cryostat.

- Accommodations shall be made to facilitate installation and maintenance activities inside the cryostat.

[Ref. GRD Section 3.2.4.1]

#### Design Life

- The cryostat shall have a design life of >10 years.

- The cryostat’s design life is not affected by accumulated machine cycles.

[Ref. GRD Section 3.2.4.2]

#### Seismic Criteria

Background

NCSX systems shall be designed in accordance with seismic design and evaluation criteria for Performance Category 1 (PC1) facilities, per DOE-STD-1020-2002, “Natural Phenomena Hazards Design and Evaluation Criteria for Department of Energy Facilities.”  The NCSX Seismic Design Criteria provides an NCSX-specific interpretation of those requirements

Requirement

The cryostat shall be design in accordance with the NCSX Seismic Design Criteria.  [Ref. GRD Section 3.3.1.5]

### Transportability

All cryostat sub-assemblies and components shall be transportable by commercial carrier via highway, air, sea, or railway.  [Ref. GRD Section 3.2.5]

## Design and Construction

### Materials, Processes, and Parts

#### Magnetic Permeability

All materials (including weld materials) used in the cryostat and its peripheral hardware must have a relative magnetic permeability less than 1.02 unless otherwise authorized by the Project.  [Ref. GRD Section 3.3.1.1]

#### Cryostat Material

##### Cryostat Structural Material

The main structure of the cryostat panels will be of epoxy/glass composite.  Cold temperature testing of the composite, reflecting NCSX service conditions shall be performed as part of the procurement process.  The panel inserts and covers shall be constructed of epoxy/glass as well.

##### Panel Insulation

The cryostat panels shall be filled with bonded layers of Dow Trymer 2000, 2000i, or 4000 closed cell polyisocyanurate foam or a similar substitute with equal or better K-factor and CTE.  Small voids in the layered insulation may be filled with Inpec Solimide open cell foam or single part expanding polyurethane foam.

##### Joint Insulation

Packing shall be provided between adjacent cryostat panels and in the annulus/gap in penetrations and may be of Inpec Solimide open cell foam layed with Teflon gas barrier membranes or single part expanding polyurethane foam.

##### Inboard/outboard Boots

Penetrations may require inboard and/or outboard “flexible” gas exclusion boots to segregate internal cryostat and ambient exterior atmospheres.  Such boots shall be made from woven glass cloth and Dow ZZZ Silicone compound.

#### Structural and Cryogenic Criteria

The cryostat shall be designed in accordance with the NCSX Structural and Cryogenic Design Criteria.  [Ref. GRD Section 3.3.1.3]

#### Corrosion Prevention and Control

Materials, processes, and protective surface treatments or finishes shall be provided to ensure that equipment capability during its service life is not degraded due to corrosion.  Where possible, contact between dissimilar metals shall be avoided.  [Ref. GRD Section 3.3.1.4]

#### Metrology

The cryostat shall provide features (e.g., fiducial markers) to facilitate accurately measuring and locating components relative to the magnetic field for the life of the machine.  [Ref. GRD Section 3.3.1.6]

### Electrical Grounding

The cryostat is primarily designed with electrically insulating materials and generally does not required grounding. Individual metallic fasteners used to join adjacent cryostat panels shall not be grounded.  Metallic support structures specific to the cryostat which react the cryostat’s gravity load shall be connected to a single-point electrical grounding system, provided in accordance with the NCSX Grounding Specification for Personnel and Equipment Safety.

[Ref. GRD Section 3.3.2]

### Nameplates and Product Marking

#### Labels

Equipment and any parts of that equipment to be used by personnel shall be identified with appropriate labels.  Labels shall indicate clearly and concisely the function and purpose of the item being labeled.  Hierarchical labeling shall be used to facilitate component location on control panels.  The terminology used for equipment, procedures, and training materials shall be the same for each case.  Label design shall be consistent to promote simplicity and avoid clutter.  The use of abbreviations and acronyms shall be minimized.  Permanent labels shall be attached to the specific component or equipment in such a manner that environmental conditions or usage by personnel will not remove or destroy the label.  Temporary labels shall be used only when necessary and shall not obscure other information or equipment.  If a temporary label is to designate a device that is out of service, the label shall be applied so that it prevents the use of that device.  Labeling shall be legible and conform to human visual capabilities and limitations in regard to physical characteristics.  [Ref. GRD Section 3.3.3.1]

### Workmanship

During cryostat fabrication and finishing, particular attention shall be given to freedom from blemishes, defects, burrs, and sharp edges; making of parts; thoroughness of cleaning; alignment of parts; and tightness and torquing of fasteners.  [Ref. GRD Section 3.3.4]

### Interchangeability

Design tolerances shall permit parts and assemblies of the same part number to be used as replacement parts without degrading the specified performance of the parent item.  [Ref. GRD Section 3.3.5]

### Environmental, Safety, and Health (ES&H) Requirements

#### Personnel Safety

The subsystem shall meet all applicable OSHA requirements in accordance with 29CFR1910.  The system shall limit personnel exposure to hazardous materials to below their OSHA permissible exposure limit (PEL).  [Ref. GRD Section 3.3.6.3]

#### Flammability

The use of flammable materials shall be minimized.  [Ref. GRD Section 3.3.6.4]

## Documentation

### Specifications

Specifications shall be developed for each configuration item as shown in Table 3-1.

Table 3-1 Cryostat Specifications

| Configuration Item | Specification Identifier | Specification Type |
| --- | --- | --- |
| Cryostat Panel Sub-assembly | NCSX-CSPEC-171-01-XX | Product specification – forms the basis of the cryostat procurement providing guidance for panel construction augmented by application-specific drawings |

## Logistics

### Maintenance

The cryostat shall be maintained using, to the greatest extent possible, standard/common tools.  Use of new/special tools and the number of standard/common tools shall be minimized through maximum commonality of fasteners, clamps, adapters, and connectors.

# Quality Assurance Provisions

## General

This section identifies the methods to be used for verification of requirements in Section Error! Reference source not found. of this specification.  General definitions of basic verification methods are outlined in Section Error! Reference source not found..  Verification of subsystem requirements will require additional testing in operational or near-operational environments.

## Verification Methods

Verification of qualification shall be by examination, demonstration, test or analysis.  Definition of examination, demonstration, test and analysis is as follows:

Examination:  Examination is an element of inspection consisting of investigation, without the use of special laboratory appliances, procedures or supplies and services to determine conformance to those specified requirements which can be determined by such investigations.  Examination is generally non-destructive and includes but is not limited to, simple physical manipulation, gauging and measurement, visual, auditory, olfactory, tactile, gustatory and other investigations.

Test:  Test is an element of inspection denoting the determination of the properties or elements of supplies or components thereof by technical means, including functional operation and the application of established principles and procedures.  The analysis of data derived from test is an integral part of the inspection element and shall not be confused with “Analysis” below.

Demonstration:  Demonstration is an element of inspection  that, although technically a variation of test, differs from “Test” above, by directness of approach in the verification of a requirement and is accomplished without the use of elaborate instrumentation or special equipment.  Thus, operation of a representative configuration item (CI) in or near its use environment would be defined as a demonstration rather than a test.

Analysis:  Analysis is an element of inspection in the form of a study resulting in data that is intended to verify a requirement when an examination, test, or demonstration cannot feasibly be employed to verify the requirement. Such data may be a compilation or interpretation of existing data, analysis, design solutions, and lower-level inspection results.

## Quality Conformance

Background

This section establishes the specific evaluation criteria for verification of the subsystem performance requirements in Section 3.  In general, all requirements shall be verified under operational or near-operational conditions as possible given test constraints.

Requirements

Test methods for each of the performance characteristics in Section 3 are identified in the Quality Conformance Matrix in Appendix A – Quality Conformance Matrix.

# Appendix A – Quality Conformance Matrix

| Section | Characteristic | Analysis | Demonstration | Inspection | Test | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 3.2 | Characteristics |  |  |  |  |  |
| 3.2.1 | Performance |  |  |  |  |  |
| 3.2.1.1 | Perform Initial and Pre-run Verification |  |  |  |  |  |
| 3.2.1.1.1 | Initial Facility Startup |  |  |  |  |  |
| 3.2.1.1.1.1 | Initial Verification of Operability |  | X |  |  |  |
| 3.2.1.1.1.2 | Design Verification |  | X |  |  |  |
| 3.2.1.1.2 | Pre-Run Facility Startup |  | X |  |  |  |
| 3.2.1.2 | Prepare for and Support Experimental Operations |  |  |  |  |  |
| 3.2.1.2.1 | Subsystem Verification and Monitoring |  | X |  |  |  |
| 3.2.1.2.2 | Bakeout |  | X |  |  |  |
| 3.2.1.2.3 | Disruption Handling |  | X |  |  |  |
| 3.2.2 | Cryostat-Specific Characteristics |  |  |  |  |  |
| 3.2.2.1 | Service Envelope |  | X |  |  |  |
| 3.2.2.2 | Aggregate Thermal Leakage | X | X |  |  |  |
| 3.2.2.3 | Additional Gravity Loads | X | X |  |  |  |
| 3.2.3 | System Quality Factors |  |  |  |  |  |
| 3.2.3.1 | Reliability, Availability, and Maintainability |  | X |  |  |  |
| 3.2.3.2 | Design Life | X | X |  |  |  |
| 3.2.3.3 | Seismic Criteria | X |  |  |  |  |
| 3.2.4 | Transportability |  | X |  |  |  |

# Text boxes

Controlled Document

This is a controlled document.  Check the NCSX Engineering Web prior to use to assure that this document is current.