PPPL

Product Requirements List

Photogrammetry Metrology Equipment

PPPL-PRL-18-001-00

December 6, 2007

Prepared by: __________________________________________________________________________

S. Raftopoulos, Metrology Engineer

Concur: ______________________________________________________________________________

M. Viola, NCSX Field Period Assembly Manager

Concur: ______________________________________________________________________________

P. Heitzenroeder, Mechanical Engineering Division Head

Concur: ______________________________________________________________________________

F. Malinowski, Quality Assurance

Approved by: _________________________________________________________________________

L. Dudek, Fabrication, Operations and Maintenance Division Head

RECORD OF REVISIONS

| Revision | Date | ECP | Description of Change |
| --- | --- | --- | --- |
| Rev. 0 | 12/6/2007 |  | Initial Release |

TABLE OF CONTENTS

1.0	SCOPE	3

2.0	REQUIREMENTS	3

2.1	General Requirements of Photogrammetry Syste	3

2.2       Salient Characteristics	3

2.2.1	Performance - 40% of evaluation	3

2.2.2	Software - 30% of the evaluation	4

2.2.3	Support/Service - 20 % of the evaluation	4

2.2.4	System Upgradability - 10% of the evaluation	4

2.3	Recommended Sources	4

# Scope

This requirements list covers the procurement of Photogrammetry Equipment for the Princeton Plasma Physics Laboratory (PPPL) to support measurement and assembly operations.

# REQUIREMENTS

This photogrammetry metrology package will be used to supplement existing mechanical measurement systems (FARO/Romer arms, Laser Trackers, and Verisurf and PowerINSPECT metrology software).

## General Requirements of Photogrammetry System

The photogrammetry system shall be required to replace and/or extend the capabilities of Laser Trackers and pCMM arms for close distance (2-5 meters) and medium distance (3-20 meters) metrology.  It shall include the following features and capabilities:

- Digital camera/capture system for taking the image data.  Wireless transfer to computer is preferable to expedite preprocessing.  Hardware shall include a protective carrying case.

- Laptop computer with software package for processing data.

- Length standard(s) - N.I.S.T. certified (or PPPL-approved equivalent). Appropriate for distances mentioned above and to be used with 5 cubic meter volume

- Capability to accept/import nominal coordinate data from existing CAD and Metrology software (versions current to this date), and work within the CAD part coordinate system.

- Characterize the fiducialized component (using standard Hubbs reflectorized targets)

- Perform best fit transformations.

- Provide distortion/deformation/translation analysis.

- Output/Export to a format that is compatible with existing CAD and Metrology software.

- Hardware/software manuals.

- Certificate of calibration for applicable components (N.I.S.T. traceable standards, camera system, etc)

### Salient Characteristics

### The proposed Photogrammetry systems shall be evaluated against the following criteria:

### Performance - 40% of evaluation

- Accuracy

- Precision

- Resolution

- Speed, in regards to handling multiple projects, allowing use of system in as many as 3 parallel measurements

- Allow simultaneous use of multiple camera systems

### Software - 30% of the evaluation

- User Interface

- Ability to handle multiple projects, allowing use of system in as many as 3 parallel measurements.

- Allow simultaneous post processing of multiple projects

- Learning Curve – expected time for someone with Laser tracker experience to gain proficiency

- Data output compatibility with existing PPPL metrology software (Verisurf 9.1-R28 and Delcam PowerINSPECT 4.315-SP1)

- Data output compatibility with existing PPPL CAD software (ProEngineer  Wildfire 2.0)

- Availability of coded targets, sufficient in number to permanently apply to individual components as they are brought together into a larger assembly. Vendor to specify the maximum possible number of targets available.

### Support/Service - 20 % of the evaluation

- Hardware:

    - Service agreements

    - Turn around time for replacement during warranty period

    - Turn around time for replacement out of warranty period

      - Software:

    - Software Maintenance Agreement

    - Software updates

    - Software support, both by phone and/or on-site

    - Training availability at vendor location or on-site (PPPL)

### System Upgradability - 10% of the evaluation

- Cost of incremental upgrade to 2 systems

- Trade-in program for hardware should substantially better hardware become available within the warranty period

## Recommended Sources

- AICON (DPA-PRO system)

- GSI (VSTARS E4X or INCA3 systems)

- GOM (TRITOP system)