PRINCETON PLASMA PHYSICS LABORATORY

#### NCSX

HVAC SYSTEMS IN THE EXPERIMENTAL AREAS

# DESIGN REQUIREMENTS

### DRAFT

Prepared by: 						 Date:

Henry Carnevale

Reviewed by: 						 Date:

Bill Slavin

Approved by: 						 Date:

Jerry Levine

Approved by: 						 Date:

Erik Perry

Approved by: 						 Date:

Carl Potensky

Approved by: 						 Date:

Hutch Neilson

NCSX Test Cell

Air Flow -

Temperature - 70°F ± 2°F

Dew Point Control - 45°F ± 5°F

Minimum Outside Air -

Emergency Vent System –

## NCSX Test Cell Basement

Air Flow -

Temperature - 70°F ± 2°F

Dew Point Control - 45°F ± 5°F

Minimum Outside Air -

## NCSX CONTROL ROOM

Air Flow -

Temperature - 70°F ± 5°F

Humidity – 50% RH ± 10%RH

Minimum Outside Air –

## NCSX NEUTRAL BEAM CONTROL ROOM

Air Flow -

Temperature - 70°F ± 5°F

Humidity – 50% RH ± 10%RH

Minimum Outside Air –

## NCSX NEUTRAL BEAM RECTIFIER ROOM

Air Flow -

Temperature - 70°F ± 5°F

Humidity – 50% RH ± 10%RH

Minimum Outside Air –

Notes:

- Penetrations in the Test Cell and Control room walls and floors will be sealed by the Project.

- Project to supply the heat load expectations for airflow to the Test Cell and Test Cell Basement and Control Rooms.

- Industrial Hygiene and Safety to determine outside air requirements and emergency vent system flow rate.

- The interior of the transite walls in the Test Cell will be sealed with some sort of paint/sealer by the Project moisture.

- The old P.B.X. Control Room Annex area (Room 235) is not included.

- The rooms on the first floor C-103 through C-109 (future DARM area) presently have no additional HVAC requirements.

- The offices West of the control room have no special HVAC requirements and are not included in either NCSX or GPP budget.