| Prepared by: |
| --- |
| R. Simmons |
| Reviewed by: |
| WBS 5 (Central Controls and Computing) | P. Sichta (WBS Manager) |
| WBS 5 (Electrical Systems) | A. vonHalle (RLM) |
| Approved by: |
| H. Neilson |

Record of Revisions

| Revision | Date | Author | Description |
| --- | --- | --- | --- |
| 0 | 9/8/2003 | Simmons | Initial issue |
| 1 | 2/17/2004 | Simmons | Updated WBS dictionary to delete technical requirements and reflect CD-2 milestone scope. |
| 2 | 7/2/2007 | Simmons | Updated WBS to Reflect Scope for 2007 Rebaseline. |

| WBS Element: 5 | WBS Level: 2 |
| --- | --- |
| WBS Title: | Central Controls and Computing |
| Description: | Central Controls and Computing (WBS 5) will provide integrated control and monitoring, diagnostic data acquisition and data management, and timing and synchronization for NCSX. This summary-level WBS element consists of the equipment and software that provide central computing, control, and synchronization for NCSX. These systems interface with the subsystem’s local I&C systems and allow for control and monitoring of NCSX experiments from the control room and includes analysis and display of the data. The systems covered under this WBS elements include: Network & Fiber Infrastructure Systems (WBS 51); Central Instrumentation and Control Systems (WBS 52); Data Acquisition and Facility Computing Systems (WBS 53); Facility Timing and Synchronization Systems (WBS 54); Real Time Control Systems (WBS 55); Central Safety & Interlock Systems (WBS 56); Control Room Facility (WBS 57); and Management and Integration (WBS 58). MIE Project Scope: Defined in lower-level WBS elements. In general the central facility I&C systems and capabilities will be limited to those only needed to satisfy CD-4 requirements. Future Scope: Future central facility I&C and data acquisition systems and capabilities will be added as the capabilities of the NCSX Project are expanded. |

| WBS Element: 51 | WBS Level: 3 |
| --- | --- |
| WBS Title: | Network and Fiber Optic Infrastructure |
| Description: | The Network & Fiber Infrastructure Systems will provide the common backbone for all data acquisition, and I&C communications. These systems shall be designed to meet the following basic requirements: Network Communications for critical and high-energy subsystems are required to be protected from intrusion from the local PPPL network and the wide area. Network Communications for critical protective systems will be implemented with dual power supply switches fed from house and UPS sources. The network is required to operate in a high noise environment close to the machine and its power sources. Isolation of diagnostic data acquisition network traffic and the facility subsystems network traffic is required to insure that high data load will not impact facility control and monitoring. A fiber optic facility will be required for the Timing and Synchronization System, diagnostic video cameras and real time plasma control system communications. The network infrastructure will be implemented with fiber optic cable, twisted-pair cable, and wireless communications as appropriate for the application. MIE Project Scope: Where appropriate, the PPPL’s existing infrastructure will be used to provide network connections to CD-4 subsystems. Additional infrastructure will be added as needed. Future Scope: Additional infrastructure will be added as additional capabilities are added to the NCSX Project. |

| WBS Element: 52 | WBS Level: 3 |
| --- | --- |
| WBS Title: | Central Instrumentation and Control |
| Description: | The Central Instrumentation and Control system (CI&C) will provide integrated control of NCSX through supervisory control and a common user interface to selected engineering subsystems and diagnostics instruments. It will provide process control and monitoring functions, inter-process synchronization, operator displays, alarm management, and historical trending,. It will be designed using the Experimental Physics and Industrial Control System (EPICS). MIE Project Scope: The EPICS infrastructure for the NCSX Fabrication Project will provide an interface with the following systems: WBS 23 First Wall Conditioning Thermocouples and Strain Gauges; and Other WBS 5 elements. Future Scope: Additional central I&C systems will be added as additional capabilities are added to the NCSX Project. |

| WBS Element: 53 | WBS Level: 3 |
| --- | --- |
| WBS Title: | Data Acquisition and Facility Computing |
| Description: | The diagnostic Data Acquisition and Facility Computing systems will provide a software structure to collect, catalog, and manage experimental results for analysis and subsequent retrieval. The design will use the MIT-developed MDSplus software for data acquisition, data archiving and display. This system will: Be a “shot” mode time system where initialization sequences are started before the experimental discharge and data archival is completed at some period after the discharge. Support “shots” dedicated to an individual system’s test or calibration function. Achieve high performance and fault tolerance by storing all experimental data on reliable storage units. Provide online access, for the life of the machine, all experimental data. Support software interfaces to EPICS software (WBS51). MIE Project Scope: There is relatively a small amount of storage needs for the CD-4 milestone. Therefore, the NSTX Data Acquisition and Storage equipment will be used as much as possible. Future Scope: NCSX data will be transferred to the NCSX-specific system in the future. |

| WBS Element: 54 | WBS Level: 3 |
| --- | --- |
| WBS Title: | Facility Timing and Synchronization |
| Description: | The Facility Timing and Synchronization System will support at least 64 hardware events to synchronize NCSX equipment and diagnostics with the NCSX shot cycle. The events will be distributed using a network of fiber optic and hardwired components. These systems will utilize a new PPPL-developed timing and synchronization system. The new system will use a 10 MHZ time base. To coordinate computer programs across the NCSX networks, this WBS will have a software interface with the NCSX software event systems used for WBS 52 and WBS 53. MIE Project Scope: Provide a timing & synchronization system sufficient to synchronize the equipment and computers used for achieving the MIE Project requirements. Future Scope: Additional facility timing and synchronizations systems/capabilities will be added as needed. |

| WBS Element: 55 | WBS Level: 3 |
| --- | --- |
| WBS Title: | Real Time Plasma and Power Supply Control |
| Description: | The real time control systems will provide real time control for the NCSX power supplies (WBS4) and the main gas injectors (WBS2). MIE Project Scope: Provide a PC-oriented, LabVIEW-like system to produce synchronized, open-loop power supply commands and gas injection commands. The system will also control a few gas delivery valves. Future Scope: Additional real time plasma and power supply control systems/capabilities will be added as needed. |

| WBS Element: 56 | WBS Level: 3 |
| --- | --- |
| WBS Title: | Central Safety and Interlock System |
| Description: | The Central Safety and Interlock System (CSIS) will provide experiment-wide coordination of personnel and hardware interlocks. The fail-safe system will be constructed from mechanical components, hardwired devices, and safety-rated programmable/electronic components, networks, and software. Each NCSX high-energy subsystem will interface with the CSIS. An access control system will be incorporated to grant access to (hazardous) experimental areas for only authorized/trained personnel, when those areas are safe. UPS and Standby power will be used for critical components. MIE Project Scope: Provide a limited CSIS, sufficient to achieve safe operation of the NCSX device. Future Scope: Additional central safety and interlock systems/capabilities will be added as needed. |

| WBS Element: 57 | WBS Level: 3 |
| --- | --- |
| WBS Title: | Control Room Facility |
| Description: | MIE Project Scope: None. NCSX will utilize the old PBX-M control room and DAS computer rooms, and the basic refurbishment of these facilities is covered by PPPL infrastructure improvement project funds. Other WBS 5 elements will use the NCSX Control Room and NCSX Computing Center to the limited degree necessary for the MIE. |

| WBS Element: 58 | WBS Level: 3 |
| --- | --- |
| WBS Title: | Management and Integration |
| Description: | MIE Project Scope: Planning and interface definition for Central Controls and Computing systems. |