# COGNIZANT INDIVIDUAL:D. Williamson

# ECN TITLE:	Thermocouples Added to Modular Coil Assembly

# CC/WP/Job:		                           AREA OR PROJECT:  NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

# If non-concurrence or associated with a work planning form, enter the WP number:  _______

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE140-101 | 0 | MODULAR COIL ASM TYPE-A |
| SE140-102 | 0 | MODULAR COIL ASM TYPE-B |
| SE140-103 | 0 | MODULAR COIL ASM TYPE-C |

DESCRIPTION OF CHANGE: (state drawing no., zone. group, or list attachments) A decision was taken to place thermocouples on all cooling line inlet and outlets, as shown in the Table on sht-3 of SE140-101, -102, and -103. The thermocouples were already shown on the drawing, but only the outlet sensors had been installed to-date. By this change, all cooling lines shall have thermocouples, mounted inside or outside the winding form shell surface, depending on coil orientation. See note added to rev-1, sht-3 of drawings. REASON FOR CHANGE: Measuring inlet manifold temperature only is not sufficient to diagnose a problem with an individual coil.

ENGINEERING CHANGE NOTICE APPROVALS: DATE: 7/16/2008

COGNIZANT INDIVIDUAL MAKING CHANGE:

RESPONSIBLE LINE MANAGER: Update Drawings Immediately Defer Update and Use ECN Stamp Other Comments: